## Slide 1: 3GPP TSG-RAN WG4 Meeting #92bis Chongqing, China, 14th – 18th October 2019
Huawei, HiSilicon, Vodafone, Orange, …
WF on UE and BS RF requirements for introduction of FDD bands with variable duplex
R4-1913075

## Slide 2: Duplex Mode
Specify n91, n92, n93, n94 as FDD bands with variable duplex operation
  Clarify that this work item is not to enable dynamic variable duplex configuration by the network
  Duplex mode of the bands is FDD
  Add a note to the duplex mode in both 38.101-1 and 38.104 Specify in the RAN4 spec(s) to clarify variable duplex operation does not enable dynamic variable duplex configuration by the network, and is used such that DL and UL frequency ranges are supported independently in any valid frequency range for the band

## Slide 3: Tx-Rx separation
RAN4 will specify the confinement Tx-Rx separation for n91, n92, n93 and n94 as minimum value within the range
RAN4 will specify in 38.101-1 the confinement Tx-Rx separation for n91, n92, n93 and n94 only as minimum value within the range
RAN4 will specify Tx-Rx separation for n91, n92, n93 and n94 as minimum value within the range
  Specify in 38.101-1 the minimum Tx-Rx separation and corresponding asymmetric bandwidth confinement
  Specify in 38.104 the minimum Tx-Rx separation
For other FDD bands with variable duplex introduced in the future FFS which value to be used

## Slide 4: 7.5kHz shift
7.5KHz uplink shift requirement is applied for band n91, n92, n93, n94
  Specify in 38.101-1 this applicability
  Specify in 38.104 this applicability
There is no specification impact

## Slide 5: Channel bandwidth and SCS
Specify channel bandwidth and SCS for band n91, n92, n93, n94 in both 38.101-1 and 38.104
  Clarify which BW is applied for uplink and which is for downlink by notes in the table
  Asymmetric channel bandwidths will be defined as agreed in RAN4#92

## Slide 6: REFSENS
Specify REFSENS for n91, n92, n93, n94
  REFSENS follows the values defined for n75 and n76 in Table X.X incorrespondingly for each channel bandwidth and SCS
  REFSENS is based on minimum Tx-Rx separation

## Slide 7: Spurious emission
Specify spurious emission requirements for n91, n92, n93 and n94
  Specify in 38.104 the additional spurious requirements and colocation requirements with other base stations
  Specify in 38.141-1 the conformance test requirements for additional spurious and colocation with other base stations
  Note that n91 and n93 are only for local area BS operation

## Slide 8: Mandatory or optional support
Support for ULSUP is optional for UEs which support FDD bands with variable duplex n91, n92, n93 and n94