## Slide 1: Power Class 1.5 control logic and proposed text
Sprint
3GPP TSG-RAN4 Meeting #94-e R4-2000426
Online, , 24th Feb 2020 - 6th Mar 2020

## Slide 2: Existing text in 38.101-1
If a UE supports a different power class than the default UE power class for the band and the supported power class enables the higher maximum output power than that of the default power class:
- if the field of UE capability maxUplinkDutyCycle is absent and the percentage of uplink symbols transmitted in a certain evaluation period is larger than 50% (The exact evaluation period is no less than one radio frame); or
- if the field of UE capability maxUplinkDutyCycle is not absent and the percentage of uplink symbols transmitted in a certain evaluation period is larger than maxUplinkDutyCycle as defined in TS 38.331 (The exact evaluation period is no less than one radio frame); or
- if the IE P-Max as defined in TS 38.331 [7] is provided and set to the maximum output power of the default power class or lower;
- shall apply all requirements for the default power class to the supported power class and set the configured transmitted power as specified in clause 6.2.4;
- else if the IE P-Max as defined in TS 38.331 [7] is not provided or set to the higher value than the maximum output power of the default power class and the percentage of uplink symbols transmitted in a certain evaluation period is less than or equal to maxUplinkDutyCycle as defined in TS 38.331; or
- if the IE P-Max as defined in TS 38.331 [7] is not provided or set to the higher value than the maximum output power of the default power class and the percentage of uplink symbols transmitted in a certain evaluation period is less than or equal to 50% when maxUplinkDutyCycle is absent. (The exact evaluation period is no less than one radio frame):
- shall apply all requirements for the supported power class and set the configured transmitted power as specified in clause 6.2.4.

## Slide 3
PC≠PC3?
Dutycycle >MaxULDC?
Y
Y
N
N
Y
PMax present?
N
Y
PMax≤23?
N
MaxUplinkDutyCycle absent?
N
PC2 applies
Dutycycle >50%?
Y
N
Y
Default PC applies
Y
Y
PMax present?
Y
PMax ≤ 23?
MaxUplinkDutyCycle absent?
Dutycycle >50%?
N
N
N
N
Dutycycle ≤MaxULDC?
Undefined, but can’t happen
Logic of existing text
Y
Y
N
Start

## Slide 4: Simplified logic for potential revised text
PC≠PC3?
Dutycycle >MaxULDC?
Y
Y
N
N
Y
PMax present?
N
Y
PMax≤23?
N
MaxUplinkDutyCycle absent?
PC2 applies
Dutycycle >50%?
Y
N
Y
PC3 applies
N
Start

## Slide 5: Potential simplified text
If a UE supports a different power class than the default UE power class for the band and the supported power class enables the higher maximum output power than that of the default power class:
- if the field of UE capability maxUplinkDutyCycle is absent and the percentage of uplink symbols transmitted in a certain evaluation period is larger than 50% (The exact evaluation period is no less than one radio frame); or
- if the field of UE capability maxUplinkDutyCycle is not absent and the percentage of uplink symbols transmitted in a certain evaluation period is larger than maxUplinkDutyCycle as defined in TS 38.331 (The exact evaluation period is no less than one radio frame); or
- if the IE P-Max as defined in TS 38.331 [7] is provided and set to the maximum output power of the default power class or lower;
- shall apply all requirements for the default power class to the supported power class and set the configured transmitted power as specified in clause 6.2.4;
- else if the IE P-Max as defined in TS 38.331 [7] is not provided or set to the higher value than the maximum output power of the default power class and the percentage of uplink symbols transmitted in a certain evaluation period is less than or equal to maxUplinkDutyCycle as defined in TS 38.331; or
- if the IE P-Max as defined in TS 38.331 [7] is not provided or set to the higher value than the maximum output power of the default power class and the percentage of uplink symbols transmitted in a certain evaluation period is less than or equal to 50% when maxUplinkDutyCycle is absent. (The exact evaluation period is no less than one radio frame):
- shall apply all requirements for the supported power class and set the configured transmitted power as specified in clause 6.2.4.

## Slide 6
PC≠PC3?
Dutycycle >MaxULDC?
Y
Y
N
N
Y
PMax present?
N
Y
PMax≤23?
N
MaxUplinkDutyCycle absent?
N
PC2 applies
Dutycycle >50%?
Y
N
Y
PC3 applies
PC>PC2?
Dutycycle >MaxULDC/2?
Y
N
Y
PMax present?
N
Y
PMax ≤ 26?
MaxUplinkDutyCycle absent?
Dutycycle >25%?
Y
N
Y
N
Y
N
PC1.5 applies
N
Logic with PC1.5 for 38.101-1
Start

## Slide 7: Proposed PC 1.5 text v1(marked up)
If a UE supports a different power class than the default UE power class for the band and the supported power class enables the higher maximum output power than that of the default power class:
- if the field of UE capability maxUplinkDutyCycle is absent and the percentage of uplink symbols transmitted in a certain evaluation period is larger than 50% (The exact evaluation period is no less than one radio frame); or
  - if the field of UE capability maxUplinkDutyCycle is not absent and the percentage of uplink symbols transmitted in a certain evaluation period is larger than maxUplinkDutyCycle as defined in TS 38.331 (The exact evaluation period is no less than one radio frame); or
  - if the IE P-Max as defined in TS 38.331 [7] is provided and set to the maximum output power of the default power class or lower;
    - shall apply all requirements for the default power class to the supported power class and set the configured transmitted power as specified in clause 6.2.4;
  - else if the UE does not support a power class higher than PC2; or
  - if the field of UE capability maxUplinkDutyCycle is absent and the percentage of uplink symbols transmitted in a certain evaluation period is larger than 25% (The exact evaluation period is no less than one radio frame); or
  - if the field of UE capability maxUplinkDutyCycle is not absent and the percentage of uplink symbols transmitted in a certain evaluation period is larger than maxUplinkDutyCycle/2 (The exact evaluation period is no less than one radio frame); or
  if the IE P-Max as defined in TS 38.331 [7] is provided and set to the maximum output power of the power class 2 or lower;
  shall apply all requirements for power class 2 to the supported power class and set the configured transmitted power as specified in clause 6.2.4;
  - else if the IE P-Max as defined in TS 38.331 [7] is not provided or set to the higher value than the maximum output power of the default power class 2 and the percentage of uplink symbols transmitted in a certain evaluation period is less than or equal to maxUplinkDutyCycle/2 as defined in TS 38.331; or
  - if the IE P-Max as defined in TS 38.331 [7] is not provided or set to the higher value than the maximum output power of the default power class 2 and the percentage of uplink symbols transmitted in a certain evaluation period is less than or equal to 2550% when maxUplinkDutyCycle is absent. (The exact evaluation period is no less than one radio frame):
  - shall apply all requirements for the supported power class and set the configured transmitted power as specified in clause 6.2.4.

## Slide 8: Proposed PC 1.5 text v2(marked up)
If a UE supports a different power class than the default UE power class for the TDD band and the supported power class enables the higher maximum output power than that of the default power class:
- if the field of UE capability maxUplinkDutyCycle is absent and the percentage of uplink symbols transmitted in a certain evaluation period is larger than 50% (The exact evaluation period is no less than one radio frame); or
  - if the field of UE capability maxUplinkDutyCycle is not absent and the percentage of uplink symbols transmitted in a certain evaluation period is larger than maxUplinkDutyCycle as defined in TS 38.331 (The exact evaluation period is no less than one radio frame); or
  - if the IE P-Max as defined in TS 38.331 [7] is provided and set to the maximum output power of the default power class or lower;
    - shall apply all requirements for the default power class to the supported power class and set the configured transmitted power as specified in clause 6.2.4;
  - else if the UE does not support a power class higher than PC2; or
  - if the field of UE capability maxUplinkDutyCycle is absent and the percentage of uplink symbols transmitted in a certain evaluation period is larger than 25% (The exact evaluation period is no less than one radio frame); or
  - if the field of UE capability maxUplinkDutyCycle is not absent and the percentage of uplink symbols transmitted in a certain evaluation period is larger than maxUplinkDutyCycle/2 (The exact evaluation period is no less than one radio frame); or
  if the IE P-Max as defined in TS 38.331 [7] is provided and set to the maximum output power of the power class 2 or lower;
  shall apply all requirements for power class 2 to the supported power class and set the configured transmitted power as specified in clause 6.2.4;
  - if the IE P-Max as defined in TS 38.331 [7] is not provided or set to the higher value than the maximum output power of the default power class and the percentage of uplink symbols transmitted in a certain evaluation period is less than or equal to maxUplinkDutyCycle as defined in TS 38.331; or
  - if the IE P-Max as defined in TS 38.331 [7] is not provided or set to the higher value than the maximum output power of the default power class 2 and the percentage of uplink symbols transmitted in a certain evaluation period is less than or equal to 50% when maxUplinkDutyCycle is absent. (The exact evaluation period is no less than one radio frame):
  - else shall apply all requirements for the supported power class and set the configured transmitted power as specified in clause 6.2.4.

## Slide 9: Proposed text v2 (clean)
If a UE supports a different power class than the default UE power class for the band and the supported power class enables the higher maximum output power than that of the default power class:
- if the field of UE capability maxUplinkDutyCycle is absent and the percentage of uplink symbols transmitted in a certain evaluation period is larger than 50% (The exact evaluation period is no less than one radio frame); or
- if the field of UE capability maxUplinkDutyCycle is not absent and the percentage of uplink symbols transmitted in a certain evaluation period is larger than maxUplinkDutyCycle as defined in TS 38.331 (The exact evaluation period is no less than one radio frame); or
- if the IE P-Max as defined in TS 38.331 [7] is provided and set to the maximum output power of the default power class or lower;
- shall apply all requirements for the default power class to the supported power class and set the configured transmitted power as specified in clause 6.2.4;
- else if the UE does not support a power class higher than PC2; or
- if the field of UE capability maxUplinkDutyCycle is absent and the percentage of uplink symbols transmitted in a certain evaluation period is larger than 25% (The exact evaluation period is no less than one radio frame); or
- if the field of UE capability maxUplinkDutyCycle is not absent and the percentage of uplink symbols transmitted in a certain evaluation period is larger than maxUplinkDutyCycle/2 (The exact evaluation period is no less than one radio frame); or
- if the IE P-Max as defined in TS 38.331 [7] is provided and set to the maximum output power of the power class 2 or lower;
- shall apply all requirements for power class 2 to the supported power class and set the configured transmitted power as specified in clause 6.2.4;
- else shall apply all requirements for the supported power class and set the configured transmitted power as specified in clause 6.2.4.

## Slide 10: Existing text in 38.101-3 for intra-band EN-DC
If UE supports a different power class than the default UE power class for EN-DC band combination, and the supported power class enables higher maximum output power than that of the default power class:
- if the E-UTRA UL/DL configuration is 0 or 6; or
- if the E-UTRA UL/DL configuration is 1 and special subframe configuration is 0 or 5; or
- if the IE p-maxUE-FR1-r15 as defined in TS 36.331 [8] is provided and set to the maximum output power of the default power class or lower;
- apply all requirements for the default power class, and set the configured transmitted power as specified in clause 6.2B.4;
- else
- apply all requirements for the supported power class, and set the configured transmitted power class as specified in clause 6.2B.4;

## Slide 11: Logic for existing intra-band EN-DC text
PC≠
default?
Config 1 SSC 0 or 5?
Y
Y
N
Y
PMax present?
N
PMax≤23?
N
PC2 applies
Config 0 or 6?
Y
N
Y
PC3 applies
N
Start

## Slide 12: Options for intra-band EN-DC PC 1.5 logic
The existing text for intra-band EN-DC disallows UL/DL configuration 1 under the worst case assumption that all GP symbols will be scheduled for UL
For 29 dBm HPUE, with worst case NR uplink assumptions only UL/DL config 5 would be below the necessary 25%
Rather than limit intra-band EN-DC with PC 1.5 to UL/DL configuration 5, we’d prefer to allow UL/DL configuration 2, 4 and 5 and have the NR UL duty cycle checked against maxUplinkDutyCycle instead of making worst case assumptions about NR symbols in the GP period.

## Slide 13
PC>PC3?
N
N
PC2 applies
PC3 applies
PC>PC2?
NR Dutycycle >MaxULDC/2?
Y
N
Y
PMax present?
N
Y
PMax ≤ 26?
MaxUplinkDutyCycle absent?
NR Dutycycle >25%?
Y
N
Y
Y
N
PC1.5 applies
N
Proposed EN-DC Logic with PC1.5
Start
Config 2, 4 or 5?
N
Config 1 with SSC 0 or 5?
Y
Y
N
Y
PMax present?
N
PMax≤23?
Config 0 or 6?
Y
N
Y
N
Y

## Slide 14: Proposed text for PC 1.5 intra-band EN-DC
If UE supports a different power class than the default UE power class for TDD EN-DC band combination, and the supported power class enables higher maximum output power than that of the default power class:
- if the E-UTRA UL/DL configuration is 0 or 6; or
- if the E-UTRA UL/DL configuration is 1 and special subframe configuration is 0 or 5; or
- if the IE p-maxUE-FR1-r15 as defined in TS 36.331 [8] is provided and set to the maximum output power of the default power class or lower;
- apply all requirements for the default power class, and set the configured transmitted power as specified in clause 6.2B.4;
- else
- if the UE does not support a power class with output power higher than power class 2; or
- if the E-UTRA UL/DLconfiguration is not 2 or 4 or 5; or
- if the field of UE capability maxUplinkDutyCycle is absent and the percentage of uplink symbols transmitted in a certain evaluation period is larger than 25% (The exact evaluation period is no less than one radio frame); or
- if the field of UE capability maxUplinkDutyCycle is not absent and the percentage of uplink symbols transmitted in a certain evaluation period is larger than maxUplinkDutyCycle/2 (The exact evaluation period is no less than one radio frame); or
- if the IE P-Max as defined in TS 38.331 [9] is provided and set to the maximum output power of the power class 2 or lower;
- apply all requirements for the power class 2, and set the configured transmitted power as specified in clause 6.2B.4;
- else
- apply all requirements for the supported power class, and set the configured transmitted power class as specified in clause 6.2B.4;

## Slide 15: Proposal
Proposal 1: Agree to the proposed text v2 for PC 1.5 power control in 38.101-3.
Proposal 2: Agree to the proposed text for PC 1.5 intra-band EN-DC in 38.101-3.