## Slide 1: Summarizing the testability of transient capability reporting feature
Qualcomm Incorporated, Skyworks Solutions Inc., Verizon, Dish Network, Ericsson, CMCC, Keysight Technologies, Nokia, Nokia Shanghai Bell, Sprint, AT&T, ZTE, Vodafone, Orange, T-mobile, Deutsche Telekom, Telecom Italia, CHTTL, China Telecom, SGS Wireless, Interdigital, Anritsu
3GPP TSG-RAN WG4 #94-e
February 24th ‒ March 6th, 2020
Electronic Meeting
R4-2002096

## Slide 2: Background: Rel-15 Status Quo
An ON/ON transient is available in case of power change, modulation, or RB change.
  The allowed transient is 10 us.
  Transient location is specified (i.e., in trailing symbol, symmetric across symbols, etc)
  Example:
EVM calculation excludes the entire symbol for which a transient may overlap
“The EVM measurement interval is reduced by any symbols that contains an allowable power transient in the measurement interval, as defined in subclause 6.3.3.” [38.101-1, subclause 6.4.2.1]
  Transient period (10us) is not tested

## Slide 3: RAN plenary company CR for Rel-16
At RAN #86, company CR RP-192948 was proposed
conclusion: task for RAN4 to clarify testability by RAN #87, i.e. how it will be tested; CR will not be further discussed in RAN4 but will be provided to RAN #87
Title: | Error Vector Magnitude including symbols with transient period
Source to WG: | Qualcomm Incorporated, Skyworks Solutions Inc., Verizon, Dish Network, Ericsson, CMCC, Keysight Technologies, Nokia, Nokia Shanghai Bell, Sprint, AT&T, ZTE, Vodafone, Orange, T-mobile, Deutsche Telekom, Telecom Italia, CHTTL, China Telecom, SGS Wireless, Interdigital, Anritsu

## Slide 4: What new features does this CR introduce?
An optional capability is introduced to allow the UE to report a single per-UE “tp” value within the set {1, 2, 4, 7} us for ON/ON transitions. If not signaled, the legacy value of 10us is the default.
EVM requirement is modified to add (no longer exclude) testing of symbols which contain a transient within them
  Details on next slide
  → Testability of this new optional capability is already included in the CR

## Slide 5: Testability details
Test requirements are applicable to 15 kHz SCS, 14 symbols per slot, and symmetric placement of transient period between 2 adjacent symbols
When transient is reported as less than 150% CP (i.e., 1, 2, 4, or 7 us for 15 kHz SCS where CP is 144 samples @30.72 MHz) for those symbols containing transient, the EVM is calculated as min (EVML, EVMH)
  EVML and EVMH are starting location of Rx FFT at 25% and 75% CP
  By choosing min (EVML, EVMH), a symmetrically located transient whose duration is less than 150% CP will fall outside of the samples used for FFT
  If the transient is longer than 150% CP, then a portion of it will fall inside of the FFT thereby revealing itself as degraded EVM
  Calculating EVM as min (EVML, EVMH) allows the existing test configuration to be used without the need to define a new window location.
  Other symbols not containing transient are computed as-is without change; i.e., max(EVML, EVMH)

## Slide 6: Testability details (transient > 150% CP)
When transient period reported is greater than 150% CP for DFT-S-OFDM waveforms, the EVM within the symbol is computed, but excluding the reported transient period. The samples impacted by transient falling into the Rx FFT but after the iDFT are not included in the calculation of EVM
  This is the same approach proven by LTE (see 36.521-1, Annex E.7)
When transient period reported is greater than 150% CP for CP-OFDM, the entire symbols impacted by transient are excluded from EVM calculation
  This only applies to the case of 10us transient when the new capability signaling is not used as all other values (1, 2, 4, 7 us) are less than 150% CP for 15 kHz SCS.
  Excluding the symbol impacted by transient is maintaining the current status quo for 10us

## Slide 7: Testability details (single symbol EVM)
In addition to the basic EVM measurement conducted over a slot (14 symbols of which only 2 may contain transient), an EVM requirement consisting of only the symbols containing transient is also introduced.
The requirement is [15%] for 64QAM and [5%] for 256QAM
  The slot-averaged EVM is 8% and 3.5% for 64QAM and 256QAM, respectively
  The purpose of the new requirement is to highlight only those symbols with transient since averaging with other symbols may obscure the impact of the transient

## Slide 8: Conclusion
A new feature is introduced in Rel-16 that allows the UE to optionally signal a transient period of 1, 2, 4, or 7 us.
EVM testing is modified as described in the CR to test the UE that implements this new feature.
For the UE that does not implement the new feature (i.e., maintains 10us transient timing), nothing is changed from the status quo. EVM requirements exclude any symbols impacted by transient.
Proposal
 The new feature of transient capability reporting is agreed and its testability is established by modified/new EVM requirements.
 LS is sent to RAN plenary to inform that RAN4 has agreed that testability of the new feature on transient capability reporting is captured in the CR.
 CR in RP-192948 to be resubmitted at RAN #87.