## Slide 1: WF on MR-DC RRM requirements
Nokia, Nokia Shanghai Bell
3GPP TSG-RAN4 Meeting #94e
E-meeting, February 24th – March 6th, 2020
R4-2002234
Document for: Approval

## Slide 2: Background
During the RAN4#94e E-meeting the dicussion related to Multi-RAT Dual-Connectivity and Carrier Aggregation enhancements [LTE_NR_DC_CA_enh] continued.
Summary of the round 1 discussion is captured in R4-2002177.
Based on this summary and round 2 discussions (R4-200xxxx) some agreements were reached which are captured in this WF
Additinal a number of open issue for further discussion were lited. Also those are listed in this WF.

## Slide 3: Agreements
RAN4 use ‘actively measured’ in the definition of overlapping and non-overlapping carriers is agreeable conditioned that RAN4 also defines the conditions for ‘actively measured’.
  RAN4 will define the conditions for ‘actively measured’ carrier.
RAN4 follow RAN2 and captures that the UE performs the idle measurement for the frequencies in configured frequency list only when the UE support CA or MR-DC between the frequency and the serving frequency.

## Slide 4: Agreements
The total number of carriers that the UE must measure, for mobility and for EMR (overlapping and non-overlapping), should not exceed UE’s NR idle mode mobility measurement capability (section 4.2.2.1 in 38.133).
UE requirements related to number of overlapping and non-overlapping carriers for EMR in NR SA idle mode, use following in order to enable further discussions in RAN4 while leaving all numbers FFS:
  The total number carriers the UE at least shall be able to measure for EMR, N ≤ 14;
    N = A + B;
    The number of overlapping carriers, A = [0;x];
    The number of non-overlapping carriers, B = [0;y]
  A, B, x and y are all FFS.
  There may be additional restrictions on number of LTE carriers to be measured in NR idle.

## Slide 5: Agreements
RAN4 agree to option 1 and defines requirements for the detected cell status for the EMR measurement when UE transitions from RRC Connected mode to Idle or Inactive mode and after UE has entered Idle or Inactive mode
  Note: further clarification as to the conditions needs to be discussed

## Slide 6: Further work
The following pages includes a collection of items
These items are for discussion in the comming meeting(s)
The open items are based on the issues left without agreement in 2nd round discussion in the RAN4#94e meeting
Companies are encouraged to bring discussion papers and views at least on those topics for the coming meeting to progress the work.

## Slide 7: Way Forward
Questions for further discussion (Measurement requirements):
Shall RAN4 define UE EMR requirements for EMR carriers while T331 timer is active?
Shall RAN4 need to define UE EMR requirements for EMR carriers when T331 timer has expired?
Shall RAN4 define UE EMR measurement requirements for EMR for overlapping EMR carriers?
  when T331 is running?
  when T331 has expired?
Shall RAN4 define UE EMR measurement requirements for EMR for non-overlapping EMR carriers?
  when T331 is running?
  when T331 has expired?

## Slide 8: Way Forward
Continue the discussion related to cell detection and measurement requirements on EMR carrier, at least addressing the following topics:
RAN4 needs to further discuss the UE measurement requirements details at least including:
  Cell detection requirements for overlapping and non-overlapping carriers.
  Measurement requirements for overlapping and non-overlapping carriers.
  Accuracy requirements for overlapping and non-overlapping carriers.

## Slide 9: Way Forward
Discuss further. Options 3 and 4 (see R4-2002177) are seemingly very similar and RAN4 could continue discussion based on those as baseline. These can also be realized without introducing any new thresholds for EMR
No additional thresholds are needed for EMR
Let RAN2 decide
Use existing search thresholds
Weighted number of EMR carriers based on cell center or cell edge based on serving cell threshold.

## Slide 10: Way Forward
Continue the discussion if or how to capture the measurement assumptions for EMR carrier when cell type changes due to cell change
RAN4 to discuss what is potentially not covered by RAN2 agreements and if this leads to a need for RAN4 requirements
RAN4 to discuss further the expected UE behaviour related to detected and measured cell needs to be captured for EMR specifically. This can be part of the discussion considering measurement requirement
RAN4 to continue to discuss Impact on early measurements after T331 stops and before reporting EMR.