## Slide 1: WF on R16 NR RRM enhancements - BWP switching on multiple CCs
Intel Corporation
3GPP TSG-RAN WG4 Meeting #94-e R4-2002244
Electronic Meeting, 24 Feb. – 6 Mar., 2020

## Slide 2: Background
In RAN4#93 WF on BWP switching on multiple CCs was approved - R4-1915933

## Slide 3: Simultaneous BWP switching on multiple CCs (1)
RRC based simultaneous triggering for NR-DC operation
Agreement: RRC based simultaneous triggering for BWP switch on multiple CCs for NR-DC operation is not considered
Delay requirements for DCI/timer based BWP switch
Agreement: ; N: Number of CCs with simultaneous BWP switch; K is number of CCs that can be processed simultaneously; D is incremental delay for BWP switch processing on additional CCs
FFS on D and K
Options for D
  D=100us for Type 1; 200 us for Type 2
  D = 450us for Type 1; 1.5ms for Type 2
  Other options not precluded
Options for K
  K=1
  K based on UE
  Other options not precluded

## Slide 4: Simultaneous BWP switching on multiple CCs (2)
Delay requirements for RRC based BWP switch
Switching delay for RRC based simultaneous switching is FFS
Option 1 : ; N: Number of CCs with simultaneous BWP switch; K: Number of CCs that can be processed simultaneously
  Options for K
    K=1
    K = 4
Option 2 : Same as single CC ( without extension

## Slide 5: Simultaneous BWP switching on multiple CCs (3)
Interruption requirements for simultaneous BWP switch
Agreement: Consider interruption on each CC separately
FFS on interruption length
Option 1: Same interruption as Rel-15 single CC on each CC.
Option 2 :Extend interruption compared to single CC case; Extension depends on number of CCs undergoing simultaneous BWP switch
Option 3a : Interruption length is determined by smallest SCS among all CCs before and after BWP switch
Option 3b : ; K=1

## Slide 6: Partial Overlap BWP switching on multiple CCs
Conditions when requirements for partial overlap BWP switch are defined
Agreement: For DCI and RRC based BWP switch with partial overlap switch requirements are defined only defined when UE is capable of per FR gap. No restriction for timer based
DCI based partial overlap BWP switch for NR-DC
Agreement: DCI based partial overlap BWP switch for NR-DC is defined
Delay requirements for DCI/Timer/RRC based BWP switch
FFS on delay requirements for partial overlap BWP switch
Interruption requirements for partial overlap BWP switch
Agreement: Same as single CC, considered on each CC separately