## Slide 1: WF on inter-frequency without MG
CMCC
3GPP TSG-RAN WG4 Meeting #94-e R4-2002250
Online, 24 Feb. – 6 Mar., 2020

## Slide 2: Background
R4-1915853 WF on inter-frequency without MG was agreed in RAN4#93meeting.

## Slide 3: Sub-topic 2-1: Capability of supporting inter-frequency measurement without MG
  Option 1: Optional with UE capability signaling
  Option 2: Mandatory with UE capability signaling

## Slide 4: Assumption of searcher numbers
The number of searchers is up to 2 when discussing the requirement of CSSF outside gap.
  For CA capable UE, the number of searchers is 2
  FFS: For non-CA capable UE, the number of searchers is 1
For CSSF outside gap, the performance of PCC in NR SA should remain the same. Therefore, the inter frequency MO without gap shares the same searcher as all the other SCCs.

## Slide 5: How to handle the backward compatible issue
  Specify the UE measurement behavior in the spec:
    If all the MOs are inter-freq w/o MG to this UE but NW configured MG, UE will use the MG to perform these inter-freq measurement;
    Note: Detailed sentences to be captured in the spec can be further discussed when drafting the CR.

## Slide 6: Sub-topic 2-1: UE behaviour for inter-frequency measurement w/o MG partially overlapped with MG
Solution#1:
  For CA capable UE :
    Define requirements based on the assumption that UE perform measurement outside gaps (same as intra-frequency measurement without MG), when configured MG is partially overlapped with inter-frequency SMTC and inter-frequency SSB is completely contained in the active BWP of the UE.
  For non-CA capable UE:
    Option 1: Inter-frequency measurements should always happen in gaps.
    Other option is not excluded

## Slide 7: Sub-topic 2-1: UE behaviour for inter-frequency measurement w/o MG partially overlapped with MG
Solution#2
  For UE configured with multiple CC’s:
    Define requirements based on the assumption that UE perform measurement outside gaps (same as intra-frequency measurement without MG), when configured MG is partially overlapped with inter-frequency SMTC and inter-frequency SSB is completely contained in the active BWP of the UE.
  For UE configured with single CC:
    Option 1: Inter-frequency measurements should always happen in gaps.

## Slide 8: Sub-topic 2-3: Scheduling restriction for inter-frequency measurement w/o MG
Synchronization is always assumed for partial and fully overlapped TDD carriers that to be measured for inter-frequency measurement without MG.
  Option 1: No new signaling is needed. Clarify in the spec that synchronization is assumed for overlapped TDD carriers.
For TDD bands on FR1 and FR2, UE is not expected to transmit PUCCH/PUSCH/SRS on SSB symbols to be measured, and on 1 data symbol before each consecutive SSB symbols to be measured and 1 data symbol after each consecutive SSB symbols to be measured within SMTC window duration
In FR1 mixed numerology (UE is not capable to support mixed numerologies), UE is not expected to transmit PUCCH/PUSCH/SRS or receive PDCCH/PDSCH/TRS/CSI-RS for CQI on all symbols within SMTC window duration.
  For partial and fully overlapped TDD carriers, UE is not expected to transmit PUCCH/PUSCH/SRS on SSB symbols to be measured, and on 1 data symbol before each consecutive SSB symbols to be measured and 1 data symbol after each consecutive SSB symbols to be measured within SMTC window duration

## Slide 9: Sub-topic 2-4: Scheduling restriction when the target SSB has a different SCS grid
  FFS: When the target SSB has a different SCS grid as that of UE’s serving cell, UE is allowed to have scheduling restriction in the entire SMTC duration.