## Slide 1
3GPP TSG-RAN WG4 Meeting #94-e R4-2002253
Electronic Meeting, Feb.24th – Mar.6th 2020
Agenda Item: 8.17.1
WF on RRM for NR HST
CMCC

## Slide 2: Background
The following WFs were approved:
  R4-1912781 WF on RRM for NR HST, RAN4#92BIS
  R4-1915887 WF on RRM for NR HST, RAN4#93

## Slide 3: Cell re-selection requirements
  Whether to keep M2, M3, M4 for cell re-selection with DRX cycle =0.32s:
    Option 1 (NOKIA,): remove M2, M3, M4 without restriction on SMTC period
    Option 2 (QC, vivo, Samsung, Intel, HW): When SMTC < 40, remove M2, M3, M4; when SMTC >= 40, M2 = 1.5, M3 = M4 = 2
    Option 3 (CMCC, Apple, QC, Intel, vivo, CATT, MTK): When SMTC < =40, remove M2, M3, M4; when SMTC >40, M2 = 1.5, M3 = M4 = 2
    Option 4 (Ericsson, QC): When SMTC < =40, remove M2, M3, M4; when SMTC >40, M2 = 1.5, M3 = M4 = 2. Adding notes in the requirements, e.g. “Note x : Operation with scaling factor M=1.5, M=2 may not be sufficient in all high speed deployments considered in this release of the specifications”

## Slide 4: Cell identification delay requirements for non-DRX case in connected mode
Rel-15 SSB index acquiring delay requirements for non-DRX case is reused for NR HST

## Slide 5: Cell identification delay requirements for DRX case in connected mode
Whether to keep the relaxation factor of 1.5 for DRX cycle <= 0.32s
  Option 1 (NOKIA): remove the factor without restriction on SMTC period
  Option 2 (QC): when SMTC < 40, remove 1.5x scaling factor; when SMTC > =40, keep the scaling factor
  Option 3 (CMCC, DCM, Apple, Samsung, Intel, QC, HW, CATT, MTK): when SMTC < =40, remove 1.5x scaling factor; when SMTC > 40, keep the scaling factor
  Option 4 (Ericsson, QC): When SMTC < =40, remove M2, M3, M4; when SMTC >40, M2 = 1.5, M3 = M4 = 2. Adding notes in the requirements, e.g. “Note x : Operation with scaling factor M=1.5, M=2 may not be sufficient in all high speed deployments considered in this release of the specifications”

## Slide 6: Cell identification delay requirements for DRX case in connected mode
Measurement delay for DRX cycle < 0.32s
  Option 1: 5 samples
  Option 2: 3 samples
  Other options are not precluded
  for measurement delay with DRX cycle = 320ms, the number of samples is:
    Option 1 (Ericsson, DOCOMO, CMCC, Nokia, CATT): 3 samples
    Option 2 (QC, DOCOMO, Intel, Vivo, MTK): 4 samples
    Option 3 (Intel, Vivo, HW, Samsung, MTK): 5 samples

## Slide 7: Cell identification delay requirements for DRX case in connected mode
Measurement delay for DRX cycle > 0.32s
  Option 1 (QC, DOCOMO, CMCC, Intel, Samsung, MTK ): 3 samples are used when SMTC <= 40ms, 5 samples are used when SMTC >40ms
  Option 2: 3 samples are used when SMTC < 40ms, 5 samples are used when SMTC >= 40ms
  Option 3 (Intel, HW, Samsung): 5 samples
  Option 4 (Ericsson, Nokia, CATT): 3 samples applied for all the candidate SMTC
  Option 5 (Ericsson): 3 samples are used when SMTC <= 40ms, 5 samples are used when SMTC >40ms. Adding notes in the requirements, e.g. “Note x : Operation with 5 samples may not be sufficient in all high speed deployments considered in this release of the specifications”
  Applied DRX cycle in cell identification requirements for HST
  Option 1: for NR HST, enhanced requirements are considered for DRX cycle <= 1.28s, and no enhanced requirements are considered for DRX cycle = 2.56s Other options are not precluded
  Other options are not precluded

## Slide 8: RLM
Q1: whether the outcome on the scaling factor for L3 measurement can be reused for RLM?
  Option 1 (Ericsson, DOCOMO, Nokia, Samsung): YES
  Option 2 (QC, CMCC, Intel, HW): NO
Q2: If the answer to Q1 is NO, whether 1.5x relaxation factor for RLM shall be kept?
  Option 1 (QC, CMCC, Intel, HW): keep the 1.5x scaling factor
  Option2: 1.5x relaxation factor is kept when TSSB >= TBD, 1.5x relaxation factor is removed when TSSB < TBD

## Slide 9: Beam management
CBD based on SSB/CSI-RS
  Rel-15 CBD requirements based on SSB/CSI-RS (including delay and accuracy) are reused for NR HST
BFD based on SSB/CSI-RS
  Q1: whether the outcome on the scaling factor for L3 measurement can be reused for BFD?
    Option 1 (Ericsson, DOCOMO, Nokia, Samsung): YES
    Option 2 (QC, CMCC, Intel, HW, MTK): NO
  Q2: If the answer to Q1 is NO, whether 1.5x relaxation factor for BFD shall be kept?
    Option 1 (QC, CMCC, Intel, HW, MTK): keep the 1.5x scaling factor
    Option2 : 1.5x relaxation factor is kept when TSSB >= TBD, 1.5x relaxation factor is removed when TSSB < TBD

## Slide 10: Beam management
L1-RSRP based on SSB/CSI-RS
  Reuse Rel-15 SSB/CSI-RS based L1-RSRP measurement requirements, including the measurement accuracy and sample number for HST. FFS: measurement delay including the 1.5x scaling factor, for NR HST

## Slide 11: Inter-RAT measurement
NR- EUTRA Inter-RAT measurement
  Enhance NR- EUTRA inter-RAT measurement requirements to support HST
  Cell re-selection requirements on NR- EUTRA inter-RAT measurement in idle mode
    Option 1 (CMCC, HW, Ericsson, vivo, Nokia, Apple, MTK, Intel): The principle is that NR to EUTRA inter-RAT measurements follows the R16 EUTRA HST enhanced measurement requirements. And the details are shown in the following Table:
DRX cycle length [s] | Tdetect,EUTRAN_Intra [s] (number of DRX cycles) | Tmeasure,EUTRAN_Intra [s] (number of DRX cycles) | Tevaluate,E-UTRAN_intra [s] (number of DRX cycles)
0.32 | 2.56 (8) | 0.32(1) | 0.96(3)
0.64 | 5.12 (8) | 0.64 (1) | 1.92 (3)
1.28 | 8.96 (7) | 1.28 (1) | 3.84 (3)
2.56 | 58.88 (23) | 2.56 (1) | 7.68 (3)
    Option 2 (QC):
DRX cycle length [s] | TdetectEUTRA_FDD [s] (number of DRX cycles) | TmeasureEUTRA_FDD [s] (number of DRX cycles) | TevaluateEUTRA_FDD [s] (number of DRX cycles)
0.32 | 7.68 (24) | 1.28 (4) | 1.6(5)
0.64 | 12.8 (16) | 1.28 (2) | 1.92 (3)
1.28 | 12.8(10) | 1.28 (1) | 3.84 (3)
2.56 | 58.88 (23) | 2.56 (1) | 7.68 (3)

## Slide 12: Inter-RAT measurement
NR- EUTRA Inter-RAT measurement
  Cell re-selection requirements on NR- EUTRA inter-RAT measurement in idle mode
    Option 3 (QC)
DRX cycle length [s] | TdetectEUTRA_FDD [s] (number of DRX cycles) | TmeasureEUTRA_FDD [s] (number of DRX cycles) | TevaluateEUTRA_FDD [s] (number of DRX cycles)
0.32 | 5.76(18) | 0.64 (2) | 0.96(3)
0.64 | 7.68 (12) | 1.28 (2) | 1.92 (3)
1.28 | 8.96(7) | 1.28 (1) | 3.84 (3)
2.56 | 58.88 (23) | 2.56 (1) | 7.68 (3)

## Slide 13: Inter-RAT measurement
NR- EUTRA Inter-RAT measurement
  Cell identification without DRX in connected mode
    Reuse R15 inter-RAT measurement requirement with non-DRX case in TS 38.133 (including both Tinter1 = 60ms and Tinter1 = 30ms) for NR HST

## Slide 14: Inter-RAT measurement
NR- EUTRA Inter-RAT measurement
  Cell identification with DRX in connected mode
    Option 1(CMCC, Ericsson, Nokia)
    Option 2 (HW, QC)
DRX cycle length (s) | TIdentify, E-UTRAN (s) (DRX cycles) | 
 | Gap period = 40 ms, 20 ms | Gap period = 80 ms
≤0.16 | Non-DRX requirements in clause 9.4.2.2 apply | Non-DRX requirements in clause 9.4.2.2 apply
0.16 < DRX-cycle<1.28 | Note1 (10) | Note1 (10)
1.28 | Note1 (8) | Note1 (8)
1.28< DRX-cycle ≤10.24 | Note1 (20) | Note1 (20)
NOTE 1: The time depends on the DRX cycle length. |  | 
DRX cycle length (s) | TIdentify, E-UTRAN TDD (s) (DRX cycles) | 
 | Gap period = 40 ms, 20 ms | Gap period = 80 ms
≤0.16 | Non-DRX requirements in clause 9.4.3.2 apply | Non-DRX requirements in clause 9.4.3.2 apply
0.256 | 3.84* CSSFinterRAT (15*CSSFinterRAT) | 3.84*K (15*CSSFinterRAT)
0.32 | 4.8*CSSFinterRAT (15*CSSFinterRAT) | 4.8*K (15*CSSFinterRAT)
0.32< DRX-cycle ≤10.24 | Note1 (20*CSSFinterRAT) | Note1 (20*CSSFinterRAT)
NOTE 1: The time depends on the DRX cycle length. NOTE 2: CSSFinterRAT is as defined in clause 9.4.3.2. |  | 

## Slide 15: Inter-RAT measurement
NR- EUTRA Inter-RAT measurement
  Cell identification with DRX in connected mode
    Option 3 (Vivo)
    Option 4 (QC, Vivo, Nokia)
DRX cycle length (s) | TIdentify, E-UTRAN TDD (s) (DRX cycles) | 
 | Gap period = 40 ms, 20 ms | Gap period = 80 ms
≤0.16 | Non-DRX requirements in clause 9.4.3.2 apply | Non-DRX requirements in clause 9.4.3.2 apply
0.16< DRX-cycle ≤0.32 | Note1 (15*CSSFinterRAT) | Note1 (15*CSSFinterRAT)
0.64 | 5.12*CSSFinterRAT (8*CSSFinterRAT) | 5.12*CSSFinterRAT (8*CSSFinterRAT)
1.28 | 8.96*CSSFinterRAT (7*CSSFinterRAT) | 8.96*CSSFinterRAT (7*CSSFinterRAT)
1.28< DRX-cycle ≤10.24 | Note1 (20*CSSFinterRAT) | Note1 (20*CSSFinterRAT)
NOTE 1: The time depends on the DRX cycle length. |  | 
QC compromised proposal for NR- EUTRA inter-RAT measurement in connected mode for DRX case |  | 
DRX cycle length (s) | TIdentify, E-UTRAN TDD (s) (DRX cycles) | 
 | Gap period = 40 ms, 20 ms | Gap period = 80 ms
≤0.16 | Non-DRX requirements in clause 9.4.3.2 apply | Non-DRX requirements in clause 9.4.3.2 apply
0.16<DRx cycle<=0.32 | Note1 (15) | Note1 (15)
0.32< DRx cycle <= 0.64 | Note1 (10) | Note1 (10)
0.64 < DRx cycle <= 1.28 | Note1 (8) | Note1 (8)
1.28< DRX-cycle ≤10.24 | Note1 (20) | Note1 (20)
NOTE 1: The time depends on the DRX cycle length. NOTE 2: The requirement only applicable to CSSFinterRAT = 1 case |  | 

## Slide 16: Inter-RAT measurement
EUTRA-NR Inter-RAT measurement
  Enhance EUTRA-NR inter-RAT measurement requirements to support NR HST
  Cell re-selection requirements on EUTRA-NR inter-RAT in idle mode
    Option 1 (CMCC, Ericsson, Nokia, Apple, MTK): the cell re-selection requirements on EUTRA-NR inter-RAT measurement follow R16 HST NR cell re-selection requirements
    Option 2 (QC, Vivo): discuss possible options between non-HST inter-RAT requirement and HST intra-frequency measurement requirement.

## Slide 17: Inter-RAT measurement
EUTRA-NR Inter-RAT measurement
  Cell re-selection requirements on EUTRA-NR inter-RAT in idle mode
    Option 3 (QC):
DRX cycle length [s] | Tdetect,NR [s] (number of DRX cycles) | Tmeasure,NR [s] (number of DRX cycles) | Tevaluate,NR [s] (number of DRX cycles) | 
0.32 | 6.4 x 1.5 (20 x 1.5) | 1.28 x 1.5 (4 x 1.5 ) | 0.96 x 1.5 (3 x 1.5) | 
0.64 | 10.24 (16) | 1.28 (2 ) | 1.92(3) | 
1.28 | 12.8 (10) | 1.28 (1 ) | 6.4(3) | 
2.56 | 58.88 x N1 (23 x N1) | 2.56 (1) | 7.68(3) | 

## Slide 18: Inter-RAT measurement
EUTRA - NR Inter-RAT measurement
  Cell identification without DRX and cell identification with DRX in connected mode
    Option 1 (CMCC, Ericsson, Apple, MTK): cell identification requirements on EUTRA-NR inter-RAT measurement in connected mode for non-DRX case follow R16 HST NR requirements
    Option 2 (QC): discuss possible options between non-HST inter-RAT requirement and HST intra-frequency measurement requirement.
    Option 3 (Vivo): Since for non-HST the measurement period requirement of an inter-RAT NR carrier in LTE is same as that of inter-frequency requirement in NR, our proposal is to follow the same enhancement methodology, but the baseline should be inter-frequency requirement
    Option 4 (Nokia): RAN4 should consider the overall system delay and consider whether the existing requirements are sufficient or whether R16 HST NR measurement requirements would need to be applied.
Condition NOTE1,2 | T SSB_measurement_period_inter
No DRX | Max(200ms, 8  Max(MGRP, SMTC period))  CSSFinter
DRX cycle ≤ 320ms | Max(200ms, Ceil(8  1.5)  Max(MGRP, SMTC period, DRX cycle))  CSSFinter
DRX cycle > 320ms | 8  DRX cycle  CSSFinter
NOTE 1: DRX or non DRX requirements apply according to the conditions described in clause 3.6.1 NOTE 2: In EN-DC operation, the parameters, timers and scheduling requests referred to in clause 3.6.1 are for the secondary cell group. The DRX cycle is the DRX cycle of the secondary cell group. | 

## Slide 19: Inter-RAT measurement
EUTRA - NR Inter-RAT measurement
  Cell identification without DRX and cell identification with DRX in connected mode
    Option 5 (QC):
Condition NOTE1,2 | TPSS/SSS_sync_intra | T SSB_measurement_period_intra | TSSB_time_index_intra
No DRX | max[600ms, [8] x max(MGRP, SMTC period)] | Max(200ms, 8  Max(MGRP, SMTC period))  CSSFinter | max[120ms, [3] x max(MGRP, SMTC period)]
DRX cycle ≤ 320ms | max[600ms, ceil([8]xM) x max(MGRP, SMTC period, DRX cycle)] | Max(200ms, Ceil(8  M)  Max(MGRP, SMTC period, DRX cycle))  CSSFinter | max[120ms, ceil([3] x M) x max(MGRP, SMTC period, DRX cycle)]
DRX cycle > 320ms | 4 x DRX cycle | 4  DRX cycle  CSSFinter | [3] x DRX cycle
NOTE 1: DRX or non DRX requirements apply according to the conditions described in clause 3.6.1 NOTE 2: In EN-DC operation, the parameters, timers and scheduling requests referred to in clause 3.6.1 are for the secondary cell group. The DRX cycle is the DRX cycle of the secondary cell group. NOTE 3: When SMTC < =40, M=1; when SMTC >40, M = 1.5 |  |  | 

## Slide 20: SS-SINR
Option 1(QC, Ericsson, DCM, HW): SINR accuracy requirement is not applicable to HST scenario when SNR > 5dB
Option 2 (vivo, HW, MTK, QC): SINR accuracy requirement is not applicable to HST scenario
Option 3 (DCM, Ericsson, CMCC): identify the SNR upper bound below which the SS-SINR measurement accuracy requirements are specified