## Slide 1: WF on NR Positioning gNB measurement requirements and report mapping
Ericsson
3GPP TSG-RAN WG4 Meeting # 94-e
Electronic Meeting, Feb 24-March 06, 2020
Agenda: 8.8.1
R4-2002275

## Slide 2: gNB Measurements for Accuracy Requirements
RAN4 shall define accuracy requirements for the following gNB positioning measurements:
  gNB Rx-Tx timing difference
  SRS-RSRP
FFS whether to define accuracy requirements for:
  “UL RTOA” and/or “AoA / ZoA” measurements.
  Companies are encouraged to bring analysis in the next RAN4 meeting.

## Slide 3: Optionality of gNB accuracy requirements
gNB positioning measurement accuracy requirements are optional:
  FFS whether accuracy requirement for a positioning measurement supported by a gNB is also optional.

## Slide 4: Scenarios for gNB accuracy requirements
Following conditions and scenarios for gNB accuracies are FFS until next RAN4 meeting
Side conditions e.g. SNR:
  Option 1: based on only serving cell and corresponding SNR level
  Option 2: based on only neighbor cell (e.g. SNR lower than in serving cell) and corresponding SNR level
Common vs specific side conditions e.g. SNR:
  Option 1: same side conditions for different type of gNB measurements
  Option 2: side conditions specific to each gNB measurement
Antenna configuration:
  Option 1: fixed antenna beams
  Option 2: other options not precluded
RS pattern:
  SRS configuration: FFS
  PRS configuration: FFS
BS type: 1-C, 1-H, 1-O, 2-O
  Option 1: accuracy depends on BS type
  Option 2: other options not precluded

## Slide 5: SRS-RSRP Report Mapping
SRS-RSRP reporting granularity = 1dB.
SRS-RSRP maximum and minimum values are FFS until next meeting.
Candidate options:
  SRS-RSRP minimum value:
    Option 1: SRS-RSRP min value = SS-RSRP min value.
    Option 2: SRS-RSRP min value  SS-RSRP min value.
  SRS-RSRP maximum value:
    Option 1: SRS-RSRP max value = SS-RSRP max value.
    Option 2: SRS-RSRP max value  SS-RSRP max value.

## Slide 6: gNB Rx-Tx Time Difference Report Mapping
gNB Rx-Tx time difference report mapping is FFS until next meeting.
Candidate options:
  Option 1: Reuse UE Rx-Tx time difference report mapping for defining gNB Rx-Tx time difference report mapping.
  Option 2: Reuse RSTD report mapping for defining gNB Rx-Tx time difference report mapping.
  Option 3: gNB Rx-Tx time difference report mapping is different than in options 1 and 2.

## Slide 7: UL RTOA Report Mapping
UL RTOA report mapping is FFS until next meeting.
Candidate options:
  Option 1: Reuse gNB Rx-Tx time difference report mapping for defining UL RTOA report mapping.
  Option 2: From 0 to 9600Ts with granularity = Tc*2k.
  Option 3: UL RTOA report mapping is different than in options 1 and 2.

## Slide 8: AoA/ZoA Report Mapping
AoA:
  from -180 to +180 degrees with granularity = 0.1 degree.
ZoA:
  from 0 to +180 degrees with granularity = 0.1 degree.