## Slide 1: WF on NR-U RRM requirements (Part 3)
Nokia, Nokia Shanghai Bell
3GPP TSG-RAN WG4 Meeting #94-e
Electronic Meeting, Feb.24th – Mar.6th 2020
      R4-2002278
Document for: Approval

## Slide 2: Agreements in 1st round Tentative Agreements in the 2nd Round

## Slide 3: L1-RSRP measurements
L1,max = 0 when timeRestrictionForChannelMeasurement is configured and the table is updated as:
Periodic and aperiodic L1-RSRP reporting delay reuses Rel-15 reporting delay
Configuration | TL1-RSRP_Measurement_Period_SSB (ms)
non-DRX | max(TReport, ceil((M+L1)*P)*TSSB)
DRX cycle ≤ 320ms | max(TReport, ceil(1.5*(M+L1)*P)*max(TDRX,TSSB))
DRX cycle > 320ms | ceil((M+L1)*P)*TDRX
Note 1: TSSB is the periodicity of the SSB-Index configured for L1-RSRP measurement. TDRX is the DRX cycle length. TReport is configured periodicity for reporting. Note 2: L1=0 if higher layer parameter timeRestrictionForChannelMeasurement is configured. Otherwise L1 is the number of SSBs not available at the UE during TL1-RSRP_Measurement_Period_SSB where L1 ≤ L1max. Note 3: L1,max=7 for Max(TDRX,TSSB) ≤ 40ms where TDRX=0 for non-DRX, L1,max=5 for 40ms < Max(TDRX, TSSB) ≤ 320ms, and L1,max=3 for TDRX > 320ms. | 

## Slide 4: CSI-RS based L1-RSRP measurement period
FFS:
  Option 1: CSI-RS L1-RSRP measurements follow the same approach of SSB L1-RSRP measurements:
    Same number of samples for both SSB based L1-RSRP measurement and CSI-RS
    Same extension value L1 and L1-max as in SSB based L1-RSRP
  Option 2: A new approach or conditions are needed for CSI-RS based L1-RSRP measurements under LBT failure.
  Other options are not precluded.

## Slide 5: Detailed UE behavior when receiving the MAC CE activation command for semi-persistent CSI reporting, in case of UL LBT failure for sending the ACK
If UE cannot transmit HARQ-ACK on MAC-CE activation due to UL CCA failure, UE continues to be in its previous state, i.e., it should not start L1-RSRP measurement and reporting

## Slide 6: SFDT measurements
It is RAN4 understanding that the UE behavior when exceeding Tmeasure_SFTD_LBT_max is that the UE shall not report the measurement and abandon the inter-RAT SFTD measurement. The exact wording can be aligned with RAN2.

## Slide 7: Inter-RAT SFTD measurements
Background from RAN4#93
UE behavior upon exceeding Tmeasure_SFTD_LBT_max: UE shall stop the search
  FFS whether UE abandons the measurement
  Tmeasure_SFTD_LBT_max = k× Tmeasure_SFTD1, k=TBD≤10
Options in RAN4#94e
Option 1: k = 6
Option 2: k =2

## Slide 8: UE behaviour in case of successive UL LBT failures during event-triggered reporting
For event triggered reporting:
  RAN4 should not specify a pre-defined value of ΔUL,max
There are RAN2 procedures in place for when either the HARQ retransmissions or UL LBT failure procedures are triggered.
FFS: whether/ how to refer to these procedures when discussing the extension of the measurement report.

## Slide 9: Additional time for PBCH payload reading for SSB index identification
There is no need to specify additional time for PBCH reading during SSB index identification in FR1 NR-U, if Q is known to the UE.

## Slide 10: RSSI and Channel Occupancy measurements
No measurement report mapping is defined for Channel Occupancy measurements in NR-U.
Measurement reporting requirements are to be specified for periodic RSSI and CO.
  Note: this agreement can be reviewed in case further agreements are made in RAN2.

## Slide 11: RSSI and Channel Occupancy Measurements
RAN4 to further discuss scheduling restrictions during RSSI/CO measurements
RAN4 to discuss interruption requirements during RSSI/CO measurements.
No wideband RSSI and channel occupancy reporting criteria are seen to be needed in Rel-16.

## Slide 12: Issues that need further discussion

## Slide 13
The intention of this part of the Way forward is to list the options discussed during RAN4 94e. Companies are encouraged to provide input to the topics in this Section.
The issues are detailed in R4-2002171.

## Slide 14: Further discussion is needed: Issue 1-3: Semi-persistent L1-RSRP reporting delay
Option 1: Extend the delay, how to extend the delay is FFS.
Option 2: Semi-persistent L1-RSRP reporting delay in NR-U reuses the Rel-15 reporting delay.

## Slide 15: Further discussion is needed: Issue 1-4: Semi-persistent CSI reporting with PUCCH
Option 1: Extend the delay, how to extend the delay is FFS.
Option 2: Semi-persistent L1-RSRP reporting delay in NR-U reuses the Rel-15 reporting delay.

## Slide 16: Further discussion is needed: New Issue 1-4-2: Detailed UE behavior when receiving the MAC CE deactivation command for semi-persistent CSI reporting, in case of UL LBT failure for sending the ACK
Option 1:
  If UE cannot transmit HARQ-ACK on MAC-CE deactivation due to UL CCA failure, UE continues to be in its previous state, i.e., it should measure and report L1-RSRP until it successfully transmits HARQ-ACK
Option 2:
  For semi-persistent CSI reporting with PUCCH, if UE cannot transmit HARQ-ACK on the MAC CE deactivation due to the UL LBT failures, UE continues the L1-RSRP measurement and delay the L1-RSRP reporting. If UE does not receive deactivation command during the delay period, UE restart to transmit L1-RSRP reporting. FFS how to extend the delay.

## Slide 17: Further discussion is needed: Issue 2-3: Inter-RAT SFTD measurements reporting delay
Proposals
  Option 1 (R4-2000931 MediaTek): For the reporting delay of inter-RAT SFTD measurement, X and Y are not necessary to be specified.
  Option 2 (R4-2002086 Ericsson): For testing of inter-RAT SFTD measurement delay under CCA, the test system shall guarantee that at some point in the test there is a time period of duration 2 × Tmeasure_SFTD1 – 1 × SMTC period during which SSBs are transmitted consecutively. Provided that such period is starting T1 ms into the SFTD measurement, the UE shall be capable of determining SFTD within a physical layer measurement period Tmeasure_SFTD_CCA = T1 + 2 × Tmeasure_SFTD1 – 1 ×

## Slide 18: Further discussion is needed Issue 3-2: Reporting delay for (event-triggered) periodic reporting
FFS: Decide the event-triggered periodic and periodic reporting delay:
  Option 1: Adopt the same definition as in Rel-15.
  Option 2: For periodic and event-triggered periodic measurement reporting, the UE measurement reporting delay is extended due to UL LBT failures until the time point of the successful reporting attempt or until the new periodic measurement is available, according to [TBD RAN2 specification]. No extension for UL channel access category 1.

## Slide 19: Further discussion is needed Issue 3-3: Reporting delay for event triggered reporting
For the event-triggered reporting delay:
  Option 1: No need to extend the delay, clarify that the measurement reporting delay excludes a delay which is caused by no UL resources available due to CCA. Wording can be further discussed.
  Option 2: For event-triggered measurement reporting, the UE measurement reporting delay is extended due to UL LBT failures until the time point of the successful reporting attempt, according to [TBD RAN2 specification]. No extension for UL channel access category 1.

## Slide 20: Further discussion is needed Issue 4-1 Additional time for PBCH payload reading for SSB index identification
Options discussed in RAN4 #94e
  Option 1: We can assume that Q is always known to the UE
  Option 2: We cannot assume that Q is always known to the UE

## Slide 21: Further discussion is needed: Issue 5-1: RSSI Intra-frequency and Inter-frequency definition
  Intra-frequency RSSI measurements are defined when both conditions are satisfied:
    Condition 1:
      Option 1a: RMTC configured SCS is the same as the active BWP in the serving cell.
      Option 1b: RMTC configured SCS is the same as the SCS of the serving cell SSB,
    Condition 2:
      Option 2a: Measurement BW is contained within the active BWP of the serving cell
      Option 2b: The center frequency of the PRB set configured for RSSI measurement is aligned with the center frequency of an intra-frequency SSB.
    Inter-frequency measurements are defined when at least one condition above is not satisfied.

## Slide 22: Further discussion is needed Issue 5-2: need for measurement gaps
Whether new measurement gap patterns are needed for RSSI measurements

## Slide 23: Further discussion is needed Issue 5-3: RSSI measurement report mapping
  Option 1: RSSI measurement report mapping is the same as for CLI-RSSI, i.e. from -100 dBm to -25 dBm with 1 dBm resolution.
    Note: this is equivalent to adopting the table in 9.1.18.5.1-1 in TS 36.133 as baseline
  Option 2: Define a new measurement report mapping

## Slide 24: Further discussion is needed Issue 5-5: RSSI/CO measurement periods
Proposal discussed during the meeting:
    The RSSI and CO measurement periods depend on:
      max(reportInterval, rmtc-Period) in non-DRX when measurement gaps are not required,
      max(reportInterval, rmtc-Period, DRX) in DRX when measurement gaps are not required, or
      FFS: max(reportInterval, rmtc-Period, MGRP and gap sharing) in DRX when measurement gaps are required.
    For intra-frequency measurements:
      In wideband operation, whether to consider the number of measurement objects (Nintra-MO) in the measurement period, in case there are multiple intra-frequency measurement objects configured.
    for inter-frequency measurements:
      Whether to consider the number of measurement reports (Ninter-MO) and Nfreq in the measurement period.
    how to consider the sharing factor CSSF, and the lower bound R15 L3 measurements

## Slide 25: Further discussion is needed Issue 5-7: RMTC periodicity
Proposals discussed during the meeting:
  Option 1: RMTC periodicity to be from the set of {40, 80, 160, 320, 640} ms exclusively. RMTC measurement duration to be from the set of {1, 14, 28, 42, 56, 70, 84, 140} in units of OFDM symbols with the limitation of max RTMC duration to be capped at 5ms (i.e., 84 and 140 symbols to be valid only for 30 kHz SCS).
  Option 2: RAN4 requirements will be defined for all RMTC configurations.

## Slide 26: Further discussion is needed Issue 5-10: RSSI measurement bandwidth
RAN4 to define the RSSI measurement accuracy requirements based on:
  Option 1: SSB bandwidth.
  Option 2: Bandwidth configured by the gNB.

## Slide 27: Further discussion is needed Issue 5-11 RSSI report normalization
Option 1: The RSSI reporting is normalized to the SCS, allowing flexibility for the UE implementation to measure based on any value of N so long as accuracy requirements are met.
Option 2: No need to normalize the RSSI report.

## Slide 28: Further discussion is needed Topic 6: Measurement and Monitoring QCL-ed SSBs
No consensus was reached in this meeting. Companies are encouraged to bring their views on the options.
Option 1:
  UE is required to monitor at least one SSB from the set of SSBs that are QCLed with each other
Option 2:
  UE is required to monitor all SSBs from the set of SSBs that are QCLed with each other
Option 3:
  UE is required to monitor all SSBs regardless of QCL assumptions

## Slide 29: Further discussion is needed Issue 7-1: UE behavior upon exceeding the maximum number of DL LBT failures during PSS/SSS detection
Candidate options:
  Option 1) Behavior is implementation specific
  Option 2) Upon exceeding LPSS/SSS,max, the UE is not required to meet the corresponding intra-frequency PSS/SSS detection requirement.
  Option 3)
    Upon exceeding the maximum acceptable number of DL LBT failures UE would stop the PSS/SSS detection on the target unlicensed frequency layer, and UE would switch to another carrier for new PSS/SSS detection if this carrier is configured in the MOs.
    RAN4 shall allow UE to stop PSS/SSS detection if UE exceeds the maximum acceptable number of DL LBT failures for PSS/SSS detection on the target carrier and no other MOs are configured from network.

## Slide 30: Further discussion is needed Sub-topic 7-3: UE behaviour in RRC_CONNECTED mode when the serving cell is unavailable for consecutive SSB bursts
Whether it is necessary to specify a UE behavior in connected mode when the serving cell is unavailable for consecutive SSB bursts.

## Slide 31: Further discussion is needed How to address consecutively missing SSBs for intra and inter-frequency cells
A note or clarification is added in the intra-frequency (and inter-frequency) measurement requirements that the requirements apply provided any two closest SSB occasions available at the UE for the measurement shall be separated by no more than the maximum time requirement for the cell to remain known (8 seconds), with a reference to the place in TS 38.133 where this is defined.

## Slide 32: Further discussion is needed Issue 7-6: How to consider the QCLed beams during cell identification stage
There was one proposal about this topic, to add the following Note in each of the tables in cell identification clauses for NR-U.
  At least one SSB index in the same SSB position index shall be detectable, as specified in clause 9.2A.2, in the time period for PSS/SSS detection.

## Slide 33: Further discussion is needed Issue 7-7: UE behaviour in case of successive DL LBT failures during measurements.
o Option 1) After N unsuccessful measurement attempts due to exceeding the max number of unavailable SMTC occasions, UE should restart from the detection stage again. Value of N can be further discussed in RAN4.
o Option 3) No new UE behavior is needed.

## Slide 34: Further discussion is needed Issue 7-11: Scheduling availability during measurements
FFS: When the UE performs intra-frequency measurements in unlicensed spectrum, the following restrictions apply due to SS-RSRP or SS-SINR measurement
- The UE is not expected to transmit PUCCH/PUSCH/SRS on SSB symbols scheduled to be measured, and on 1 data symbol before each consecutive SSB symbols scheduled to be measured and 1 data symbol after each consecutive SSB symbols scheduled to be measured within SMTC window duration. If the high layer in TS 38.331 [2] signalling of smtc2 is configured, the SMTC periodicity follows smtc2; Otherwise SMTC periodicity follows smtc1.
FFS: When the UE performs intra-frequency measurements in unlicensed spectrum, the following restrictions apply due to SS-RSRQ measurement
- The UE is not expected to transmit PUCCH/PUSCH/SRS on SSB symbols scheduled to be measured, RSSI measurement symbols, and on 1 data symbol before each consecutive SSB scheduled to be measured/RSSI symbols and 1 data symbol after each consecutive SSB scheduled to be measured/RSSI symbols within SMTC window duration. If the high layer signalling of smtc2 is configured(in TS 38.331 [2]), the SMTC periodicity follows smtc2; Otherwise the SMTC periodicity follows smtc1.
FFS: When intra-band carrier aggregation in unlicensed spectrum is performed, the scheduling restrictions due to a given serving cell should also apply to all other serving cells in the same band on the symbols that fully or partially overlap with the aforementioned restricted symbols.

## Slide 35: Further discussion is needed Issue 8-2: Per sub-band RSSI report
o Option 1 Qualcomm (R4-2000722) MediaTek (R4-2000932): A RSSI/CO report consists of 1 RSSI measurement and 1 CO measurement.
  RSSI/CO report over multiple sub-bands requires multiple measurement objects.
o Option 2 Ericsson(R4-2001938): With Ecat=1, 1 report for RSSI and channel occupancy measurements is capable of minimum 1 RSSI measurement and 1 channel occupancy measurement over a channel [TS 37.213] per carrier frequency with CCA