## Slide 1: 3GPP TSG-RAN WG4 Meeting #94-e Electronic Meeting, 24 Feb.- 6 Mar.,2020
ZTE, …
WF on IAB EMC core requirements
R4-2002348

## Slide 2: Background
Based on [1] current EMC emission requirement is discussed in three parts:
Radiated emssion
conducted emission
harmonic and flicker
For radiated emission and harmonic and flicker, some agreements has been captured in slide 3 while for conducted emission the issue is captured in slide 4.
Based on [2] current EMC immunity requirement is dicussed in two parts:
Radiated immunity
Other immunity
So far no agreement on immunity requirement can achive, the issue is captured in slide 4.

## Slide 3: Radiated emission and harmonic and flicker - agreements
We will not define 2 sets of EMC requirement for DU and MT, but to define requirements per each enclosure and each port.
For IAB EMC radiated emission requirement,
1, DU and MT in different enclosure:
Radiated emission requirement for IAB with different enclosure, the requirements are the same and they are applied per enclosure.
2, DU and MT in one enclosure:
For TDM IAB-node with only one enclosure, reuse current radiated emission requirement of BS in TS 38.113.
For FDM and SDM IAB-node with only one enclosure, radiated emission should be tested in 3 cases based on declaration.
  3 cases to be tested as:
    DU TX and MT function turned off
    DU function turned off and MT TX
    Both DU and MT TX
  FFS to requirement for each case or only to choose one case to test
  Further analysis is needed to avoid redundancy
3, Similar principle of BS EMC spec for the type 1-O and 2-O BS will be applied to the type 1-O and 2-O TDM IAB-node for radiated emission requirement.
-- the OTA radiated spurious emission definiton for IAB is still under discussion in RF session.
Reuse base station requirement for harmonic current emission and voltage fluctuation and flicker to an IAB-node.

## Slide 4: Issues
Conducted Emission requirement:
Whether to have different requirements for in-door and out-door use:
  Option 1: Define different requirement based on the use environment, the use case can be declared
    Use environment as class A or class B defined in CISPR 32.
  Opiton 2: Define only one set of requiremnt based on BS regulatory requiremnt
  Ohter options not precluded
Radiated Immunity requirement
Testability issue as one link or two links
  Option 1: Test one link each time. This is easy to do so but not the real case of IAB.
  Option 2: Test both links.
    Need to consider different requirements for BS and UE and corresponding links.
  Other options not precluded
Other immunity requirement except for radiated immunity requirement
How to define the test level
  Option 1: Based on regulatory requirement of BS
  Option 2: Define different test level in case of different enclosure for DU and MT based on use environment
  Other options not precluded

## Slide 5: Reference
[1] R4-2001253 further discussion on IAB EMC emission requirement, ZTE
[2] R4-2001254 further discussion on IAB EMC immunity requirement, ZTE
[3] R4-2002369 R4-2002369 summary for RAN4#94e_#78_NR_NewRAT_EMC , Email discussion