## Slide 1: WF on BS demodulation requirements for 2-step RACH
ZTE
3GPP TSG-RAN WG4 #94e Meeting
Electronic Meeting, Feb 24th – Mar 6th 2020
R4-2002389

## Slide 2: Agreements from 1st round discussion
No additional preamble performance requirement for preamble is needed.
Leave performance requirements for interlaced PUSCH design and long preamble to NR-U WID.

## Slide 3: Essential open issues
Application scenarios,
  whether or not to consider only small cell case?
  Whether 2 step RACH is only activated near to the centre of large cells ?
Timing offset (TO) issue:
  Can BS assume the same or different timing offsets among UEs?
  Potential impact on the performance of different TOs

## Slide 4: Application scenarios
RAN1 agreed to support all different preamble formats for 2-step RACH
If the timing offset between different UEs is large in comparison to the CP length, then some taps of the channel impulse response may fall outside of the CP and the msgA PUSCH from those UEs will not be orthogonal in the frequency domain and will not be orthogonal with regular PUSCH
  This may restrict the system capacity

## Slide 5: Agreements
RAN4 should determine relevant application scenarios for MsgA performance evaluation
  Including a request to all companies to contribute parameters needed for analysis, e.g., cell size of the use cases
RAN4 should study if new requirements for MsgA performance should be defined
  FFS on whether the new requirements are functional or performance.

## Slide 6: Reference
R4-2002387 Email discussion summary for RAN4#94e_#96_NR_2step_RACH_Demod, ZTE
R4-2000801 BS demodulation requirements for 2-step RACH, ZTE
R4-2000802 2-step RACH workplan, ZTE
R4-2000314 View on BS demodulation requirement for NR 2-step RACH, Samsung
R4-2001183 On 2 step RACH demodulation, Ericsson
R4-2001491 On 2-step RACH BS demodulation requirements, Nokia

## Slide 7: Background information (not for agreement)

## Slide 8: Timing Offsets (1): 2-step Vs 4-step RACH
Timing adjusted
Timing offset for each UE is estimated, and sent to the UE in Msg2
Lack of timing offsets adjustment
so all UEs preambles are received within one CP at BS side
Timing offsets among UEs are not guaranteed

## Slide 9: Timing offsets (2): examples
Timing offset in the unit of CPs cause by round-trip delay
Fraction of CP due to round trip delay |  |  |  |  |  |  |  | 
Distance/SCS | 20 | 50 | 200 | 500 | 1732 | 25000 | Symbol length | CP length
15 kHz | 0.016344 | 0.04086 | 0.16344 | 0.408599 | 1.415387 | 20.42995 | 71.88 | 4.71
30 kHz | 0.032688 | 0.08172 | 0.326879 | 0.817198 | 2.830773 | 40.85989 | 35.94 | 2.355
60 kHz | 0.065376 | 0.16344 | 0.653758 | 1.634396 | 5.661547 | 81.71978 | 17.97 | 1.1775
120 kHz | 0.130752 | 0.326879 | 1.307517 | 3.268791 | 11.32309 | 163.4396 | 8.99 | 0.58875
To | 0.066667 | 0.166667 | 0.666667 | 1.666667 | 5.773333 | 83.33333 |  | 
TO(us) | 0.07698 | 0.19245 | 0.7698 | 1.924501 | 6.666471 | 96.22504 |  |