## Slide 1: Way forward on PMI reporting requirements for NR eMIMO
Qualcomm
3GPP TSG-RAN4 Meeting #94-e
Electronic Meeting, Feb.24th - Mar.6th 2020
Agenda item: 8.11.3
R4-2002421
Document for: Approval

## Slide 2: Test Cases with Interference
Whether to define the test cases covering CSI-RS interference from neighboring cells and/or sectors
  Option 1: Yes
  Option 2: No

## Slide 3: Test Case Design
Option 1: Similar assumption as that of the test case for Rel-15 Type II Codebook.
Other options not precluded.

## Slide 4: Number of ports and subbands
Number of CSI-RS ports:
  Option 1: 16 ports with (N1,N2) = (4,2) and (O1,O2)=(4,4)
  Option 2 : 32 ports with (N1,N2) = (4,4) and (O1,O2)=(4,4)
  Option 3: 4 ports with (N1,N2) = (2,1) and (O1, O2)=(4,1)
  Other options not precluded
Number of PMI Sub-bands per CQI Sub-band
  Option 1: R = 1
  Option 2: R = 2
Wideband and sub-band PMI
  Option 1: Wideband
  Option 2: Sub-band

## Slide 5: Codebook Parameters and Beam Steering
Codebook parameter configuration
  Option 1: paramCombination-r16: 6, with L =4, pν =1/2, β=1/2
  Other options not precluded
Beam-steering model
  Option 1: Taking beam steering approach as specified in B.2.3B.4A of TS 36.101 as staring point with further extension applicable for L beams
  Other options not precluded

## Slide 6: Propagation Condition
Channel Model
  Option 1: TDLA30-5
  Other options not precluded
MIMO Correlation
  Option 1: XP High
  Option 2: XP Medium
  Other options not precluded

## Slide 7: Other Test Parameters
MCS and Rank
  Option 1: MCS 20 (64QAM Table), Rank 2
  Other options not precluded
Whether to reuse remaining parameters from Rel-15 Type II Codebook requirements
  Option 1: Yes
  Option 2: No

## Slide 8: Test Metric
Option 1: Relative Throughput ratio between following PMI and random PMI
Option 2: Relative Throughput ratio with following PMI between enhanced Type II codebook and Rel-15 Type II codebook
Option 3: Same test metric as in LTE for advanced CSI requirements
Other options not precluded

## Slide 9: Simulation Assumptions
For initial simulations:
  Use the parameters listed in previous slides.
  The remaining parameters will be same as for Rel-15 Type II codebook simulation assumptions in R4-2002394