## Slide 1: Way forward on DL channels mapping and power ratio
Intel Corporation, …
3GPP TSG-RAN WG4 Meeting #94-e
E-meeting, 24 February – 6 March, 2020
Agenda Item: 6.12.1
R4-2002534

## Slide 2: DL channels mapping
      SS-Block mapping to physical antennas
  The SS-Block is mapped to one single physical antenna
      PDCCH mapping to physical antennas
  PDSCH requirements: Use precoding configuration from Rel-15 PDCCH requirements
  SDR requirements: Use precoding configuration from Rel-15 PDCCH requirements
  CSI requirements:
    Option 1: Use precoding configuration from Rel-15 PDCCH requirements
    Option 2: The PDCCH is mapped to one single physical antenna
      PDSCH mapping to physical antennas
  Add references to TS 38.214 to clarify beamforming matrix used for requirements definition
  FFS if additional clarifications are needed

## Slide 3: DL signal power ratios
      Option 1: Modification of existing DL channel signal power ratios configuration is needed
      Option 2: Existing DL channel signal power ratios configuration is correct