## Slide 1: WF on Signaling newly supported NS values
NTT DOCOMO, INC., T-Mobile USA, US Cellular, AT&T, Ericsson
TSG RAN WG4 meeting: 94-e Electronic Meeting R4-2002737
Feb.24th – Mar.6th 2020

## Slide 2: Background
There are proposals to add new NS(s) to existing bands.
Adding new NS(s) generates issues for attach procedure and handover. These issues are elaborated in [2]
For SA,
  attach procedure can be accommodated by NR-NS P-Max list. gNB, however, shall know which NS each of UEs can deal with for handover procedure to convey the information to the destined gNB.
  Note if the UEs do not understand the New NS if the network dose not use NR-NR P-Max list, the UE considers the cell as barred but this does not solve handover issue.
For NSA,
  there are no attach issue since attach is done via LTE. NSA, however, also has the same issue that of SA for handover.

## Slide 3: WF
A feature for a UE to report newly supported NS(s) to a network is introduced.
The feature is specified in the following manner.
  Broadening a definition of “modifiedMPR-Behaviour” in RAN4 specifications in a way that a new bit is defined and listed in a table in Annex H when MPR or A-MPR for the existing NS is modified or a new NS is added to an existing band
  The feature together with conventional “modifiedMPR-Behaviour” for MPR or A-MPR will be specified into at least TS38.101-1 and TS38.101-2.
Example: Introduce a new NS_20X to a Band A from release 16.18.0
  In Rel15 spec, a new row for a new bit map is added to a table where the new NS support is optional.
  In Rel16(v16.18.0) and beyond, a new row for a new bit map is added to a table where the new NS support is mandatory from the version of release.

## Slide 4: Example for 38.101-2
NR Band | Index of field (bit number) | Definition (description of the supported functionality if indicator set to one) | Notes
n258 | 0 (leftmost bit) | - NS_205 as defined in clause 6.x of 38.101-2 v16.y.z | - This bit shall only be set to 1 by a UE supporting Band n258
NR Band | Index of field (bit number) | Definition (description of the supported functionality if indicator set to one) | Notes
n258 | 0 (leftmost bit) | - NS_205 as defined in clause 6.x of 38.101-2 v16.y.z | - This bit can be set to 1 by a UE supporting Band n258
In case a new NS is added to n258 from v16.x.z
Rel16 spec
Rel15 spec

## Slide 5: Reference
[1] R4-2000219: dCR to 38.101-2: Visualizing A-MPR from WRC19 Resolutions, Qualcomm Incorporated
[2] R4-2000220: Necessity of signaling supported NS values, NTT DOCOMO, INC.