## Slide 1: WF on Intra-band non-contiguous DL CA
Qualcomm
R4-2002824
3GPP TSG-RAN WG4 Meeting #94-e
Online Meeting, 24 Feb-6 Mar 2019
Agenda: 8.14.1.4
Email Thread: #22

## Slide 2: Background
Rel-16 DL CA BW enhancement feature is definition of DL-only frequency coverage spectrum
In a previous WF (R4-1916021) DL-only spectrum was narrowed-down to two configurations:
  The spectrum covered by the DL-only frequency separation shall be located relative to bidirectional spectrum(*) in one of two configurations:
    Extends on one side
    Extends equally on both sides, half on each side
      FFS if both-sided DL-only spectrum can be dropped for rel-16.
      Single bit can be used to indicate configuration if both possibilities retained
(*) Bidirectional spectrum is spectrum covered by DL frequency separation

## Slide 3: WF on intra-band non-contiguous DL CA
The DL-only spectrum shall be located relative to the bidirectional spectrum(*) in one of two configurations:
  Extends to one side
  Extends equally on both sides, half on each side
A single bit shall be used to indicate configuration supported by UE
There is no restriction on UE architecture to implement DL-only spectrum
(*) Bidirectional spectrum is spectrum covered by DL frequency separation