## Slide 1: WF on FR2 ACLR MBW
Skyworks Solutions Inc., ….
R4-2002827
3GPP TSG-RAN WG4 Meeting #94-e
Online, 24th February – 6th March, 2020

## Slide 2: Background on FR2 ACLR MBW issue
Reference: R4-2002144 "FR2 ACLR Measurement Bandwidth Definition“ Skyworks Solutions Inc. The following issue related to position of ACLR MBW are discussed:
  Current specification uses a MBW equal to Transmission Bandwidth Configuration but centered on the wanted and adjacent channels
  This does not account for the half SCS Shift and thus results in the transmission signal not being fully captured in the ACLR measurement BW for all cases.

## Slide 3: Background on FR2 ACLR MBW issue
Two solutions were proposed:
  Option 1: modify FR2 MBW according to FR1 method where MBW is increased by 1 SCS and stays centered on the channels
  Option 2: maintain existing FR2 MBW, and change the text defining the center frequency of the measurement BW for the wanted channel so that MBW becomes centered on the Transmission Bandwidth Configuration.

## Slide 4: WF on FR2 ACLR MBW issue
In order to minimize the impact on the specification the following is proposed:
  If no impact on existing regulatory is confirmed, use option 2 from R4-2002144:
    Keep ACLR measurement bandwidth as is
    Change the ACLR measurement bandwidth from centered on the channel to centered on the Transmission Bandwidth Configuration for the wanted signal and measurement bandwidth offset for adjacent channels stay at +/- channel BW
  Bring CR in April meeting to change the text in 38.101-2 Table 6.5.2.3-1 accordingly
    For both release 15 and release 16