## Slide 1: WF on NR Inter-RAT EMR requirements
Nokia, Nokia Shanghai Bell
3GPP TSG-RAN4 Meeting #94e
E-meeting, February 24th – March 6th, 2020
R4-2002235
Document for: Approval

## Slide 2: Background
During the RAN4#94e E-meeting the dicussion related to Multi-RAT Dual-Connectivity and Carrier Aggregation enhancements [LTE_NR_DC_CA_enh] continued.
Summary of the round 1 discussion is captured in R4-2002177.
Based on this summary and round 2 discussions (R4-200xxxx) some agreements were reached which are captured in this WF
Additinal a number of open issue for further discussion were lited. Also those are listed in this WF.

## Slide 3: Agreements
UE requirements scenarios:
  RAN4 to continue the discussion related to UE requirements for supporting NR Inter-RAT measurements for EMR. Later RAN4 can, if needed, return to the capability discussion.
  RAN4 defines the LTE NR Inter-RAT measurements requirements for EMR regardless of the capability, which will be discussed separately

## Slide 4: Agreements
number of LTE EMR carriers to support:
  At least agree that the total number of carriers for EMR and mobility should not exceed the corresponding Rel-15 capability
  RAN4 discussion to continue to decide the actual number.
Number of NR inter-RAT carriers:
  At least agree that the total number of carriers for EMR and mobility should not exceed the corresponding Rel-15 capability.
  RAN4 discussion to continue to decide the actual number.

## Slide 5: Agreements
Cell detected status at transitioning from connected mode
  Adopt the LTE concept:
    An NR inter-RAT cell which is a detected cell in Connected mode prior to connection release, shall remain detected after UE has entered Idle/Inactive mode
  Open: conditions when the detected cell status remain detected during transitioning from connected to idle or inactive mode.

## Slide 6: Way Forward
Measurement requirements for NR Inter-RAT EMR carrier
  RAN4 will discuss and if needed define requirements for an NR Inter-RAT EMR carrier:
    UE performs periodic cell detection and measurement for LTE – NR inter-RAT EMR measurement
    UE measurement requirements
Companies are encouraged to bring discussion papers and views at least on the topics addressed in this WF for the coming meeting to progress the work.