## Slide 1: 3GPP TSG-RAN WG4 Meeting #93 Reno, USA, November 18 -22, 2019
Ericsson, Huawei, HiSilicon
WF on Rel-16 MTC RRM Requirements
R4-2002268

## Slide 2: Preconfigured UL resource
No technical open issues are remaining for PUR feature.
RAN4 is discussing how to capture the agreements that were made in previous RAN4 meetings. The agreements can be found in following agreed way forwards:
  R4-1907733, “Way forward on Rel-16 MTC RRM enhancement”, May 2019
  R4-1910107, “Way forward on Rel-16 MTC RRM enhancement“, August 2019
  R4-1912735, “Way forward on Rel-16 MTC RRM enhancement”, October 2019
  R4-1915889, “Way forward on Rel-16 MTC RRM enhancement”, November 2019

## Slide 3: Mobility enhancement: RSS based RSRP measurement for UEs
RAN4 to define RSS based RSRP measurements in IDLE and CONNECTED mode for serving cells and neighbor cells under certain conditions regarding location of RSS resources in the cell bandwidth.
  The conditions are to be discussed at next meeting.
  RAN4 is to discuss the measurement delay requirements for RSS based RSRP measurements at next meeting.
  RAN4 agrees to use the same RF margin that was used for deriving the CRS based RSRP measurement accuracy requirements for cat-M.

## Slide 4: MPDCCH performance improvement for RLM
The SNR test points at which RLM based on improved MPDCCH is open.
Following options on SNR test points are under consideration
  Option 1: RAN4 does not consider defining new RLM test cases based on R16 MPDCCH performance improvement in SNR points above -10 dB or in fading channel conditions.
  Option 2: RAN4 to discuss the possibility of adding new RLM test cases based on R16 MPDCCH performance improvement in SNR points below -10 dB and AWGN channel.
  Option 3: When the network configures the enhanced RLM (rlm-ReportConfig) and improved MPDCCH (mpdcch-crs-connected-config), UE applies the improved MPDCCH transmission parameters for evaluating the out-of-synch when UE reports the Event E1 to the network. This is applicable for both CE Mode A UE and CE Mode B UE.
To reach consensus, companies are encouraged to provide simulation results based on agreed simulation assumptions (ref. R4-1914343).

## Slide 5: DL quality reporting
Separate accuracy requirements for fixed AL24 and fixed RL=1
  Set -15 ≤ Es/Iot ≤ [-3] dB as the side condition to report the repetition level with the fixed AL=24.
  Set Es/Iot ≥ [-3] dB as the side condition to report the aggregation level with the fixed RL=1.
Use static channel for test case as same as Rel-14 NB-IoT channel quality reporting.

## Slide 6: DL quality reporting
Following 8-bit reporting table is agreed:
RAN4 waits for RAN2 conclusion on 2-bit reporting table.
Reported level | MPDCCH repetition level | MPDCCH aggregation level | CE mode
0 | No measurement reporting | No measurement reporting | A, B
1 | 1 | 1 | A
2 | 1 | 2 | A
3 | 1 | 4 | A
4 | 1 | 8 | A
5 | 1 | 16 | A
6 | 1 | 24 | A, B
7 | 2 | 24 | A, B
8 | 4 | 24 | A, B
9 | 8 | 24 | A, B
10 | 16 | 24 | A, B
11 | 32 | 24 | A, B
12 | 64 | 24 | A, B
13 | 128 | 24 | A, B
14 | 256 | 24 | A, B

## Slide 7: Performance requirements
Feature | Test case
WUS | RAN4 agrees to not specify any performance tests for group WUS.
PUR | More discussions needed
Improved MPDCCH | More discussions needed
RSS | More discussions needed
DL quality reporting | RAN4 agrees to introduce test case for DL quality reporting in IDLE and CONNECTED mode. Test configurations are to be discussed further at next meeting.