## Slide 1: Way forward on PMI reporting requirements for Tx ports larger than 8 and up to 32
Ericsson, Samsung
3GPP TSG-RAN4 Meeting #94e
Electronic Meeting February 24 – March 6 , 2020
Agenda item: 8.18.1.2
R4-2002393
Document for: Approval

## Slide 2: Timeline of previous agreements
#92
  WF: R4-1910017
#92bis
  WF: R4-1912834
  simulation assumptions: R4-1912811
#93
  WF: R4-1915858
  Simulation assumptions: R4-1915859

## Slide 3: PMI tests for single panel type I requirements
Wideband PMI requirements
  32Tx ports
Subband PMI requirements for 16 Tx ports
  Option 1: Introduce subband PMI requirements for 16 Tx ports
  Option 2: Not introduce subband PMI requirements for 16 Tx ports (Set 16Tx port requirements with Wideband PMI)

## Slide 4: 16Tx ports requirements for Single panel type I
Duplex mode:
  FDD 10MHz/15kHz BW/SCS
  TDD 40MHz/30kHz BW/SCS
Number of Rx antennas:
  2Rx, and 4Rx
Subband size (if applicable)
  FDD: 8
  TDD: 16

## Slide 5: NZP-CSI-RS configuration for Single panel type I
16Tx ports:
  (k0, k1, k2, k3) = (2, 4, 6, 8), l0 = (5)
32Tx ports:
  (k0, k1, k2, k3) = (2, 4, 6, 8), (l0, l1) = (5, 12)

## Slide 6: Single Panel Type I results
Further alignment needed given current divergency amonst companies’ results.
Detailed simulation assumptions found in tdoc R4-2002394

## Slide 7: Codebook construction for Type II
Option 1: 16Tx ports (N1,N2) = (4,2), (O1, O2) = (4,4)
Option 2: 32Tx ports (N1,N2) = (4,4), (O1, O2) = (4,4)
Option 3: Option 1, and Option 2
Other options not precluded

## Slide 8: Channel model for type II codebook
Option 1: TDLA30-5
Use option 1 as baseline, and not preclude other options

## Slide 9: L, Npsk, and subband amplitude configurations for Type II Codebook
L (numberOfBeams):
  Option 1: 2
  Other options are not precluded
Npsk (phaseAlphabetSize):
  Option 1: 4
  Option 2: 8
subbandAmplitude:
  Option 1: False
  Option 2: True
  Keep open until the next meeting

## Slide 10: MCS and rank for Type II Codebook
Option 1: MCS20 (64QAM ½), Rank2
Other options are not precluded

## Slide 11: MIMO correlation for Type II Codebook
Option 1: XP High
Option 2: XP Medium
Other options are not precluded

## Slide 12: Beam steering model for type II codebook
Option 1: Reusing beam steering approach with dual-cluster beams as as specified in B.2.3B.4A of TS 36.101
  Relative power ratio among two beams can be fixed as 1 (p =1)
  Use option 1 as baseline, and not preclude modification/other option for coming meetings.
Other options not precluded

## Slide 13: Test metric for type II codebook
Option 1: TP ratio between following PMI with Type II codebook and following PMI with Type-I single panel codebook
Option 2: TP ratio between following PMI and rand PMI
Other options are not precluded