## Slide 1: 3GPP TSG-RAN WG4 Meeting #94-e R4-2002429 Electronic Meeting, Feb.24th – Mar.6th 2020
Huawei, HiSilicon
Way forward on NR URLLC BS performance requirements

## Slide 2: BS demodulation requirements for high reliability
BS FR1 URLLC PUSCH demodulation requirement for high reliability with higher BLER:
    Target BLER : 1%
    Target confidence level: 99%
    Calculate the target BLER after all transmission if HARQ activated.
    Number of HARQ transmission: 4
    MCS: MCS 5 in table 3
    Waveform: CP-OFDM
    TDD pattern:
      15kHz SCS: 3D1S1U, S=10D: 2G: 2U
      30kHz SCS: 7D1S2U, S=6D: 4G: 4U
    Symbol length is 14 with starting symbol 0
    DM-RS configuration: Type 1 with single-symbol: 1+1
    Antenna configuration: 1x2, low
    Propagation condition: TDLB100-400
    Mapping Type: Type A and B with test applicability rule defined.
    SCS&BW for FR 1
      10MHz/15kHz
      40MHz/30kHz
      Other sets are not precluded

## Slide 3: BS demodulation requirements for high reliability
BS FR1 URLLC PUSCH demodulation requirement for high reliability with higher BLER:
    Issue 1: PUSCH aggregation level
      Option 1: 2
      Option 2: 4
      Option 3: 2, 4
      Option 3: 8
    Issue 2: Number of PRBs
      Option 1: 25
      Option 2: Full bandwidth
      Option 3: Other options not precluded (depending on bandwidth set)
    Issue 3: Whether to introduce DFT-s-OFDM:
      Option 1: No
      Option 2: Yes

## Slide 4: BS demodulation requirements for high reliability
BS FR1 URLLC PUSCH demodulation requirement for high reliability with higher BLER and/or confidence level:
    Issue 4: Safety critical aspects:
    Proposals
    Proposal 11: If high reliability will be tested with BLER metric, add the following note to the test specification: “Note that this test procedure will only provide an indication to a certain confidence level that the target reliability requirements are likely to be satisfied, and it is assumed that for critical applications further testing would be done to ensure suitability of the equipment for the intended application.” (Nokia)
      Since the URLLC features of 5G NR will potentially be used in safety critical applications, the ultimately chosen statistical testing methodology for testing of these features must be verified by an independent body of experts/statisticians, before requirements and test can be used as basis for safety critical implementations. All statistical analysis and discussions provided in this meeting are to be taken as a best effort and is not to be taken as due diligence. (Nokia)
    Option 1: Need to be clarified in 3GPP specification.
    Option 2: No need to be clarified in 3GPP specification.

## Slide 5: BS demodulation requirements for high reliability
BS FR2 URLLC PUSCH demodulation requirement for high reliability with higher BLER:
    Issue 1: Whether to define BS FR2 URLLC performance requirements for high reliability
    Proposals
      Option 1: Do not define
      Option 2: Define.
    Issue 2: Test applicability rule for FR1 and FR2 performance requirements if both requirements are defined
    Proposals
      Option 1: Based on BS declaration of support FR1 or FR2
      Option 2: If BS supports both FR1 and FR2, the performance requirements for both FR1 and FR2 should be tested
    Issue 3: SCS&BW for FR2 if FR2 will be defined
      60kHz SCS
        Option 1: 50/100MHz
        Option 2: No test
        Option 3: 50 MHz
      120kHz SCS
        Option 1: 50/100/200MHz
        Option 2: No test
        Option 3: 100 MHz

## Slide 6: BS demodulation requirements for low latency
BS FR1 URLLC demodulation requirements for PUSCH mapping Type B
    Starting symbol: 0
    PUSCH aggregation level is 1.
    TDD pattern:
      15kHz SCS: 3D1S1U, S=10D: 2G: 2U
      30kHz SCS: 7D1S2U, S=6D: 4G: 4U
    Antenna configuration: 1x2, low
    Waveform: CP-OFDM
    Channel condition: TDLC300-100 Low for FR1.
    No PUSCH performance requirements for UL transmission with grant free/UL configured grant.
    Number of HARQ transmission: 1
    SCS/BW:
      15 kHz/10 MHz and 30 kHz/40 MHz with defined test applicability rule
      Other sets are not precluded

## Slide 7: BS demodulation requirements for low latency
BS URLLC demodulation requirements for PUSCH mapping Type B
    Issue 1: Whether to define requirements for BS FR2 URLLC performance requirements for low latency
      Option 1: Do not define
      Option 2: Define
    Issue 2: Symbol length (L)
      Option 1: 4os
      Option 2: 2os
      Option 4: 7os
      Option 5: 2os and 7os
    Issue 3: DM-RS configuration Type 1 with single symbol
    Proposals for symbol lengths of 7os if agreed
      Option 1:1+0
      Option 2: 1+1

## Slide 8: BS demodulation requirements for low latency
BS FR1 URLLC demodulation requirements for PUSCH mapping Type B
    Issue 4: MCS
      Option 1: MCS 5 from Table 3
      Option 2: MCS 21 (658/1024) from Table 2
    Issue 5: Number of PRB
      Option 1: full bandwidth
      Option 2: A fixed number of RB
    Issue 6: Test metrics
      Option 1: 70% throughput
      Option 2: 10% BLER (= 90% throughput)
    Issue 7: Whether to introduce DFT-s-OFDM:
      Option 1: No
      Option 2: Yes

## Slide 9: BS demodulation requirements for high reliability
Define the PUCCH performance requirements for high reliability
  Do not define the PUCCH performance requirements for high reliability.