## Slide 1: WF on IAB-MT ACLR and minimum Tx power in FR2
Nokia, Nokia Shanghai Bell
R4-2002492
3GPP TSG-RAN WG4 Meeting #94-e
Electronic Meeting, Feb.24th – Mar.6th 2020

## Slide 2: Contributions in RAN4#94-e
R4-2000973, ZTE
R4-2001432, Nokia, Nokia Shanghai Bell
R4-2001280, Qualcomm Incorporated
R4-2001865, Ericsson

## Slide 3: Background
Tentative agreement in discussion #82 of RAN4#94-e to define two classes for IAB-MT, out of which at least one is for macro/planned/high power deployments
Coexistence simulation results have been performed for two different layouts, one addressing HetNet deployment and other reflecting macro/planned/high power deployment
Coexistence results differ between the layouts. The trend is that more relaxed ACLR and dynamic range guarantee co-existence in the macro/planned/high power deployment, while there has been no agreement the exact required values
Occupied bandwidth limit of 99% sets implicitly approximately 23 dBc ACLR requirement, corresponding to 0.5% of power at adjacent channel

## Slide 4: Way forward
IAB-MT ACLR minimum requirement in FR2 is 24 dBc
  For Wide area IAB MT class:
    Option 1: reuse BS ACLR
    Option 2: 24 dBC
  For [Local area] IAB MT class: 24 dBc
IAB-MT minimum Tx power in FR2 is class dependent
  For Wide area IAB MT class:
    Option 1:Derived from Tx dyanmic range and declared max Tx power
    Option 2:25 dBm for macro/planned/high power deployment based class
  For [Local area] IAB MT class:
    25 dBm for macro/planned/high power deployment based class
    13 dBm for small cell / unplanned / low power deployment
  Power levels are specified as TRP
Minimum power requirement means that IAB-MT shall be able to transmit the widest declared channel BW with maximum possible number of RBs allocated for the said channel at the specified or lower power output power.