## Slide 1: WF on IAB-MT Beam Correspondence
Qualcomm Incorporated
R4-2002503
3GPP TSG-RAN WG4 Meeting #94-e
Electronic Meeting, Feb.24th – Mar.6th 2020

## Slide 2: Background
In RAN4#94 the following was agreed:
  Ability of MT to pick the right UL direction based on the DL signal arrival direction is mandatory (decision on the RF requirement is still FFS)
  Requirement definition for above MT ability to be decided next meeting
    Options:
      1. MT declares UL EIRP range in different directions, MT picks UL beam based on received DL signals(reference signal) and has to meet EIRP in the direction it received from with TBD accuracy relative to declared EIRP capability in that direction
        Functionality to be tested:
        1. MT detects best DL beam with some accuracy
        2. MT applies detected direction to the UL Tx beam
        3. MT needs to transmit UL beam in the direction applied form step 2.
        Accuracy would have to be derived based on combined accuracy/error from all 3 steps
      2. MT declares UL EIRP and EIS range in different directions, functionality that MT can pick the right UL direction based on DL signals is assumed to be implicit if MT meets UL EIRP and EIS in the declared directions

## Slide 3: Way Forward
No explicit requirement will be defined for the IAB-MT beam correspondence
FFS on need for conformance testing of IAB-MT Beam Correspondence