## Slide 1: WF on new intra-band CA BW classes for NR-U
Ericsson
R4-2002748
3GPP TSG-RAN WG4 Meeting #94-e
Electronic meeting, 24 February – 6 March 2020

## Slide 2: Background
According to the WID [1], wideband operations in multiples of 20 MHz should be supported by both multiple serving cells (i.e. CA of 20 MHz cells) and one serving cell with bandwidth > 20 MHz with potential scheduling constraint (i.e. “wideband carrier”). The RAN1 objectives in the WID state
  “Physical layer aspects including [RAN1]:
  […]
  Wide band operation (in integer multiples of 20MHz) for DL and UL for NR-U supported with multiple serving cells, and wideband operation (in integer multiples of 20MHz) for DL and UL for NR-U supported with one serving cell with bandwidth > 20MHz with potential scheduling constraint subject to input from RAN2 and RAN4 on feasibility of operating the wideband carrier when LBT is unsuccessful in one or more LBT subbands within the wideband carrier. For all wide-band operation cases, CCA is performed in units of 20MHz (at least for 5GHz).”
RAN4 should therefore specify NR CA BW classes supporting both modes of wide band operation in multiples of 20 MHz
Wide band operation (in integer multiples of 20MHz) for DL and UL for NR-U supported with multiple serving cells not possible with current CA BW Classes
1. RP-191575

## Slide 3: Way forward
Define three new NR CA bandwidth classes to allow intra-band contiguous CA in Band n46 in multiples of 20 MHz and wider bandwidths
  class “M”: 50 MHz ≤ BWChannel_CA ≤ [240] MHz (3 CC)
    The lower limit also covers one 10 MHz channel bandwidth (10 + 20 + 20 MHz to cover 50 MHz allocation)
  class “N”: 80 MHz ≤ BWChannel_CA ≤ [320] MHz (4 CC)
  class “O”: 100 MHz ≤ BWChannel_CA ≤ [400] MHz (5 CC)
belonging to the same fall-back group
The upper limits tentative (n * 80 MHz)
  recognising that these tentative values are not possible in n46 but may allow reuse of the BW classes above 5925 MHz
BCS can be defined with restrictions on the total aggregated bandwidth for each class
2 CC covered by the existing CA BW classes B and C
The classes M, N and O only applies to Band n46 operation
Note: agreed assumptions on number of CCs for DL/UL and scope (e.g. two contiguous CCs in the UL) for Rel-16 remains (RAN4#92bis)