## Slide 1: WF on UE receiver requirements for NR-U
Ericsson
R4-2002756
3GPP TSG-RAN WG4 Meeting #94-e
Electronic meeting, 24 February – 6 March 2020

## Slide 2: Background
According to the WID [1], wideband operations in multiples of 20 MHz should be supported by both multiple serving cells (i.e. CA of 20 MHz cells) and one serving cell with bandwidth > 20 MHz with potential scheduling constraint (i.e. “wideband carrier”). The RAN1 objectives in the WID state
  “Physical layer aspects including [RAN1]:
  […]
  Wide band operation (in integer multiples of 20MHz) for DL and UL for NR-U supported with multiple serving cells, and wideband operation (in integer multiples of 20MHz) for DL and UL for NR-U supported with one serving cell with bandwidth > 20MHz with potential scheduling constraint subject to input from RAN2 and RAN4 on feasibility of operating the wideband carrier when LBT is unsuccessful in one or more LBT subbands within the wideband carrier. For all wide-band operation cases, CCA is performed in units of 20MHz (at least for 5GHz).”
Requirements for receiver characteristics to be specified for both wideband modes with assumptions on number of CCs for DL/UL and scope (e.g. two contiguous CCs in the UL when applicable) according to Rel-16 agreement (RAN4#92bis)

## Slide 3: WF REFSENS
The requirement specified for full downlink allocation, all LBT sub-bands allocated, all channel bandwidths ≥ 20 MHz (10 MHz in CA only)
For wideband, all intra-cell guard bands between sub-bands should be filled if the UE is capable of scheduling within these guard bands
  FFS if the UE is not capable of scheduling within the intra-cell GB, then the guard-band RB should not be allocated for reference sensitivity
  one single requirement may be feasible nevertheless
Define an exclusion region rather than MSD value for harmonic interference when the degradation occurs in Band n46
For harmonic mixing interference into the downlink of a licensed band due to transmission from the NR-U band, (tentatively) no licensed band REFSENS requirement applies in this condition as a general rule (to be confirmed)

## Slide 4: WF Adjacent channel selectivity
ACS and blocking requirements apply under static/semi-static conditions of configuration and scheduling only
Two test configurations considered (ACS and in-band blocking)
ACS requirement FFS
  Proposals range from ACS = 14 dB to 25-30 dB (20 MHz wanted and ACI bandwidths)
CHBW
CHBW
20 MHz
CHBW
-56 dBm/CHBW
-44 dBm/CHBW
ACS
ACS
-56 dBm/20 MHz
-44 dBm/20 MHz
(Could be used for both intra-band CA and wideband)

## Slide 5: WF In-band and out-of-band blocking
The NR requirements are leveraged for NR-U.
The out-of-band blocking requirements for CA/EN-DC apply to CA/EN-DC configurations, not the individual constituent bands (same as for LAA). Each downlink is measured in turn, and the interferer power profile is the same for all bands. The following interferer profile for LAA (no blocker in own licensed downlink) is FFS

## Slide 6: Some other topics for consideration
Maximum input level
Specification of in-channel selectivity for wideband
Wideband intermodulation