## Slide 1: WF on method and assumptions in determining NR-U MPR and A-MPR in Band n46
Skyworks Solutions Inc., [Charter], [Ericsson], [LGE], [Nokia], [Qualcomm], ….
R4-2002757
3GPP TSG-RAN WG4 Meeting #94-e
Online, 24th February – 6th March, 2020

## Slide 2: Background: Status on NRU MPR evaluation in RAN4#94-e
In R4-2002094 [2] and R4-2000708 [3] PA EVM budget is discussed
In R4-2000708 [3] and R4-2000709 [4] procedure on how to apply NR-U masks in dBR is discussed for both single carrier and wideband operation
This way forward makes proposals for the following aspects:
  Procedure on how to evaluate the NRU mask failure,
  MPR evaluation assumptions for PA EVM and related Image Leakage budget.
Modulation | Total transmitter (%) | Partitioned to PA (%)
QPSK | 17.5 | 8
16QAM | 12.5 | 7.5
64QAM | 8 | 4
256QAM | 3.5 | 1.5
R4-2002094
R4-2000708
After showing EVM vs Pout and discussing PA vs rest EVM budget makes proposal:
Proposal on PA EVM target: PA EVM budget for PC5 is 12%

## Slide 3: Background: NRU mask test procedure and 0dBR Peak Reference level
Figure below shows a measurement example performed on a spectrum analyzer using 802.11ax test procedure for the case of an 80MHz NRU single carrier mask,
Total Channel Power Measurement BandWidth (MBW) = total Channel Bandwidth, example below = 80MHz.
0dBR Peak Reference level: Peak power integrated in 1MHz MBW, Carrier Leakage excluded,
Averaging: x20 sweeps, VBW=7.5kHz
80MHz Single Carrier (CP-OFDM) example:
RBW 100kHz and VBW 7.5kHz
Blue: in band 0dBR peak reference level in 1MHz. Example here Peak Ref = -4.73dBm
Purple: NRU mask applied as agreed versus 0dBR level. Integration BW = 100kHz, See limits in table
Green: Total power MBW = Channel BW = 80MHz
Red: mask failed by 0.17dB (at limit) in the -80MHz to -120MHz offset region.

## Slide 4: WF on Single Carrier, CA and Wideband Operation NRU Masks
NRU Mask Measurement / Simulation procedure.
Applicable to both Single Carrier and Wideband Operation:
  Resolution Bandwidth: 100kHz.
  In-band total power measurement BW equal to the channel bandwidth for single carrier as agreed,
  0dBR peak Reference level: in band-peak integrated in 1MHz BW, Carrier Leakage excluded,
  NRU Mask limits: Applied as agreed from the 0dBR peak Reference Level,
  Averaging: Recommended x10 sweep trace averaging and Video Bandwidth 7.5kHz, other values not precluded,
Note: this procedure enables carrier leakage exception to be within 200kHz in this measurement.

## Slide 5: WF on NRU MPR Evaluation Assumptions
PA EVM and Image Leakage Budget – see table.
ACLR: 27dB for PC5, 30dB for PC3, reported regardless of the requirement being agreed or not,
AMPR for n46 NS requirements (at least for QPSK)
Post PA losses and part to part variations
  4dB post PA losses is assumed
  Part to part variations may be allocated into additional post PA losses and/or power class tolerances
Waveforms:
  Reference for back-off reporting: DFT-s-OFDM QPSK 100RB0,
    Reporting of negative back-off is allowed,
    MPR value and limiting factor must be reported including,
  Tested waveforms: companies are encouraged to evaluate as many as possible,
    Fully allocated waveforms and 1RB Interlace waveforms (at RB position 0)
    20, 40, 80MHz single carrier
    For 80MHz wideband operation, 0100, 1100, 1110 scheduled bandwidth parts
It has to be noted that if PA is measured with a waveform including the image leakage, its contribution should be removed from the PA results
for interlaces, some cases do not have image overlap and may be used
Modulation | specification [% rms EVM] | PA | Rest | Image [dB] | Image [%] | rest -image | 
QPSK | 17.5 | 12.0 | 12.7 | 28 | 4.0 | 12.1 | 
16QAM | 12.5 | 8.0 | 9.6 | 28 | 4.0 | 8.7 | 
64QAM | 8 | 4.0 | 6.9 | 28 | 4.0 | 5.7 | 
256QAM | 3.5 | 1.8 | 3.0 | 34 | 2.0 | 2.2 | 

## Slide 6: Annex
Background: EVM budget
Background: NRU masks test procedure

## Slide 7: Background on EVM budget
Starting from the budget used in LTE, one can further take into account the further NR improvements and see what can be allocated to PA:
  Image leakage at 28 dBc for NR instead of 25 dBc in LTE and UE default capability is 64QAM for NR
  Table 1 shows the LTE budget (equal split till 64QAM then more stringent requirement on PA for 256QAM which is justified as MPR can improves PA contribution)
  Table 2 shows improvement of the rest of the UE excluding PA from better image leakage
  Table 3 shows range of PA EVM depending on the capability of the rest of the UE (yellow highlight)
  From table 3 it can be observed that for QPSK PA budget could be between 12.4 to 16.5% depending on how the improved UE baseline performance is allocated to the PA
  It seems reasonable to allocate some part back to the PA to avoid that NRU PC5 power capability is limited by EVM
  It has to be noted that if a PA is measured with a waveform including the image leakage, its contribution should be removed from the PA results, for interlaces, some cases do not have image overlap

## Slide 8: Background on dBR NRU masks test procedure
Compared to the masks used in 3GPP the agreed NRU mask is similar to 802.11ac or 802.11ax masks:
  It is relative (dBR) to the in-band signal instead of absolute
    (covers SEM and ACLR in some ways)
  It is not “square” thus shifting measurement point by ½ MBW is not adequate
  Main difference is that 0dBR in-band range is full channel bandwidth compared to 802.11 masks that are restricted to the respective transmission bandwidths
For 802.11ax the mask, which has SCS closer to NRU, is measured using:
  100kHz resolution bandwidth and 7.5kHz video bandwidth
  Mask applied as defined in [1] in dBR referred to the in band peak measured with 1MHz integration bandwidth within the in-band bandwidth
    Channel bandwidth for single carrier NRU
    Active sub-band bandwidth for wideband operation
    Aggregated bandwidth for contiguous CA

## Slide 9: References
[1] R4-1915979 WF on NR-U spectrum emission mask, Nokia, CableLabs, Charter, RAN4#93
[2] R4-2002094 NR-U MPR for PC5 single carrier, Qualcomm Incorporated
[3] R4-2000708 [NRU] Single Carrier Back-off measurements for UE power class and MPR, Skyworks Solutions Inc.
[4] R4-2000709 [NRU] Wideband Operation Back-off Measurements for UE, Skyworks Solutions Inc.