## Slide 1: WF on MPR on S-SSB simulation assumptions and parameters
Agenda item: 8.4.4.1
Source: CATT,…
3GPP TSG-RAN WG4 Meeting #94-e R4-2002759
Electronic Meeting, Feb.24th – Mar.6th 2020

## Slide 2: Background
In last RAN4#93 meetings and e-mail discussion, RAN4 discussed the general MPR simulation assumptions for NR V2X.
In RAN4#94e meeting, companies provide simulation evaluations to specify MPR requirements for S-SSB transmission but without aligned simulation assumptions.

## Slide 3: MPR for S-SSB transmission
During RAN4#94e meeting, MPR for S-SSB as a sub-topic was discussed in the 1st round. Two options are derived to specify MPR for S-SSB transmission.
Option1: Follow LTE V2X MPR for SSSS and follow NR Uu MPR for PSBCH and PSSS.
Option2: RAN4 need MPR evaluation campaign for S-SSB transmission
Above two options will be further discussed in the 2nd round.

## Slide 4: Way Forward
Companies are encouraged to provide comments for the following issues in the 2nd round discussion based on summary of 1st round e-meeting:
  Whether LTE V2X or NR Uu requirements can be used for NR V2X S-SSB
RAN4 need to align the simulation assumptions for S-SSB transmission if not. The same or different MPR requirements for S-PSS, S-SSS and PSBCH will be determined by simulation results.
FFS: whether MPR requirements for S-PSS, S-SSS and PSBCH is same or different

## Slide 5: MPR/AMPR Assumption of S-SSB
parameter | Assumption
Bandwidth | 10/20/30/40MHz
numerology | 15 kHz/30kHz/60kHz
Modulation for PSBCH | QPSK
S-PSS | M-sequence
S-SSS | Golden-sequence
Waveform | CP-OFDM
Carrier leakage | 25dBc
IQ image | 25dBc
CIM3 | 45 or 60 dBc
RB allocation | RBstart: All the possible cases LCRB: 11 RB
S-PSS, S-SSS and PSBCH Power configuration | Option 1: Same power per RE Option 2: Same total transmit power Based on RAN1’s agreement
S-SSB structure | 

## Slide 6: Reference
R4-2001215, Summary on E-mail discussion for NR V2X, LG Electronics
R4-2001085, [V2X] TP on S-SSB MPR requirements for NR V2X in band n47, Huawei, HiSilicon
R4-2002685, Email discussion summary for RAN4#94e_#11_5G_V2X_NRSL_UE_TX, LG Electronics