## Slide 1: WF on A-MPR simulation assumptions when adding CBW to band n65
Ericsson
3GPP TSG-RAN WG4 Meeting #94-e-bis R4-2005186
Electronic meeting, April 20-30, 2020

## Slide 2: Background
Contributions and discussion on:
  A-MPR simulations results [1], [2] and [3].
  Measurements [4] which confirm:
    B34 protection: needs power back-off of ~19dB (fc=1980MHz).
    B3 protection: no power back-off (fc=1945) and 37dB rejection filter.

## Slide 3: A-MPR
New NS will be specified to protect:
  Band 34
  Band 33 and remove RB restrictions in coex. table (Note 27 in Table 6.5.3.2-1).
NS_24 is not updated with 50MHz CBW.

## Slide 4: A-MPR simulation
Simulation assumptions:
  CIM3: -60 dBc.
  IQ image: -28 dB.
  LO leakage: -28 dBc.
  PA calibration point is 20 MHz, 15 kHz, QPSK, DFT-S-OFDM, 100 RB at lower channel edge with 1 dB MPR
  Filter rejection for band 34 Rx: 0dB.
  Filter rejection for band 3 Rx: 37dB.
  50 MHz Channel bandwidth located:
    Band 34 protection:
      Fc at 1980 MHz.
      Fc at 1975 MHz, this would consider 5+5 MHz offset from band edge, similar to what has been done for 20 MHz.
    Band 33 protection: Fc at 1945 MHz.

## Slide 5: A-MPR simulation
Considering the expected back-off values, an optimum PA bias current should be considered:
  This might not be taken into account in the A-MPR simulations.
  Actual measurements would be major input to correct simulation results.

## Slide 6: Reference
R4-2000089, n65 50MHz AMPR, Qualcomm
R4-2004126, Band n65 – wider CBW – UE RF requirements – A-MPR simulation results, Ericsson
R4-2004693, A-MPR Proposal for n65, Apple
R4-2004817, Back-off Measurements for 50MHz QPSK waveforms, Skyworks
R4-2004817, Email discussion summary for [RAN4#94-e-bis][28]_NR_BW