## Slide 1: WF on FR2 Pcmax correction for CA
Qualcomm,
R4-2005212
3GPP TSG-RAN WG4 Meeting #94Bis-e
Online, , 20th - 30th April 2020

## Slide 2: Background
Text in 6.2A.4 is not aligned with ran1 since it says:
  A UE configured with carrier aggregation can configure its maximum output power for each uplink carrier f of activated serving cell c and its total configured output power PCMAX
  The total configured power PCMAX in a transmission occasion is the sum of the configured power for carrier f of serving cell c with non-zero granted transmission power in the respective reference point
What is seen confusing is the statement that PCMAX would be total configured power
This implies recalculation of PCMAX Based on actual configured power after scaling (TS 38.213 section 7.5)
In addition, somehow maximum configured power includes f which means each carrier for each cell. In FR2 there is only one carrier per cell.

## Slide 3: Way forward
Agreements
  PCMAX = Maximum limit of configured power
  PCMAX = Calculated based on grant, in CA case based on all grants that result into simultaneous transmission within evaluation period
  PUMAX = The total measured configured power
UE does not need to recalculate PCMAX to adjust after scaling
For FR2 there is only one carrier for each serving cell. Notation f can be removed
PCMAX is not total configured output power
Text will be corrected