## Slide 1: WF on NR-U UE Tx Requirement
Skyworks Solutions Inc, Nokia, Ericsson, [Qualcomm, Charter]
3GPP TSG-RAN WG4 Meeting #94-bis-e R4-2005221
Electronic Meeting, Apr.20th – Apr.30th 2020

## Slide 2: Background and WF goal
Many contributions [5-10] discussed requirements or proposed CRs to introduce them in the specification
This WF clarify which requirements apply and if they are part on general requirements or band n46 specific requirement
A few contributions [1-4] provided MPR simulations or measurements but do not necessarily use same assumptions but have discussed them.
This WF further aligns assumptions and evaluation criteria
Scope and assumptions
  Only contiguous CC allocation is supported in CA (2CC) or wideband operation
  10MHz is ignored in single CC UL or wideband operation
  PI/2 BPSK is not supported in release 16
  Since 60KHz interlace definition is not agreed associated requirements are not developed in release 16
  In cases where in-band PSD do not apply requirement should apply to partially allocated NR waveforms

## Slide 3: WF on NR-U UE RF UL Requirements
NR General requirement that apply to NR-U
  Applicable power class and tolerance
  System EVM requirement
  Transmit impairments assumptions like 28dB carrier and image leakage
  NR IBE and impairment exceptions have to be adapted for interlace waveforms
  Maintain occupied bandwidth requirement even though it may be met automatically
  NR SEM does not apply but NR-U mask applies as general requirement
  The same may apply for 6GHz band and different/additional requirement are FFS but specification structure should enable that future addition
  Inter-band EN-DC and UL CA should be in general part

## Slide 4: WF on NR-U Specific Requirements
Structure of specification is TBD (suffix may be used for NR-U specific emission requirements)
Intra-band UL CA requirement are captured in this section
NR-U single CC and wideband operation mask as general requirement
NR SEM does not apply
ACLR: 27dB for PC5, [30-27]dB for PC3 reusing NR MBW associated with same channel bandwidth
IBE requirement starts from eLAA principles but:
  SCS scaling need to be clarified
  image and carrier exceptions position and specific tests needs to be developed for interlaces
  If possible it should remain applicable to fully and partially allocated waveforms
  Companies are encouraged to provide input to this requirement with the underlying assumption that in-band requirements should not govern MPR at least for DFT-s-OFDM QPSK waveforms

## Slide 5: WF on NR-U MPR evaluation - Mask
Since there is some differences in the evaluation of the mask, an alignment is needed whatever the procedures:
  One procedure is to use 100KHz RBW and apply the mask as is from the in-band peak measured in 1MHz
  The other one uses the agreed measurement bandwidths (1MHz except 100kHz in the first MHz adjacent to the wanted channel) for integration of the different mask sections but in this case the integration should be swept within ½ MBW inward in each section to avoid integrating emissions from other section that also see different slopes and/or MBW.
The NR-U mask specification should capture this behavior
It also needs to clarify LO exceptions for both single CC and Wideband operation
If contiguous 2CC UL CA is introduced the associated mask should be derived from the NR-U mask for wideband operation with all sub-block scheduled and limited to 80MHz aggregated bandwidth
    consistent with European regulation (EN 301 893)

## Slide 6: WF on NR-U MPR evaluation – EVM and impairments
Main difference between companies that has on impact on MPR result is the EVM budget for QPSK
Proposal: the following EVM and image rejection budget is used for MPR evaluation. Evaluation is done against the last column if the input waveform already includes the image leakage or if image contribution is not subtracted from the output signal
Agreement: PA EVM [10%] for QPSK (only limits CP-OFDM) and 8% for 16QAM
Modulation | SystemEVM | PA only | Image | PA+image
QPSK | 17.5% | [10]% | 28dB | [10.8]%
16QAM | 12.5% | 8% | 28dB | 8.95%
64QAM | 8% | 4% | 28dB | 5.65%
256QAM | 3.5% | 1.8% | 34dB | 2.69%

## Slide 7: WF on power class definition and MPR baseline
Agreement for n46 to be captured in general part:
  Power class 5 is 20dBm +2/-3
  If developed, Power class 3 is 23dBm +2/-3
    In release 16 assumes two PC5 paths in UL MIMO or TxDiv mode according to eMIMO WI progress and definitions and availability of related sugnaling
    Other implementations are not precluded
In order to compare MPR values a common MPR baseline needs to be agreed.
For PC5 the current range is from 0dB to 1.5dB MPR for DFT-s-OFDM QPSK 100RB0 20MHz waveform (or 100RB3 if it can be a higher power) to meet all requirements
Agreement: 1dB MPR for PC5 and DFT-s-OFDM QPSK 100RB3 20MHz waveform
Depending on ACLR agreement on PC3 additional [0-1]dB MPR may be needed

## Slide 8: WF on n46 Specific Requirements
NS introduced for B46 in LTE apply with associated requirements and A-MPR should be defined with appropriate scaling
  All channel bandwidths and SCS should be considered
  Single CC and wideband operation should be considered
  Requirements for NS (Europe) may be revised based on progress in ETSI BRAN
  Since NR-U masks is part of the general requirement it is not needed under NS
Open points for Japan NS 29:
Applicability of ACLR2 for Japan
  Is 40dB for PC5 valid? For all channel bandwidths?
  how does this work for wideband operation?
  Input from operators is needed
Applicability of 19/18.7MHz limits, how to scale?

## Slide 9: WF on NR-U MPR and A-MPR evaluation
MPR is evaluated with previous requirements at least for PC5 path
MPR is reported evaluating both 27 and 30dB ACLR to assess additional MPR for PC3
Full allocation and interlaced waveforms
QPSK, 16QAM, 64QAM and 256QAM
20, 40, 60 and 80MHz BW and wideband operation up to 80MHz
2CC Contiguous UL CA MPR is FFS
Companies are encouraged to provide all or subset of the above based on simulations and/or measurements
A-MPR Evaluation of in band power limitations for fully allocated and interlace waveform for:
  20, 40, 60, 80MHz single CC and wideband operation up to 80MHz
  At least QPSK DFT-s-OFDM waveforms

## Slide 10: References
[1] R4-2004725 NR-U MPR for PC5 single carrier and wideband Qualcomm Incorporated, R4#94B-e
[2] R4-2003871 Initial simulations of required MPR and A-MPR for PC5 and prerequisites for PC3, Ericsson, R4#94B-e
[3] R4-2004934 [NRU] MPR and Partial A-MPR for QPSK Waveforms, Skyworks Solutions Inc. , R4#94B-e
[4] R4-2004933 [NRU] EVM Budget and Other Assumptions for MPR and Applying NRU Masks, Skyworks Solutions Inc. , R4#94B-e
[5] R4-2004936 [NRU] UE Power Class Definition and Options, Skyworks Solutions Inc. , R4#94B-e
[6] R4-2004727 Introduction of NR-based access to unlicensed spectrum, Qualcomm Incorporated, R4#94B-e
[7] R4-2004232 NR-U - Capturing the Spectral Emission Mask, Nokia, Nokia Shanghai Bell, R4#94B-e
[8] R4-2004233 NR-U - draft CR to introduce SEM and ACLR for NR-U to TS 38.101-1, Nokia, Nokia Shanghai Bell, R4#94B-e
[9] R4-2004237 NR-U - Power Classes and Network Signalling values for Band n46, Nokia, Nokia Shanghai Bell, R4#94B-e
[10] R4-2004490 Considerations of in-band emissions for NR-U, Huawei, HiSilicon, R4#94B-e
[11] R4-2004724 NR-U In-band emissions requirement, Qualcomm Incorporated, R4#94B-e
[12] R4-2004723 NR-U Occupied bandwidth requirement, Qualcomm Incorporated, R4#94B-e