## Slide 1: 3GPP TSG-RAN WG4 Meeting # 94-Bis-e Electronic Meeting, 20 – 30 April, 2020
Huawei, HiSilicon
WF on SCell activation requirements
R4-2005269

## Slide 2: Issue 5-4: Correction of activation timeline in FR2 (background)
In current SCell activation requirements, TFirstSSB, Trs, TFirstSSB_MAX and TSMTC_MAX are used to account for delays in acquiring different SSB bursts
Assumption in SCell activation requirements
  TFirstSSB is the time to first SSB burst that is used for T/F tracking or cell search (w/o AGC)
  Trs is the periodicity of SSB burst that is used for T/F tracking and cell search (w/o AGC)
  TFirstSSB_MAX is the time to first SSB burst that is used for AGC
  TSMTC_MAX is the periodicity of SSB burst that is used for AGC
For FR1 unknown SCell activation, delay for AGC and cell search is TFirstSSB_MAX + TSMTC_MAX + Trs
For FR2 unknown SCell activation, delay for AGC and cell search is 24* Trs

## Slide 3: Issue 5-4: Correction of activation timeline in FR2 (WF)
For FR2 unknown SCell activation, replace 24*Trs with
  Option 1a: TFirstSSB + 23* Trs
  Option 1b: TFirstSSB_MAX + 23* Trs
  Option 2: TFirstSSB_MAX + 15* TSMTC_MAX + 8*Trs
Way forward
  Adopt option 2
  To be captured in revised R4-2004337

## Slide 4: Issue 5-5: Interruption window definition for SCell activation (background)
Interruption during SCell activation
  During SCell activation interruption is allowed due to RF re-tuning and AGC
  Interruption window is specified in section 8.3.2
  Interruption length is specified in section 8.2
RF re-tuning in SCell activation may happen any time between
  Earliest: UE finishes MAC CE processing for the activation command, and
  Latest: the first SSB burst UE is going to use
AGC in SCell activation may happen at
  The first SSB burst
  Note: AGC is only needed for FR1/FR2 unknown case and FR1 known case with measurement cycle > 160ms
  Note: AGC interruption only applies to intra-band active serving cells
RF re-tuning and AGC may not be adjacent in time

## Slide 5: Issue 5-5: Interruption window definition for SCell activation (WF)
Start point of interruption window during SCell activation
  Option1: shall not occur before slot n+1+ and not occur after slot n+1+ ,
  Option 2: shall not occur before slot n+1+
  where TX is:
  TFirstSSB, for any scenario where Tactivation_time includes TFirstSSB;
  TFirstSSB_MAX, for any scenario where Tactivation_time includes TFirstSSB_MAX;
  Tuncertainty_MAC +TFineTiming, for any other scenario where Tactivation_time includes TFineTiming
End point of interruption window during SCell activation shall not occur after slot n+1+ + Ninterruption, where Ninterruption is the length of interruption defined in section 8.2
To be captured in revised R4-2004419

## Slide 6: Issue 5-6: SSB pattern for FR2 intra-band CA case for SCell activation (background)
If the SCell being activated belongs to FR2 and if there is at least one active serving cell on that FR2 band, then Tactivation_time is TFirstSSB+ 5ms provided:
  The UE is provided with SMTC for the target SCell, and
  The SSBs in the serving cell(s) and the SSBs in the SCell fulfil the condition defined in clause 3.6.3.
The requirement is assuming UE to fine time tracking based on the timing and beam information obtained from the active serving cell
It is unclear to UE which SSB in the SSB burst it should use on the to-be-activated SCell, if the SSB pattern ssb-PositionsInBurst is different in the active serving cell (e.g. Cell 1) and the to-be-activated Scell (e.g. Cell 2)

## Slide 7: Issue 5-6: SSB pattern for FR2 intra-band CA case for SCell activation (WF)
FFS for RAN4-95-e: whether a new condition as in red for the requirements is needed
If the SCell being activated belongs to FR2 and if there is at least one active serving cell on that FR2 band, then Tactivation_time is TFirstSSB+ 5ms provided:
  The UE is provided with SMTC for the target SCell, and
  The SSBs in the serving cell(s) and the SSBs in the SCell fulfil the condition defined in clause 3.6.3.
  The parameter ssb-PositionsInBurst is same for the serving cell(s) and the Scell

## Slide 8: Issue 5-7: Definition of TFirstSSB and TFirstSSB_MAX (background)
The current definition of TFirstSSB and TFirstSSB_MAX are defined as the “first SSB indicated by the SMTC”
UE needs to receive the complete SSB burst to do AGC or T/F tracking, and with current definition the time of the SSB burst is missed from the activation delay

## Slide 9: Issue 5-7: Definition of TFirstSSB and TFirstSSB_MAX (WF)
Update the definition of TFirstSSB and TFirstSSB_MAX
TFirstSSB : the time to the end of the first complete SSB burst indicated by the SMTC after slot n + THARQ+3ms
TFirstSSB_MAX : the time to the end of the first complete SSB burst indicated by the SMTC after slot n + THARQ+3ms
To be captured in revised R4-2004337

## Slide 10: Issue 5-8: Restriction of RRM measurements for unknown SCell activation (background)
For unknown SCell activation, UE is assumed to do cell search.
The search time is not scaled with CSSF, Kp or Klayer1_measurement, meaning UE is prioritizing the cell search for the to-be-activated SCell
UE will have no opportunities to perform L3 and L1 measurement during the cell search time in SCell activation
For Rel-16 multiple SCell activation, it has been agreed in R4-2002249 that “the cell identification and RRM measurement for other SCCs is not assumed during the longest cell detection time among unknown SCells being activated in multiple SCell activation requirement design”

## Slide 11: Issue 5-8: Restriction of RRM measurements for unknown SCell activation (WF)
Longer delays for RRM measurement requirements, and in case of FR2 also SSB based RLM/BFD/CBD/L1-RSRP measurement requirements, can be expected during the cell detection time for unknown SCell activation
To be captured in revised R4-2004337