## Slide 1: Way forward on FR2 inter-band CA requirement
Huawei, HiSilicon
3GPP TSG-RAN4 Meeting #94-ebis
Online, 20th– 30th April, 2020
Agenda: 6.15.1.10
R4-2005353

## Slide 2
The RRM requirements for FR2 inter-band CA scenario shall be defined based on the following principles:
    RRM requirements work for FR2 inter-band CA should be aligned with the deployments, scenarios, band combinations and RF architectures discussed for release 16 for FR2 inter-band CA in the RF session.
    For FR2 inter-band CA for common beam and independent beam, UE should begin with understanding which scenarios can be supported with common beams and which will need independent beams. The corresponding requirements for common and independent beams can then be derived.
Agreements on FR2 inter-band CA requirements

## Slide 3: Agreements on the scaling factor CSSFoutside_gap
The scaling factor CSSFoutside_gap for FR2 inter-band CA is defined as:
Where, only two FR2 bands are specified for FR2 inter-band CA in release 16. It is assumed that UE has two searchers for performing intra-frequency measurements without gaps.
Scenario | CSSFoutside_gap,i for FR2 PCC (in SA or NE-DC mode) or FR2 PSCC (in EN-DC mode) | CSSFoutside_gap,i for FR2 SCC where neighbour cell measurement is required | CSSFoutside_gap,i for FR2 SCC where neighbour cell measurement is not required
FR2 inter-band CA | 1 | 2Note 1 | 2×(Number of configured SCell(s) - 1)
Note1: CSSFoutside_gap,i =1 if only one SCell is configured and neighbour cell measurement is required on this Scell. |  |  | 

## Slide 4
For a FR2 inter-band CA combination with using independent beam management, the existing interruption requirements for inter-band CA can be applied.
For a FR2 inter-band CA combination with using common beam management, FFS whether the existing interruption requirements for inter-band CA can be applied.
    RF inputs on RF architectures for FR2 inter-band CA combination with using common beam management are required.
    If the separate RF chains are assumed for FR2 inter-band CA combination with using common beam management, the existing interruption requirements of inter-band CA can be applied.
    If the same RF chain is assumed for FR2 inter-band CA combination with using common beam management, FFS whether the existing interruption requirements of intra-band CA can be applied.
Agreements on interruption requirements

## Slide 5: Agreement on beam management requirementz
Beam management resource configuration for FR2 inter-band CA combination with independent beam:
    Beam management resources on one cell in each band may be configured.
    Network may also configure beam management resources only on one cell such as Pcell, e.g. if network knows nodes on both bands are collocated.
Beam management requirements for FR2 inter-band CA combination with independent beam:
    For BFD/CBD on PCell/PSCell
      R15 BFD/CBD measurement requirements in FR2 can be applied for FR2 inter-band CA scenario.
    For BFD/CBD on SCell
      RAN4 to use SCell BFD/CBD requirements as being defined in eMIMO WID as baseline.
    For L1-RSRP reporting.
      R15 L1-RSRP measurement requirements in FR2 can applied for FR2 inter-band CA scenario.
Beam management requirements for FR2 inter-band CA combination with common beam :
    RAN4 needs to study whether UE is necessary to perform BFD/CBD measurements on SCell.
      Option 1:The BFD/CBD on SCell is not necessary, because the beam management can rely on the PCell which the common beam is applied as it for the SCell.
      Option 2: Others.

## Slide 6: Agreement on scheduling restriction requirement
Scheduling restriction requirements for FR2 inter-band CA combination with independent beam
    Option 1:
      There are no scheduling restrictions on one FR2 band due to RLM/BFD/CBD/L1-RSRP measurements being performed on another FR2 band.
      The scheduling availability requirements for FR2 inter-band CA scenario shall be introduced to clarify there is no scheduling restriction if UE uses independent beam.
    Option 2:
      No scheduling restriction from UE RX beam perspective, but further discussion is needed from the perspective of different numerologies and collision between UL and DL transmission.
Scheduling restriction requirements for FR2 inter-band CA combination with common beam
    The scheduling availability requirements for FR2 inter-band CA scenario shall be introduced to clarify there is scheduling restriction on one FR2 band due to RLM/BFD/CBD/L1-RSRP measurements being performed on another FR2 band if UE uses common beam.
    The existing scheduling restriction requirements on FR2 shall be extended to serving cells in different bands.

## Slide 7: Agreement on measurement restriction requirements
Measurement restriction requirement for FR2 inter-band CA combination with common beam
    The measurement restriction requirements due to RLM/BFD/CBD/L1-RSRP measurements being performed on different FR2 bands need to be introduced for FR2 inter-band CA if UE uses common beam.
    Option 1:
      There are no measurement restriction if following conditions are satisfied:
        Transmission points of each FR2 band are co-located.
          FFS whether QCL type D between measurement resources of each band is needed.
        Time domain allocation of each measurement RS is partially or fully overlapped.
    Option 2:
      The existing measurement restriction requirements for FR2 shall be extended to serving cells in different bands.
    Others

## Slide 8: Agreement on SCell activation delay requirements
SCell activation requirement for case 1: SCell being activated belongs to FR2 and if there is at least one active serving cell on that FR2 band
    The existing SCell activation delay requirements in case of “SCell being activated belongs to FR2 and if there is at least one active serving cell on that FR2 band” can be reused for FR2 inter-band CA.
SCell activation requirement for case 2: SCell being activated belongs to FR2 and if there is no active serving cell on that FR2 band provided that PCell or PSCell is FR2
    For FR2 inter-band CA combination with independent beam.
      The existing requirement of “SCell being activated belongs to FR2 and if there is no active serving cell on that FR2 band provided that PCell or PSCell is FR1” can be applied.
    For FR2 inter-band CA combination with common beam.
      The existing requirement of “SCell being activated belongs to FR2 and if there is no active serving cell on that FR2 band provided that PCell or PSCell is FR1” cannot be applied.
      The SCell activation delay for case 2 can be studied from the following aspects:
        Whether AGC settling time need to be included.
        Whether cell search time need to be included.
        Whether fine timing tracking delay need to be included.