## Slide 1: WF on intra-band UL contiguous CA emission requirement
Huawei, HiSilicon, Qualcomm, Skyworks, Nokia
R4-2005657
3GPP TSG-RAN WG4 #94bis-e
April 20th – 30th, 2020
Electronic meeting

## Slide 2: Background
Currently BWchannel_CA is specified in TS 38.101 as below:
BWChannel_CA = Fedge,high - Fedge,low (MHz), Fedge,low = FC,low - Foffset,low, Fedge,high = FC,high + Foffset,high
Foffset,low = (NRB,low*12 + 1)*SCSlow/2 + BWGB (MHz)
Foffset,high = (NRB,high*12 - 1)*SCShigh/2 + BWGB (MHz)
BWGB = max(BWGB,Channel(k))
Considering the RF requirements are evaluated and specified under nominal channel space:
BWchannel_CA= Nominal channel space+ Foffset,low + Foffset,high
In Which, nominal channel space for CA are specified with fixed numerology which ensures there is a channel space entry less than or equal to the nominal channel space for any CC configurations, where the SCS for Foffset,low and Foffset,high are specified with the assigned SCS to each CC. It leads to: BWchannel_CA= Nominal channel space+ Foffset,low + Foffset,high>CBW1+CBW2
To solve the issue, Several Options for BWchannel_CA are discussed in RAN4 #94bis-e meeting:
Option 1:
Option 2: Aggregated channel bandwidth= channel space+ Foffset,low+ Foffset,high, channel space can be less than nominal channel space
Option 3: For Foffset,low and Foffset,high, SCS adoption of each CC is defined as μ0 in 5.4A.1 of 38.101(μ0 defined for nominal channel space)
Aggregated channel bandwidth=nominal channel space+ Foffset,low+ Foffset,high

## Slide 3: Background
ACLR MBW are discussed with following solutions:
Solution 1:
, where (=1, 2) are the minimum guard band widths used in subclause 5.4A.1.
If ,
,
else
Solution 2:
MBW= BWchannel_CA -2*max(BWGB1, BWGB2). SCS adoption of each CC is defined as current 5.3A.3 of 38.101
Channel space can be less or equal to nominal channel space to ensure BWchannel_CA not exceed CBW1+CBW2
Channel space=nominal channel space for simulation assumption of UL CA MPR.
Solution 3:
Define dedicated nominal channel space for RF CA test:
Nominal channel space use the least common multiple of configured SCS and channel raster
Channel space=nominal channel space for RF CA test
For Foffset,low and Foffset,high, SCS adoption of each CC is defined as current 5.3A.3 of 38.101
Channel space can be less than nominal channel space when defining RF requirement
Solution 4:
ACLR MBW=BWChannel_CA – GBChannel(1) - GBChannel(2). Where BW = nominal channel spacing + Foffset,low, + Foffset,high, do not use largest common μ for Foffset,low and Foffset,high, largest common μ is only for nominal channel spacing.

## Slide 4: WF on BWchannel_CA
Agreement on BWchannel_CA
  BWchannel_CA= Nominal channel space+ Foffset,low + Foffset,high
  the SCS adoption for Foffset,low + Foffset,high are the common largest SCS specified in 5.4A.1 of TS 38.101.
Proposed CR to 5.3A.3 based on the agreement:
The lower and upper frequency offsets depend on the transmission bandwidth configurations of the lowest and highest assigned edge component carrier and are defined as
Foffset,low = (NRB,low*12 + 1)*SCSlow/2 + BWGB (MHz)
Foffset,high = (NRB,high*12 - 1)*SCShigh/2 + BWGB (MHz)
BWGB = max(BWGB,Channel(k))
BWGB,Channel(k) is the minimum guard band defined in clause 5.3.3 of carrier k, while NRB,low and NRB,high are the transmission bandwidth configurations according to Table 5.3.2-1 for the lowest and highest assigned component carrier, SCSlow and SCShigh are the sub-carrier spacing for the lowest and highest assigned component carrier respectively. The SCS for each CC SCSlow, SCShigh, NRB,low, NRB,high, and BWGB,Channel(k) use the common largest μ value among the subcarrier spacing configurations supported in the operating band for both of the channel bandwidths according to μ0 in 5.4A.1 and BWGB,Channel(k) is the minimum guard band for carrier k according to Table 5.3.3-1 for the said μ value.

## Slide 5
WF on ACLR MBW
Define a single ACLR MBW for each bandwidth combination across all SCS combinations
Agreement on ACLR MBW:
and are the single-channel ACLR measurement bandwidths specified for channel bandwidths and in 6.5.2.4.1, respectively.
FFS on the center of ACLR MBW, following analysis is provided during discussion:
Center of ACLR MBW within transmitted (aggressor) sub-block is .
Centers of MBWs within victim sub-blocks are ,

## Slide 6
Reference on BWchannel_CA
Option 1 [R4-2003236]:
Option 2:
  BWchannel_CA= Nominal channel space+ Foffset,low + Foffset,high
  the SCS adoption for Foffset,low + Foffset,high are the common largest SCS specified in 5.4A.1 of TS 38.101.
Comparison:
CBW1(MHz) | CBW2(MHz) | Nominal channel space(MHz) | μ0 defined in 5.4A.1. for SCS adoption | Foffset,low in Option 2 (MHz) | Foffset,high in Option 2 (MHz) | BWchannel_CA for option 1 | BWchannel_CA for option 2
5 | 100 | 52.14 | 30kHz | 2.84 | 49.97 | 105 | 104.95
10 | 100 | 54.6 | 60kHz | 5.36 | 49.94 | 109.8 | 109.9
60 | 100 | 79.8 | 60kHz | 30 | 50.1 | 159.6 | 159.9

## Slide 7
Reference on ACLR MBW
Option 1 [R4-2003236]:
Option 2:
  ACLR MBW= BWchannel_CA -2*max(BWGB1, BWGB2).
  Ensure all wanted signal is captured for ACLR measurement, take the minimum value among Max(BWGB1,BWGB2) for all SCS band combinations:
Comparison:
CBW1 | CBW2 | MBWACLR1 in option1 | MBWACLR2 in option1 | BWchannel_CA for option 1 | BWchannel_CA for option 2 | Foffset,low in Option 1 | Foffset,high in Option 1 | Min {Max(BWGB1,BWGB2)} In Option2 | MBW ACLR for option 1 | MBW ACLR for option 2
5 | 100 | 4.515 | 98.31 | 105 | 104.95 | 3.37 | 50 | 845kHz | 103.31 | 103
10 | 100 | 9.375 | 98.31 | 109.8 | 109.9 | 5.36 | 50 | 845kHz | 108.455 | 108
60 | 100 | 58.35 | 98.31 | 159.6 | 159.9 | 30 | 49.8 | 845kHz | 158.31 | 158