## Slide 1: WF on intra-band UL non-contiguous CA general requirements
KDDI, Skyworks, Qualcomm, Huawei
3GPP TSG-RAN WG4 Meeting #94-bis-e R4-2005660
Electronic Meeting, Apr.20th – Apr.30th 2020

## Slide 2: Background
UL NC CA requested configurations in Rel-16 are as follows
  n41(2A), n77(2A), n78(2A)
  The number of UL subcarrier allowed in Rel-16 is two
Comparison of different PA/LO architectures [2]
  1PA/1LO:
    instantaneous TX bandwidth: ~200MHz
    Number of TX chain: 1 (2TX to support UL MIMO)
  2PA/2LO:
    instantaneous TX bandwidth: >200MHz can be supported (and below obviously)
    Number of TX chain: 2 (4TX to support UL MIMO)
  1PA/2LO has the same situation as 2PA/2LO. However, it is not recommended for the following reasons
    inherent power backoff (insertion loss) issue [3]
      One possible solution is to put 3dB combiners and switches in the PA
    requires extra complexity and may still be limited for UL MIMO due to limited number of TX chains
Instantaneous TX bandwidth: frequency range from the lower bound of lower CC to the upper bound of upper CC.

## Slide 3: WF of applicability of intra-band UL NC CA requirements
It is unclear when to apply intra-band UL non-contiguous CA requirements.
RAN4 will further discuss and clarify the applicability aspect in Rel-16 timeframe.

## Slide 4: WF of UE architecture
Only consider 2PA/2LO case for intra-band UL NC CA in Rel-16.
  According to spectrum allocation information from interested operators in [1], most cases cannot apply 1PA/1LO architecture which has limitation of instantaneous TX bandwidth as up to 200MHz.
  1PA/1LO architecture can apply to n41(2A), however there are no comments on UE architecture for n41(2A) so far. 1PA/1LO case can be discussed based on operator requests as the 2nd priority after 2PA based requirements are finalized.
Since 1PA/1LO architecture is an essential case and can apply to most refarming bands, discussion of general requirements and UE capability in this WF also consider 1PA/1LO.
  To make sure that signaling and spec structures enable the introduction of 1PA/1LO related requirements and potential exception

## Slide 5: WF of ACLR
No ACLR requirement
  if Wgap < max(CC1BW, CC2BW) to prevent excessive in-band emission with other sub-block.
For 1PA/1LO architecture, exception should be allowed while the leakage and image falling on a frequency belonging to another licensee assuming synchronization across licensees, or if LO leakage lands on licensee's own spectrum holding.

## Slide 6: WF of SEM
Where two masks overlap, the most relaxed limit is used.
Composite spectrum emission mask applies to frequencies up to  ΔfOOB starting from the edges of the sub-blocks
If for some frequency an individual sub-block spectrum emission mask overlaps with the bandwidth of another sub-block, the emission mask does not apply for that frequency.
For 1PA/1LO architecture, exception should be allowed while the leakage and image falling on a frequency belonging to another licensee assuming synchronization across licensees, or if LO leakage lands on licensee's own spectrum holding.

## Slide 7: WF of spurious emission
The spurious emission limits apply for the frequency ranges that are more than ∆FOOB (MHz) from the edge of the aggregated channel bandwidth for frequencies in the gap and out of the gap. For frequencies ΔFOOB greater than FOOB, the spurious emission requirements in Table 6.5.3-2 (TS38.101-1) are applicable
No spurious requirement applies in the gap if Wgap < ∆FOOB1 + ∆FOOB2, otherwise only composite SEM

## Slide 8: WF of synchronization of n77/n78/n79
UL NC CA follows Rel-16’s assumption that n77 is synchronized with n79.
Async operation is specified in Rel-16 for n78-n79 only UE with special filter assumption. Asynchronous n78-n79 assumes no concurrent n77-n78 operation as stated in R4-1915529. Async operation of UL NC CA can be discussed based on operator request.
  The band n78 filter provides some protection from a single CC TX noise but this may not be sufficient for IMDs (IMD5 and 7). We need to clarify max TX BW for n78(2A) to check filters and IMDs if n78 and n79 are Asynchronous

## Slide 9: WF of Radio altimeter protection
No additional requirement for radio altimeter protection at 4200MHz – 4400MHz.

## Slide 10: WF of MIMO supporting for UL NC CA
Requirements for MIMO related signalling
  If UL MIMO support is signalled for nXXA it cannot be supported for nXX(2A) if dual-PA is signalled under current signalling
  MIMO supporting with 4TX for 2PA UL NC CA should not be excluded, and capture it in RAN4 Rel-16 feature list for UL NC CA.
Send LS to RAN2

## Slide 11: Reference
[1] R4-2002812, “WF on Intra-band Non-contiguous ULCA TX Architectures and Issues”, Qualcomm, Skyworks, KDDI
[2] R4-2005100, “Email discussion summary for RAN4#94be_#14_NR_RF_FR1_Part_1”, Huawei
[3] R4-2004467, “FR1 Intra-band Non-contiguous ULCA”, Qualcomm