## Slide 1: WF on 2-step RACH RRM requirements
ZTE
3GPP TSG-RAN WG4 Meeting #94-e-Bis
Electronic Meeting, Apr. 20th – Apr. 30th 2020
R4-2005844

## Slide 2: Agreements
Create new clause 6.2.2.3 in TS38.133 to capture the 2-step RACH RRM requirements.
RRM requirements are specified for both contention-based and contention-free 2-step RACH.
Scenarios for specifying UE behaviour for contention-based 2-step RACH and contention-free 2-step RACH
  Correct behavior when transmitting MsgA
  Correct behavior when receiving MsgB
  Correct behavior when not receiving MsgB
UE behaviour to be specified when receiving MsgB for contention-based 2-step RACH
  UE behavior after receiving Fallback RAR
  UE behavior after receiving Success RAR
  UE behavior regarding Backoff indicator

## Slide 3: Agreements
The existing requirements for following procedures in TS 38.133 and TS 36.133 are applicable for both 4-step RACH and 2-step RACH
  Handover
  UL transmit timing
  RRC Re-establishment to NR
  RRC connection release with redirection to NR
  PSCell addition in NR-DC
  PSCell addition in EN-DC
Terminology for differentiating 4-step RACH and 2-step RACH in TS 38.133
  “4-step RA type” and “2-step RA type”
FFS if clarification in the spec is needed for existing RRM requirements that are applicable to both 4-step RACH and 2-step RACH

## Slide 4: WF
FFS if clarification in the spec is needed for existing RRM requirements that are applicable to both 4-step RACH and 2-step RACH