## Slide 1: 3GPP TSG-RAN WG4 Meeting #94-e-Bis R4-2005187 Electronic Meeting, 20 – 30 April, 2020
Way forward on NR band n259
Agenda Item: 8.16
Document for: Approval
Source: Ericsson

## Slide 2: Background
The remaining open issues to complete the introduction of band n259 WI that have been discussed in RAN4#94-e-Bis, R4-2005113:
  Beam correspondence: R4-2003177 (NTT DOCOMO) and R4-2004749(Huawei)
  Intra band contiguous CA: R4-2003177 (NTT DOCOMO) and 3UK
  EESS protection: R4-2004877 (Qualcomm), R4-2003177 (NTT DOCOMO) and R4-2004749(Huawei)
and
  Multiband relaxation framework: This issue has been discussed in [94e Bis][20] NR_RF_FR2_req_enh_Part_4 thread

## Slide 3: Agreements
Beam correspondence
Rel-15 beam correspondence mechanism can be reused for n259 with the following value for beam correspondence tolerance for PC3:
Table 2-1: UE beam correspondence tolerance for power class 3
Operating band | Max ∆EIRPBC at 85th %-tile ∆EIRPBC CDF (dB)
N257 | 3.0
N258 | 3.0
N259 | 3.2
N260 | 3.2
N261 | 3.0
NOTE: The requirements in this table are verified only under normal temperature conditions as defined in Annex E.2.1 | 
The BC requirement will be updated to reflect the outcome of the Rel-16 BC discussion in UE RF FR2 WI once the discussion is concluded
Multiband relaxation framework
As agreed in [94e Bis][20] NR_RF_FR2_req_enh_Part_4 thread.

## Slide 4: Agreements
Intra band contiguous CA
CA_n259B | CA_n259B | 50, 100, 200, 400 | 400 |  |  |  |  |  |  | 800 | 0
CA_n259C | CA_n259B | 50, 100, 200, 400 | 400 | 400 |  |  |  |  |  | 1200 | 0
CA_n259G | CA_n259G | 50, 100 | 100 |  |  |  |  |  |  | 200 | 0
CA_n259H | CA_n259G CA_n259H | 50, 100 | 100 | 100 |  |  |  |  |  | 300 | 0
CA_n259I | CA_n259G CA_n259H CA_n259I | 50, 100 | 100 | 100 | 100 |  |  |  |  | 400 | 0
CA_n259J | CA_n259G CA_n259H CA_n259I CA_n259J | 50, 100 | 100 | 100 | 100 | 100 |  |  |  | 500 | 0
CA_n259K | CA_n259G CA_n259H CA_n259I CA_n259J CA_n259K | 50, 100 | 100 | 100 | 100 | 100 | 100 |  |  | 600 | 0
CA_n259L | CA_n259G CA_n259H CA_n259I CA_n259J CA_n259K CA_n259L | 50, 100 | 100 | 100 | 100 | 100 | 100 | 100 |  | 700 | 0
CA_n259M | CA_n259G CA_n259H CA_n259I CA_n259J CA_n259K CA_n259L CA_n259M | 50, 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 800 | 0

## Slide 5: Way-forward for EESS protection
How to incorporate WRC-19 conclusion for EESS protection in 36-37GHz into 3GPP specification:
Proposals
  Option 1: EESS protection for band n259 should be treated in the introduction of NR band n259 WI with the condition that agreement can be reached in RAN4#95-e (May meeting)
  Option 2: EESS protection for both band n259 and n260 should be treated together
The solution should be in line with solution at 24 GHz
The completion of n259 WI does not depend on the study progress of EESS protection

## Slide 6: References
[1] R4-2005708 , “Email discussion summary for [94e Bis][27] NR_n259”, Ericsson
[2]R4-2003177, “Towards completion of n259 UE RF requirements”, NTT DOCOMO
[3]R4-2004749, “On remaining UE RF requirements for n259”, Huawei
[4]R4-2004877, “dCR to 38.101-2: Incorporation of WRC19 Resolutions into n259”, Qualcomm