## Slide 1: WF on merged A-MPR proposals
LG Electronics,
3GPP TSG-RAN WG4 Meeting #94-bis-e R4-2005189 Electronic Meeting, 20th – 30th Apr., 2020

## Slide 2: Background(1)
[1] was approved in RAN4#94-e meeting to have a common understanding of the baseline architecture option and PC2 A-MPR in Rel-15.
Based on comments from interested companies during 1st round of email discussion [2] in RAN4#94-bis-e meeting, both architecture options of 2x23dBm and 2x26dBm can be supported in Rel-15 and RAN4 has chosen to focus on discussing Rel-16 requirements of B41/n41 29dBm HPUE.
There are a few things to be finalized in 2nd round and they can be listed as follows:
  Rel-16 A-MPR for PC2 and PC1.5 intra-band EN-DC based on 2x26dBm
  ModifiedMPRbehavior bit for PC2 intra-band EN-DC in Rel-16
  General MPR for PC3 and PC2 intra-band EN-DC in Rel-16

## Slide 3: Background(2)
Rel-16 B41/n41 A-MPR
  Merged A-MPR from [3] and [4], and [5]
<-13dBm/MHz>
<-25dBm/MHz>
<-30dBm/MHz>
  Note: 10dB antenna isolation A-MPR values are used to be merged for [5]

## Slide 4: Background(3)
General MPR for PC3 and PC2 intra-band EN-DC in TS38.101-3
  In [2], the moderator has suggested candidate options as follows:
    Keep the same arrangement for MPR and A-MPR sections of intra-band non-contiguous. New Rel-16 A-MPR to be applied relative to 26 dBm for a PC2 cell group and relative to 23 dBm for a PC3 cell group for PC3, PC2 and PC1.5 intra-band EN-DC.

## Slide 5: Way Forward(1)
    <-13dBm/MHz>
    12 ; 0 ≤B<0.54
    10 ; 0.54 ≤B<1.08
    9 ; 1.08 ≤B<2.16
    8.5 ; 2.16 ≤B<3.24
    8 ; 3.24 ≤B<5.4
    6 ; 5.4 ≤B
  <-25dBm/MHz>
  15; 0 ≤B<1.08
  14; 1.08 ≤B<5.4
  13; 5.4 ≤B<8.1
  12; 8.1≤B <25.2
  10; 25.2 ≤B
    <-30dBm/MHz>
    18; 0 ≤B<1.08
    17.5; 1.08 ≤B<2.16
    17; 2.16 ≤B<3.24
    15; 3.24 ≤B<5.4
    14; 5.4 ≤B<10.8
    13; 10.8 ≤B
Proposal 1-2’(a): Based on the moderator’s comment [2], maximum A-MPR values from [3], [4], and [5] in the slide 3.
Note: (Other companies are okay for the proposal values and Qualcomm needs to check them in RAN4#95)

## Slide 6: Way Forward(2)
Proposal 1-3’:
  The new A-MPR for 26 dBm cell groups relative to 26 dBm also applies to 23 dBm cell groups relative to 23 dBm in Rel-16 so that we only have one set of A-MPR tables.
  The conclusion of Rel-16 A-MPR will have no impact on Rel-15.
One of proposals in Proposal 1-4’:
  Keep the same arrangement for MPR and A-MPR sections.
    If there is a need for a single PA architecture for a new intra-band EN-DC band in the future, then RAN4 can discuss about new MPR/A-MPR requirements.
Proposal 1-6’:
  Discuss options for resolving Apple’s ACLR comment first and then RAN4 will decide whether the final option can be included in the revision of R4-2003015 and the definition of NS_04 A-MPR or not.

## Slide 7: Remaining issues
RAN4 can further discuss about the proposal 1-4’ in the next meeting.
Proposal 1-3’:
  The new A-MPR for 26 dBm cell groups relative to 26 dBm also applies to 23 dBm cell groups relative to 23 dBm in Rel-16 so that we only have one set of A-MPR tables.
Proposal 1-4’:
  Keep the same arrangement for MPR and A-MPR sections.
  New Rel-16 A-MPR table to be applied relative to 26 dBm for a PC2 cell group and relative to 23 dBm for a PC3 cell group for PC3, PC2 and PC1.5 intra-band EN-DC.
  Modified MPR bit allows a PC3, PC2 or PC1.5 UE to use Rel-15 or Rel-16 A-MPR.

## Slide 8: References
[1] R4-2002913, “Way Forward on A-MPR for PC1.5 intra-band EN-DC,” Sprint, Qorvo, Intel
[2] R4-2005111, “Email discussion summary for [94e Bis][25] LTE_NR_B41_Bn41_PC29dBm,” T-Mobile USA
[3] R4-2003247, “A-MPR for PC1.5 intra-band EN-DC,” LG Electronics
[4] R4-2004689,”A-MPR Proposal for B41/n41 EN-DC,” Apple
[5] R4-1911029,”A-MPR MPR improvement for B41/n41 EN-DC,” Intel