## Slide 1: WF on new intra-band BW classes
Ericsson
R4-2005220
3GPP TSG-RAN WG4 Meeting #94-e-bis
Electronic meeting, 20 – 30 April 2020

## Slide 2: Background
According to the WID [1], wideband operations in multiples of 20 MHz should be supported by both multiple serving cells (i.e. CA of 20 MHz cells) and one serving cell with bandwidth > 20 MHz with potential scheduling constraint (i.e. “wideband carrier”). The RAN1 objectives in the WID state
  “Physical layer aspects including [RAN1]:
  […]
  Wide band operation (in integer multiples of 20MHz) for DL and UL for NR-U supported with multiple serving cells, and wideband operation (in integer multiples of 20MHz) for DL and UL for NR-U supported with one serving cell with bandwidth > 20MHz with potential scheduling constraint subject to input from RAN2 and RAN4 on feasibility of operating the wideband carrier when LBT is unsuccessful in one or more LBT subbands within the wideband carrier. For all wide-band operation cases, CCA is performed in units of 20MHz (at least for 5GHz).”
RAN4 should therefore specify NR CA BW classes supporting both modes of wide band operation in multiples of 20 MHz
Wide band operation (in integer multiples of 20MHz) for DL and UL for NR-U supported with multiple serving cells not possible with current CA BW Classes
1. RP-191575

## Slide 3: Way forward
Define three new NR CA bandwidth classes to allow intra-band contiguous CA for NR-U in multiples of 20 MHz and wider bandwidths
  class “M”: 50 MHz ≤ BWChannel_CA ≤ 180 MHz, number of contiguous CC = 3
    The lower limit also covers one 10 MHz channel bandwidth (10 + 20 + 20 MHz to cover 50 MHz allocation)
  class “N”: 80 MHz ≤ BWChannel_CA ≤ 240 MHz, number of contiguous CC = 4
  class “O”: 100 MHz ≤ BWChannel_CA ≤ 300 MHz, number of contiguous CC = 5
belonging to the same fall-back group
Upper limits defined as multiples of the 60 MHz channel bandwidth
  larger aggregated bandwidths covered by existing classes (see next slide)
2 CC covered by the existing CA BW class B and C
The classes M, N and O only applies to NR-U operation
Note 1: agreed assumptions on number of CCs for DL/UL and scope (e.g. two contiguous CCs in the UL) for Rel-16 remains
Note 2: the channel raster frequencies for the 10 MHz are restricted

## Slide 4: Relation to other BW classes
Larger aggregated bandwidths for intra-band contiguous CA will be covered by the existing CA BW classes, e.g.
  3 * 80 MHz by BW Class D
  4 * 80 MHz by BW Class E
  and with the fallback paths covered by the existing specification
This suggests that the new classes should cover aggregation of 10 MHz, 20 MHz, 40 MHz and 60 MHz bandwidths that is not fully covered by the existing classes
Therefore, n * 60 MHz chosen as the upper limits of M, N and O, the combinations up to 5 * 60 MHz providing a fallback path to a single 60 MHz carrier