## Slide 1: WF on max. input levels for NR V2X UE at n47
3GPP TSG-RAN WG4 Meeting #94-e-bis
Electronic Meeting, Apr. 20th - 30th 2020
Agenda item: 6.4.4.2
Document for: Approval
R4-2005230
CATT, Huawei

## Slide 2: Background
In RAN4#94-e meeting, it was agreed that the maximum input level at n47 for NR V2X should be specified based on channel bandwidths and modulation orders as indicated below, and the corresponding CR [1] with TBDs was endorsed as per [2].
  Issue 2-2-1: Maximum input level
  Agreement: Apply the same methodology in NR Uu or LTE V2X to introduce the maximum input level for NR V2X.

## Slide 3: Background
The maximum input level for LTE V2X is specified as follows:
The maximum input level for NR Uu is specified as follows:
Rx Parameter | Units | Channel bandwidth |  |  |  |  | 
 |  | 1.4 MHz | 3 MHz | 5 MHz | 10 MHz | 15 MHz | 20 MHz
Power in Transmission Bandwidth Configuration | dBm |  |  |  | -222 |  | -222
 |  |  |  |  | -233 |  | -233
NOTE 1: Reference measurement channel is defined in Annex A.8.2. NOTE 2: This requirement is applicable for 16QAM. NOTE 3: This requirement is applicable for 64QAM. |  |  |  |  |  |  | 
Rx Parameter | Units | Channel bandwidth |  |  |  |  |  |  |  |  |  |  |  | 
 |  | 5 MHz | 10 MHz | 15 MHz | 20 MHz | 25 MHz | 30 MHz | 40 MHz | 50 MHz | 60 MHz | 70 MHz | 80 MHz | 90 MHz | 100 MHz
Power in Transmission Bandwidth Configuration | dBm | -252 |  |  |  | -242 | -232 | -222 | -212 | -202 |  |  |  | 
 |  | -273 |  |  |  | -263 | -253 | -243 | -233 | -223 |  |  |  | 
NOTE 1: The transmitter shall be set to 4 dB below PCMAX_L,f,c at the minimum uplink configuration specified in Table 7.3.2-3 with PCMAX_L,f,c as defined in clause 6.2.4. NOTE 2: Reference measurement channel is A.3.2.3 or A.3.3.3 for 64 QAM. NOTE 3: Reference measurement channel is A.3.2.4 or A.3.3.4 for 256 QAM. |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 4: Way forward
  The maximum input level at n47 has been discussed in the 1st round based on [5]. The following options are summarized for the 2nd round discussion as follows:
  Maximum input level at n47
  Option 1: Follow max. input levels from NR Uu for 64QAM and 256QAM
  Option 2: Follow LGE proposal (R4-2003840) considering max. power at n47
  Option 3: -25dBm for 64QAM and -27dBm for 256QAM applicable to all CBWs
  WF: It will be decided in the next meeting.

## Slide 5: Reference
[1] R4-2002796, CR for TS38.101-1, Introduce Rx requirements for NR V2X, CATT, RAN4#94e
[2] R4-2002687, Email discussion summary for RAN4#94e_#14_5G_V2X_NRSL_UE_RX, Moderator (CATT), RAN4#94e
[3] R4-2002029, On remaining NR-V2X UE RF requirements, Huawei, HiSilicon, RAN4#94e
[4] R4-2000607, Dicussion on remaining RF requirements for NR V2X, CATT, RAN4#94e
[5] R4-2005094, Email discussion summary for 94e Bis_#8_5G_V2X_NRSL_UE_RF_1st round, Moderator (LG Electronics), RAN4#94-e-bis
[6] R4-2003840, Updated CR on introducing RF requirements for 5G V2X service in TS38.101-1 in rel-16, LG Electronics France, RAN4#94-e-bis
[7] R4-2003300, Discussion on remaining issues on Rx RF requirements for NR V2X, CATT, RAN4#94-e-bis