## Slide 1: WF on RRM measurement relaxation for Power Saving
CATT
3GPP TSG-RAN WG4 Meeting #94ebis R4-2005330
Electronic Meeting, Apr.20th – Apr.30th 2020

## Slide 2: Background
For information: Scenarios
  #1: Low mobility scenario
  #2: Not in cell-edge scenario
  #3: Low-mobility + Not in cell-edge scenario
RRM measurement relaxation methods for UE power saving in RRC_idle/inactive state
  Option 1: Allow RRM measurements with longer intervals
  Option 2: UE is not required to meet the intra-frequency and inter-frequency neighbor cell measurement requirements
Applicability of RRM relaxation methods when the relaxation criteria are fulfilled
 | Applicable RRM relaxation methods
Scenarios #1 | Option 1
Scenarios #2 | Option 1
Scenarios #3 | Option 2

## Slide 3: WF on RRM measurement relaxation
Fixed scaling factor of measurement interval is used for scenario#1 and scenario#2
  FFS the same value is used for scenario#1 and scenario#2
    Option 1: the same value (Nokia, CATT, vivo, MTK, Qualcomm, CMCC, ZTE)
      Option 1: 2 times (CMCC, ZTE)
      Option 2: 4 times (Nokia, CATT, MTK, vivo, Qualcomm, NEC)
    Option 2: different value (Nokia, CATT, Ericsson, CMCC)
      4 times for scenario#1 and 2 times scenario#2 (Ericsson, Nokia, CATT, CMCC, NEC)
  The scaling factor of RRM measurement relaxation with longer intervals shall apply to Tdetect, Tevaluate, and Tmeasure.
  The time interval for measurement relaxation since last measurement for cell reselection for scenario#3 (Low mobility and Not in cell-edge scenario) is 1 hour
  When network configures the parameters of both low mobility and not-at-cell-edge criteria,
  If network indicates option a,
    the relaxation method corresponding to scenario #3 when both relaxation criteria have been fulfilled
  If network indicates option b,
    the relaxation method corresponding to scenario #1 when only low mobility criteria is fulfilled
    the relaxation method corresponding to scenario #2 when only not-at-cell-edge criteria is met.
    FFS the relaxation method corresponding to scenario #3 when both relaxation criteria have been fulfilled

## Slide 4: WF on RRM measurement relaxation
RRM measurement relaxation for inter-frequency layer with higher priority
  When Srxlev > SnonIntraSearchP and Squal > SnonIntraSearchQ, no relaxation of the current measurement delay requirement is expected for inter-frequency measurement with higher priority.
    The agreement is only applicable when condition of scenario 2 is fulfilled and condition of scenario 1 is not fulfilled or not configured.
    UE can stop both equal/low priority and high priority inter-freq/inter-RAT measurements in scenario 3.
  When Srxlev ≤ SnonIntraSearchP or Squal ≤ SnonIntraSearchQ, the relaxed requirement for the frequency layer of higher priority shall use the same relaxed measurement requirement as those for the frequency layer of equal/lower priority.
  FFS the measurement relaxation method for higher priority carriers or equal/lower priority carriers applies to inter-RAT carrier with higher priority or equal/lower priority.

## Slide 5: WF on RRM measurement relaxation
RRM measurement relaxation by reducing the number of frequency layer to be measured
  No consensus to introduce the RRM measurement relaxation by reducing the number of frequency layer.
    No further discussion in RAN4.
Transition period requirement
  Option 1: (MTK, Apple, CATT)
    When the intra/inter-frequency measurement transitions between any of two scenarios during one cell-reselection or measurement period, the cell re-selection or measurement requirements shall be the maximum of corresponding to the first mode before transition and the second mode after transition.
  Option 2: (Ericsson, Qualcomm, Nokia, NEC)
    When switching from scenario #1 or #2 to scenario #3, the UE shall fulfil the requirements corresponding to scenario #1 or #2 for N DRX cycles and thereafter switch to requirements corresponding to scenario #3
    When switching from scenario #3 to scenario #1 or #2, the UE shall fulfil the requirements corresponding to scenario #1 or #2 upon fulfilling the switching criteria.
    When switching from normal mode to scenario #1/#2/#3, the UE shall fulfil the requirements corresponding to normal mode for N DRX cycles and thereafter switch to requirements corresponding to scenario #1/#2/#3
    When switching from scenario #1/#2/#3 to normal mode, the UE shall fulfil the requirements corresponding to normal mode upon fulfilling the switching criteria.
  Option 3: (vivo)
    Define transition requirement between normal mode to relaxed mode (scenario 1/2/3) and vice versa
    Not define transition period between scenario 1/2 and 3 and vice versa

## Slide 6: WF on RRM measurement relaxation
FFS the triggering RRM relaxation mode
FFS the threshold mismatch between not at cell edge condition and cell centre condition
Not to introduce idle mode measurement accuracy requirements
EMR impact in power saving mode
  Option 1: Measurements on EMR carriers should not be relaxed if T331 is running. (LGE, Nokia, CATT, Qualcomm, Ericsson, Apple, CMCC, NEC)
  Option 2: Measurements on EMR carriers shall be relaxedif T331 is running (vivo, MTK, Huawei)

## Slide 7: WF on RRM measurement relaxation
  RRM measurement relaxation threshold for inter-frequency measurement
  Option 1: It is up to RAN2’s decision on whether to introduce carrier specific threshold for inter-frequency measurement relaxation. (Apple, CATT, CMCC, Huawei, Ericsson, Qualcomm, NEC)
  Option 2: Introduce carrier specific search thresholds for measurement relaxation. (LGE, Nokia, vivo)
  Companies are encourage to provide analysis of performance impact due to measurement relaxation.
  RRM impact due to cross-slot scheduling power saving technique
  Option 1: no RRM impact (Ericsson)
  Option 2: RAN1 will resolve the issue in RAN1 spec (CATT, vivo, MTK, Qualcomm, Huawei)
  Agreement: no further discussion in RAN4.