## Slide 1: WF on R16 NR RRM enhancements - BWP switching on multiple CCs
Intel Corporation
3GPP TSG-RAN WG4 Meeting #94-e-Bis R4-2005339
Electronic Meeting, 20 Apr. – 30 Apr., 2020

## Slide 2: Background
In RAN4#94e WF on BWP switching on multiple CCs was approved - R4-2002244

## Slide 3: Simultaneous BWP switching on multiple CCs (1)
Delay requirements for DCI/timer based BWP switch
; N: Number of CCs with simultaneous BWP switch; K is number of CCs that can be processed simultaneously; D is incremental delay for BWP switch processing on additional CCs
Agreement in 1st round: K = 1
FFS on D
Options for D
  Option 1: D=100us for Type 1; 200 us for Type 2
  Option 2: D = 450us for Type 1; 1.5ms for Type 2;
  Other options are not precluded.

## Slide 4: Simultaneous BWP switching on multiple CCs (2)
Delay requirements for RRC based BWP switch
;
Where DRRC is FFS and will be decided in RAN4#95-e.
- Option 1: DRRC = 1.5ms
- Option 2: DRRC = 0ms
- Other options are not precluded.

## Slide 5: Simultaneous BWP switching on multiple CCs (3)
Interruption requirements for simultaneous BWP switch
Agreement in 1st round: The length of each separate interruption caused by each CC where UE performs BWP switching is same as Rel-15 single CC
No requirement is needed for total interruption length .

## Slide 6: Partial Overlap BWP switching on multiple CCs (1)
Conditions when requirements for partial overlap BWP switch are defined
Agreement in 1st round: For DCI and RRC based BWP switch with partial overlap, partial overlap is defined for FR1+FR2 in NR-DC when UE is capable of per FR gap.

## Slide 7: Partial Overlap BWP switching on multiple CCs (2)
Delay requirements for DCI based BWP switch
  No extra waiting time is considered. Re-use the switching delay requirements from single CC and simultaneous triggering case.

## Slide 8: Partial Overlap BWP switching on multiple CCs (3)
Delay requirements for Timer based BWP switch
Agreement in 1st round: timer-based BWP switch should be delayed by ongoing timer-based BWP switch.
Further agreement:
UE should be allowed to conduct the BWP switch for different request sequentially in a first-come-first-serve manner for non-simultaneous Timer-based BWP switch in the same FR, i.e. additional TDelay is allowed, where TDelay is the time delayed by ongoing BWP switching on other CCs.
It is FFS how to address the impact from partial overlap BWP switching in the other FR.

## Slide 9: Partial Overlap BWP switching on multiple CCs (4)
Delay requirements for RRC based BWP switch
It is FFS whether extra waiting time should be defined. If the extra waiting time is needed, it should be upper bounded by
option 1: the multiple BWP switch delay of the 1st CG.
option 2: the RRC processing time in the 1st CG.