## Slide 1: WF on spatial relation switch
Mediatek Inc.
3GPP TSG-RAN WG4 #94-e-Bis Meeting
Electronic Meeting, 20 – 30 Apr., 2020
R4-2005340

## Slide 2: Background
In RAN Plenary #86, the WI of NR RRM enhancement requirements for R16 was revised. The following issue is agreed to be discussed.
  Active spatial relation switch for uplink
Scenario overview
# | Scenario | PHY channel | Triggering method | associated source | Whether to introduce requirement
1 | PUCCH-RRC-DL | PUCCH | RRC | DL RS | No
2 | PUCCH-RRC-UL | PUCCH | RRC | UL SRS | No
3 | PUCCH-MAC-DL | PUCCH | MAC | DL RS | Yes
4 | PUCCH-MAC-UL | PUCCH | MAC | UL SRS | No
5 | PUSCH-DCI | PUSCH | DCI | - | No
6 | pSRS-RRC-DL | P-SRS | RRC | DL RS | Yes
7 | pSRS-RRC-UL | P-SRS | RRC | UL SRS | No
8 | spSRS-MAC-DL | SP-SRS | MAC | DL RS | Yes
9 | spSRS-MAC-UL | SP-SRS | MAC | UL SRS | No
10 | aSRS-DCI-DL | A-SRS | DCI | DL RS | Yes
11 | aSRS-DCI-UL | A-SRS | DCI | UL SRS | No

## Slide 3: Agreement(1)
No requirement is needed for spatial relation info switching associated with UL SRS.
  No requirement is needed for MAC CE based spatial relation info switching associated with SRS for PUCCH.
  No requirement is needed for RRC based spatial relation info switching associated with SRS for P-SRS.
No requirements are defined for spatial relation info switching delay for PUSCH.
No requirements are defined for spatial relation info switching for PUCCH when PUCCH-SpatialRelationInfo is not configured.
No requirements are defined for spatial relation info switching for RRC based spatial relation info switching with DL-RS for PUCCH.

## Slide 4: Agreement(2)
Define delay requirement for RRC based spatial relation info switching with DL-RS for P-SRS.
Define DCI based spatial relation info switching delay for A-SRS.
  When spatial relation info associated with DL-RS
    For unknown spatial relation condition, there is no requirement.
    For known spatial relation condition, refer to RAN1 spec.
Define delay requirement for MAC CE based spatial relation info switching associated with DL-RS for PUCCH.
Define delay requirement for MAC CE based spatial relation info switching with DL-RS for SP-SRS.

## Slide 5: Agreement(3)
The known condition on spatial relation when associated with DL-RS,
  The spatial relation associated to DL RS is known if the following conditions are met:
  - During the period from the last transmission of the DL RS resource used for the L1-RSRP measurement reporting for the target spatial relation to the completion of active spatial relation switch, where the DL RS resource for L1-RSRP measurement is the DL RS in target spatial relation or QCLed to the target spatial relation with QCL type-D.
  - Spatial relation switch command is received within 1280 ms upon the last transmission of the RS resource for beam reporting or measurement
  - The UE has sent at least 1 L1-RSRP report for the target spatial relation before the spatial relation switch command
  - The [DL RS configured in spatial relation] remains detectable during the spatial relation switching period
  - The SSB associated with the spatial relation remains detectable during the spatial relation switching period
  - SNR of the spatial relation ≥ -3dB
  Otherwise, the spatial relation is unknown.

## Slide 6: Way Forward
Whether define the spatial relation delay requirement for UE which only supports BC Bit-0?
  Option 1: Yes
  Option 2: No

## Slide 7: Way Forward
When the UL signal has spatial relation to an unknown DL RS,
  Option 1: UE transmits using previous TX beam
  Option 2: Drop UL transmission until TCI state is known
  Option 3: Up to UE implementation and no need to be specified.

## Slide 8: Way Forward
Whether to consider timing tracking when associated DL-RS?
  Sub1. Whether to consider timing tracking when associated DL-RS QCLed with a different qcl-Type1 RS?
    Option 1: No
    Option 2: Yes
    Option 3: Up to UE
  Sub2. Whether to consider timing tracking when associated DL-RS is an unknown DL RS?
    Option 1: No
    Option 2: Yes
    Option 3: Up to UE
  Sub3. Whether to consider timing tracking when PUSCH/PUCCH and SRS associated with different DL-RSs in one slot?
    Option 1: No
    Option 2: Yes
    Option 3: Up to UE

## Slide 9: Way Forward
Define delay requirement for MAC CE based spatial relation info switching associated with DL-RS for PUCCH
For known TCI state
  Option 1: THARQ +3ms
  Option 1a: THARQ +3ms/NR slot length
  Option 2: THARQ +3ms + time for time tracking if applicable
  Option 3: The PDCCH TCI switch timeline to be used as baseline
For unknown TCI state
  Option 1: THARQ + 3ms + TL1-RSRP
  Option 1a: THARQ +(3ms+ TL1-RSRP)/NR slot length
  Option 2: THARQ + 3ms + TL1-RSRP + time for time tracking if applicable
  Option 3: THARQ + 3ms + ‘time for tracking’
  Option 4: No requirement
# | Scenario | Whether to introduce requirement
3 | PUCCH-MAC-DL | Yes

## Slide 10: Way Forward
Delay requirement for RRC based spatial relation info switching associated with DL-RS for P-SRS
For known TCI state
  Option 1: Define delay based on RRC based TCI state switching requirements
  Option 2: TRRCprocessing + time for time tracking if applicable
  Option 3: TRRCprocessing (timing is not required)
For unknown TCI state
  Option 1: Define delay based on RRC based TCI state switching requirements
  Option 2: TRRCprocessing + TL1-RSRP + time for time tracking if applicable
  Option 3: TRRCprocessing + TL1-RSRP
  Option 4: No requirements
# | Scenario | Whether to introduce requirement
6 | pSRS-RRC-DL | Yes