## Slide 1: WF on R16 NR RRM enhancements – SRS carrier switching
ZTE
3GPP TSG-RAN WG4 Meeting #94-e-Bis
Electronic Meeting, Apr. 20th – Apr. 30th 2020
R4-2005341

## Slide 2: Agreements
Applicability of SRS carrier switching time for defining interruption requirements
  200us for intra-band CA in both FR1 and FR2
  200us , 500us and 900us for inter-band CA in FR1, and inter-band CA between FR1 and FR2
  Wait for RF room on conclusion of applicable SRS carrier switching time for inter-band CA in FR2
For per-FR gap capable UE, interruptions are not allowed due to SRS carrier switching in different frequency range
Define interruption requirements as sync case for CA
  Option 1: Interruption length is the same as for async case
  Option 2: Interruption length is 1 slot less than for async case

## Slide 3: Agreements
In EN-DC and NE-DC, the interruption to NR DL reception and UL transmission due to LTE SRS carrier switching are specified in interruption requirements.
In EN-DC and NE-DC, the interruption to LTE DL reception and UL transmission due to NR SRS carrier switching are specified in interruption requirements.
Follow SRS carrier switching procedures specified by RAN1/RAN2 if applicable. Reference to RAN1/RAN2 spec in RRM requirements is preferable if it is necessary.
If SRS carrier switching is dropped, no interruption is allowed.

## Slide 4: WF
Impact on NR measurement requirements based on SSB/PBCH/CSI-RS due to LTE SRS carrier switching
  Option 1a
    NR measurements in FR2 are NOT allowed to be interrupted for UE capable of per-FR gap
    NR measurements in FR1 are allowed to be interrupted.
    NR measurements are allowed to be interrupted for UE not capable of per-FR gap.
  Option 2
    Collision between SRS switching on one technology and measurement occasion on another is an error condition from UE perspective and UE behavior is not defined for such scenarios.
    Depending on scenario UE may choose to interrupt other tech or drop SRS switching.

## Slide 5: WF
Impact to E-UTRA measurement requirements due to NR SRS carrier switching
  Option 1a
    E-UTRA measurements are NOT allowed to be interrupted due to NR SRS carrier switching in FR2 for UE capable of per-FR gap
    E-UTRA measurements are allowed to be interrupted for UE not capable of per-FR gap.
    E-UTRA measurements are allowed to be interrupted due to NR SRS carrier switching in FR1.
  Option 2
    Collision between SRS switching on one technology and measurement occasion on another is an error condition from UE perspective and UE behavior is not defined for such scenarios.
    Depending on scenario UE may choose to interrupt other tech or drop SRS switching.