## Slide 1: WF on R16 NR RRM enhancements – mandatory gap patterns
ZTE
3GPP TSG-RAN WG4 Meeting #94-e-Bis
Electronic Meeting, Apr. 20th – Apr. 30th 2020
R4-2005345

## Slide 2: Agreements in the previous meetings
Confirmed R15 capability information elements cannot be changed in meaning by any new capability signaling introduced in R16
Confirmed R15 gap pattern applicability rule is not changed due to introduction of additional mandatory gap patterns in R16

## Slide 3: Agreements
​Applicability of mandatory gap patterns in GP#12-GP#23 shall follow the Rel-15 applicability table in TS38.133
  Mandatory gap patterns in GP#12-GP#23 are applicable to NR SA, NR DC, NE-DC and EN-DC operations for per-FR gap capable UE
  Mandatory gap patterns in GP#12-GP#23 are applicable to NR SA and NR DC operations for per-UE gap only capable UE

## Slide 4: Agreements
​In NR SA and NR-DC operation
  NR-only measurement means the target measurement objects to be measured within the measurement gap are all NR carriers
  UE capability of NR-only measurement is introduced
    The UE capability is to indicate if the gap patterns from GP#2 to GP#11 can only be used to do NR only measurement and to indicate the gap patterns are supported by the UE.
  All UEs are mandated to support the additional mandatory gap patterns
For LTE SA, EN-DC, NE-DC
  Support of a set of “mandatory additional gap patterns defined for NR SA and NR-DC for NR only measurement” is an optional UE capability
  Introduce a new UE capability signalling where UE may indicate the support for a full set of “mandatory additional gap patterns defined for NR SA and NR-DC for NR only measurement”

## Slide 5: Agreements
Support of “mandatory MG patterns” for NR measurement only for NR SA and NR DC is mandatory feature with capability signalling. UE capability shall be indicated for each gap pattern.

## Slide 6: WF
FFS if GP#17, #,18 and GP#19 in FR2 shall be additional mandatory for Rel-16 UE
FFS if any gap patterns among GP#2, GP#3, GP#6, GP#7, GP#8, GP#9, GP#10 and GP#11 in FR1 shall be additional mandatory for NR only measurement for Rel-16 UE in NR SA and NR-DC operation