## Slide 1: WF on impact of positioning on RRM requirements
Ericsson
3GPP TSG-RAN WG4 Meeting # 94-e-Bis
Electronic Meeting, April 20-30, 2020
Agenda: 6.8
R4-2005379

## Slide 2: New MG Patterns
FFS: Introduction of new measurement gap pattern with MGL > 6 ms.
Candidate MGL and MGRP if new MG patterns are specified:
  MGL = {10, 20, 40 and 50} ms
  MGRP = {80, 160, 320 and 640} ms
  Combination of MGL and MGRP is FFS
Independent MG patterns for positioning and RRM measurements is deferred to future release.

## Slide 3: Gap sharing between RRM and positioning measurements
Gap sharing between RRM and positioning measurements is based on CSSF defined in Rel-15 of TS 38.133.
Details of CSSF for gap sharing between RRM and positioning measurements are FFS.
Details on extending measurement periods of RRM and positioning measurements due to gap sharing are FFS.

## Slide 4: Impact of interrupted PRS due to BWP switch on positioning measurement performed within the active BWP
FFS: Impact on positioning measurement being performed within the active BWP if the active BWP switching interrupts any PRS and/or SRS configured for that positioning measurement.
Candidate options:
  Option 1: Even if active BWP switching interrupts any PRS/SRS, the UE continues performing positioning measurement over an extended measurement period; details of extension are FFS.
  Option 2: If active BWP switching interrupts any PRS/SRS then the UE is not required to meet positioning measurement requirements.
  Other options are not precluded.

## Slide 5: Active BWP switch during gaps used for PRS measurements
FFS: priority between active BWP switching in gap and PRS measurement in gap
Candidate options:
  Option 1:
    Active BWP switching is prioritized over PRS measurement in a gap where active BWP switching is triggered.
  Option 2:
    PRS measurement is performed in a gap even if active BWP switching is triggered in that gap.
  Option 3:
    Triggering of active BWP switching in gap can always be avoided by gNB.

## Slide 6: BWP switch triggers UE to request gaps
Following is the UE behavior and applicable positioning measurement requirements when the UE is performing positioning measurement in active BWP and the active BWP change triggers the UE to request gaps:
  UE abandons old/incomplete positioning measurement performed within the active BWP, restarts the positioning measurement and performs the positioning measurements in gaps.

## Slide 7: Impact of concurrent RRM/PRS processing/measurement
FFS: whether concurrent RRM/PRS processing/measurement impacts RRM and/or PRS measurements i.e.
  Whether concurrent RRM processing and PRS measurement, impacts RRM and/or PRS measurements.
  Whether concurrent PRS processing and RRM measurement, impacts RRM and/or PRS measurements.
Candidate options:
  Option 1: No impact on both intra- and inter-frequency measurements.
  Option 2: No impact on intra-frequency but impact on inter-frequency measurements.
  Option 3: impact on intra-frequency and inter-frequency measurements RRM and/or PRS measurement requirements need to be relaxed for both intra- and inter-frequency measurements.
  Other options are not precluded.
Candidate solutions if it is identified that the concurrent RRM/PRS processing/measurement impacts RRM and/or PRS measurements are FFS

## Slide 8: Additional SSB measurement for SSB configured as QCL source of PRS resource
UE is not required to perform additional SSB measurement for the SSB configured as QCL source of PRS resources.