## Slide 1: Way forward for NR UE URLLC performance requirements
Intel Corporation, …
3GPP TSG-RAN WG4 Meeting #94-e-Bis
E-meeting, 20 April – 30 April, 2020
Agenda Item: 6.9.1.2
R4-2005527

## Slide 2: High reliability (1)
      Background (Agreed parameters from #94e)
  TDD pattern: 7D1S2U, S=6D: 4G: 4U for 30 kHz SCS.​
  Propagation condition: TDLA30-10​
  SCS & CBW: ​
  FDD: 15 kHz & 10 MHz​
  TDD: 30 kHz & 40 MHz​
  PDSCH configuration: Mapping type A, symbol length 12, starting symbol 2.​
  Antenna configuration: 2x2 and 2x4, ULA low​
  Target BLER: 1%​
  Target Confidence level: 99%​
  BLER is calculated after all transmission​
  Max number of HARQ transmissions: 4​

## Slide 3: High reliability (2)
      PDSCH Aggregation level:
  2 for FDD and TDD
      MCS: Select a suitable MCS value as per the evaluation results for MCS13/14/15/16
      FR2 requirements for High reliability
  Keep it open meanwhile prioritize discussion on introducing FR1 requirements in Q2; and interested companies are encouraged to bring more information and analysis for the deployment/usage scenarios

## Slide 4: PDSCH mapping Type B and processing capability 2 (1)
Background (Agreed parameters from #94e)
  Slots to be scheduled:
    FDD: All DL slots
    TDD: S slots with K1=0
  Starting symbol: 2
  Symbol length: 2
  Slot aggregation level: 1
  Max number of HARQ transmissions: 1
  Verify PDSCH processing capability 2 and type B mapping together

## Slide 5: PDSCH mapping Type B and processing capability 2 (2)
      SCS/CBW:
  FDD: 15 KHz/10 MHz
  TDD: 30 KHz/ 40 MHz
      TDD pattern (30KHz SCS)
  DDDSU, S=10:2:2
      Number of HARQ process:
  FDD: 2
  TDD
    Option 1: 2
    Option 2: 4
      K1 for FDD: K1=0
      Channel model: TDLA30-10
      Antenna configuration: 2x2 and 2x4, ULA Low.

## Slide 6: PDSCH mapping Type B and processing capability 2 (3)
      MCS:
  Option 1: Only MCS 4
  Option 2: Only MCS 17
  Option 3: MCS 4 and MCS 17
      Number of RBs:
  Full bandwidth only for MCS4
  FFS for MCS17
      PDSCH symbol length for FDD and TDD
  2os
  FFS whether to define additional requirements for 4os or 7os
      Test metrics: Based on 70% throughput or 30% BLER
      FR2 requirements for PDSCH mapping Type B and processing capability 2
  Keep it open meanwhile prioritize discussion on introducing FR1 requirements in Q2; and interested companies are encouraged to bring more information and analysis for the deployment/usage scenarios

## Slide 7: Pre-emption indication (1)
Background (Agreed parameters from #94e)
  No URLLC PI performance requirements
  Time frequency set: 14x1
  Number of symbols to be pre-empted: 2
  Starting symbol to be pre-empted: 3
  Test applicability for eMBB UE PI requirements: optional with UE capability signalling
  Antenna Configuration: 2x2 and 2x4, ULA low

## Slide 8: Pre-emption indication (2)
      Pre-emption probability
  Option 1: 10% within 1 radio frame
  Option 2: 20% within 1 radio frame
      Pre-emption sheduling
  Option 1: Fixed scheduling
  Option 2: Non-fixed scheduling (slot periodicity/offset 10/5)
      Number of pre-empted symbols: Only 2os
      eMBB MCS
  Option 1: MCS13 in Table 1
  Option 2: MCS4 in Table 1
      Companies are encouraged to prepare comparison analysis of UE with and without HARQ buffer flushing of pre-empted bits to decide on options above
      Test metric
  Option 1: 70% of max T-put
  Other options are not precluded

## Slide 9: Pre-emption indication (2)
      Further discuss if the following parameters from Rel-15 PDSCH requirements can be reused for eMBB PDSCH configuration
Parameter |  | Value
Duplex mode |  | FDD, TDD
Active DL BWP index |  | 1
PDSCH configuration | Mapping type | Type A
 | k0 | 0
 | Starting symbol (S) | 2
 | Length (L) | 12
 | PDSCH aggregation factor | 1
 | PRB bundling type | Static
 | PRB bundling size | 2
 | Resource allocation type | Type 0
 | RBG size | Config2
 | VRB-to-PRB mapping type | Non-interleaved
 | VRB-to-PRB mapping interleaver bundle size | N/A
PDSCH DMRS configuration | DMRS Type | Type 1
 | Number of additional DMRS | 1
 | Maximum number of OFDM symbols for DL front loaded DMRS | 1
Number of HARQ Processes |  | FDD: 4 TDD: 8
The number of slots between PDSCH and corresponding HARQ-ACK information and TDD pattern |  | FDD: 2 TDD: FR1.30-1
CBW/SCS |  | FDD: 10/15 TDD: 40/30
RB allocation |  | Full bandwidth
MIMO layer |  | Rank 1
Propagation condition |  | TDLA30-10

## Slide 10: CQI reporting requirements (1)
      Propagation channel for CQI reporting
  Option 1: AWGN
  Option 2: Fading channel
      Target BLER in case AWGN conditions will be used
  Option 1: 10^-3
  Option 3: 10^-5

## Slide 11: CQI reporting requirements (2)
      Test metric in case AWGN conditions will be used
  Option 1: Reuse Rel-15 CQI test metric
  Option 2: Reuse Rel-15 CQI test metric and define a lower bound for median reported CQI in the CQI reporting tests for 99.999% reliability
  Other options are not precluded
      Test metric in case Fading conditions will be used
  Option 1:
    A CQI index not in the set {median CQI -1, median CQI, median CQI +1} shall be reported at least α% of the time
    The ratio of the throughput with follow CQI vs median CQI shall be ≥ γ
  Other options are not precluded
      In case AWGN conditions with target BLER 10^-5 will be used, FFS feasibility to define CQI reporting test case and FMCS case at the same SNR and define an applicability rule between CQI reporting test and FMCS test