## Slide 1: WF on UE demodulation and CSI reporting requirements for FR2 DL 256QAM
China Telecom
3GPP TSG-RAN4 Meeting #94e-Bis
Electronic Meeting, 20 – 30 Apr., 2020
Agenda item: 6.12.4
R4-2005531
Document for: Approval

## Slide 2: PDSCH Demodulation: Main Parameters
Define FR2 PDSCH demodulation requirements for 256QAM
  Tx EVM
  Option 1: 3%
  Option 2: 3.5%
  Option 3: 2%
  Rx EVM
  Option 1: 2%
  Option 2: Not Specified
  Option 3: Consider agreements from WF R4-1811394 as starting point and check if it is applicable to 256QAM discussion
  MIMO configuration
  2Tx 2Rx ULA low
  Other options are not precluded

## Slide 3: PDSCH Demodulation: Main Parameters cont’d
  Rank
  Option 1: rank 1
  Option 2: rank 1 and 2
  Other options are not precluded
  Propagation condition
  Option 1: Fading channel
    Option 1a: TDLA30-300
    Option 1b: TDLD30-75
    Option 1c: TDL-D for Rank 1, TDL-D for Rank 2
    Option 1d: TDL-A for Rank 1, TDL-D for Rank 2
    Option 1e: TDLD30-35
  Option 2: Static channel
  TBD based on simulation results

## Slide 4: PDSCH Demodulation: Main Parameters cont’d
  Channel bandwidth and PRB allocation
  Option 1: 100MHz CBW with full PRB allocation
  Option 2: 100MHz CBW with partial PRB allocation
  Option 3: 50MHz CBW with full PRB allocation
  MCS
  Option 1: MCS 20 or higher depending on the allocated PRB number
  Option 2: MCS 21
  Option 3: MCS 20
  Option 4: MCS 25/26/27
  Other options are not precluded
  Carrier frequency
  Option 1: band agnostic
  Option 2: Further analyze whether it is possible to define band agnostic requirements

## Slide 5: PDSCH Demodulation: Other Parameters
SCS: 120kHz
  PT-RS configuration:
  per 2PRB in frequency domain, per symbol in time domain
Overhead for TBS determination: 6
  PDSCH mapping type: Type A
  DM-RS configuration
  Option 1: Type 1 single symbol front loaded, 1 additional DMRS
  Option 2: Type 1 single symbol front loaded, 0 additional DMRS
  TDD Configuration: DDDSU, S=10D:2G:2U
  PDCCH and PDSCH duration
  PDCCH: Symbol #0 in each slot
  PDSCH configuration:
    Full DL slots: Type A, Start symbol 1, Duration 13
    Special slots: Type A, Start symbol 1, Duration 9

## Slide 6: PDSCH Demodulation: Other Parameters cont’d
PRB bundling size and Precoding model
  Option 1:
    PRB bundling size: 2
    Precoding model: Random Precoding, per slot , WB granularity
  Other options are not precluded
SSB and TRS configuration
  SSB configuration: Periodicity 20 ms, Allocated in first slot within 20ms
  TRS configuration: 20 ms periodicity, 2 slots, Offset 10 ms
    HARQ RV sequence
  {0, 2, 3, 1}
  HARQ process number
  Option 1: 8
  Other options are not precluded
    Receiver assumption
  MMSE-IRC
    Test metric
  70% of max TP

## Slide 7: SDR Requirements
FFS whether to define SDR requirements for FR2 256QAM
  If it is agreed to define SDR requirements, consider the following test parameters:
  MCS and rank
    Option 1: Add MCS indexes 26, 21, 20 and 11 in MCS table 2 for both 1 and 2 MIMO layers. Run simulations for these MCS indexes to derive the required SNR achieving 85% of peak throughput under AWGN conditions
    Other options are not precluded

## Slide 8: CQI reporting Requirements
FFS whether to define FR2 CQI reporting requirements for CQI table 2
If it is agreed to define FR2 CQI reporting, consider the following test parameters:
  Propagation condition
    Option 1: Cover both AWGN and fading conditions
    Other options are not precluded
  SNR testing point
    Option 1: Cover higher SNR testing point compared to that in Rel-15 FR2 CQI tests
    Other options are not precluded
  Other parameters
    Option 1: Reuse the assumptions in Rel-15 FR2 CQI tests
    Other options are not precluded