## Slide 1: Way forward on UE power imbalance requirements for FR1 CA and EN-DC
NTT DOCOMO
3GPP TSG-RAN4 Meeting #94e-Bis
Electronic Meeting, 20 – 30 Apr., 2020
Agenda Item: 6.18.1.4
R4-2005547

## Slide 2: Wayforward
For FR1 intra-band contiguous CA
How to define the Channel bandwidth combination
  Option 2: Define requirements for 5+5 MHz bandwidth for FDD+FDD CA, 10+10 MHz bandwidth for TDD+TDD CA, with the following test applicability
    The test is done for any one of the supported bandwidth combination, by using performance requirement for 5+5 MHz FDD+FDD CA or 10+10 MHz TDD+TDD CA.
    The tested PRBs shall be placed in the highest part for the CC with lower carrier frequency, and placed in the lowest part for the CC with higher carrier frequency.
  Option 3: Define generic methodology for selection of CBW combination among all CBW combinations in supported CA configurations
    Methodology of Option 3 is to be clarified.
  PDSCH RB allocation
    To be decided after the channel bandwidth combination is agreed

## Slide 3: Wayforward
For FR1 intra-band contiguous CA
TDD pattern for 30 kHz SCS
  7D1S2U(S=6d4s4u)
MIMO configuration
  Option 1: 2x2 and 2x4
  Option 2: 1x2 and 1x4
  Option 3: Simulation is needed
    Further evaluate the throughput at 19dB SNR point
MCS
  Simulation is needed
    Option A: use different MCSs for 2Rx and 4Rx.
    Option B: use same MCS for 2 Rx and 4 Rx
PRB bundling size
  Option 1: WB
  Option 2: 2 PRBs
PDCCH allocation
  Symbol #0 and #1

## Slide 4: Wayforward
For intra-band contiguous EN-DC
Duplex mode
  Option 1: FDD and TDD
  Option 2: FDD
SCS
  Option 1: 15kHz for both FDD and TDD
  Option 2: 15kHz for FDD, 30kHz for TDD
  Option 3: 15kHz for FDD
TDD pattern for 30kHz SCS
  7D1S2U
TDD pattern for 15kHz SCS
  Option 1: DSU+DD
  Other options are not precluded.
Other parameters
  Generally ok to reuse simulation assumptions from NR CA requirements to define EN-DC requirements with power imbalance for the following parameters: PDSCH configuration, PDCCH allocation, antenna configuration and propagation conditions.
  Power setting relation between LTE carrier and NR carrier
    Option 1: LTE cell 6dB higher than NR Cell
    Other options are not precluded.
  Propagation conditions
    Option 1: static channel similar to LTE
    Other options are not precluded

## Slide 5: Wayforward
For intra-band non-contiguous EN-DC
Whether to define power imbalance requirement for FR1 intra-band non-contiguous EN-DC
  Option 1: Yes
    Power imbalance value for non-contiguous EN-DC is 6dB.
    UE should be tested according to the following applicability rules
  Option 2: No
apply the same parameters as the FR1 intra-band contiguous EN-DC requirement.
Test applicability rules
  Option 1
    UE supports only intra-band contiguous EN-DC, i,e., if UE does not indicate “intraBandENDC-Support”,
      apply power imbalance requirement for FR1 intra-band contiguous EN-DC
    UE supports only intra-band non-contiguous EN-DC, i.e., if UE indicates “non-contiguous” in “intraBandENDC-Support” ,
      apply power imbalance requirement for FR1 intra-band non-contiguous EN-DC
    UE supports both intra-band contiguous and non-contiguous EN-DC, i.e., if UE indicates “both” in “intraBandENDC-Support” ,
      FFS. apply both power imbalance requirement for FR1 intra-band contiguous EN-DC and FR1 intra-band non-contiguous EN-DC
    In case of inter-band EN-DC combination, where the frequency range of the E-UTRA band is a subset of the frequency range of the NR band (as specified in Table 5.5B.4.1-1 of TS 38.101-3)
      UE supports only intra-band non-contiguous EN-DC, i,e., if UE does not indicate “interBandContiguousMRDC”[1][2],
        apply power imbalance requirement for FR1 intra-band non-contiguous EN-DC
      UE supports both intra-band contiguous and non-contiguous EN-DC, i,e., if UE indicates “interBandContiguousMRDC”[1][2],
        FFS. apply power imbalance requirement for for FR1 intra-band contiguous EN-DC and FR1 intra-band non-contiguous EN-DC
  Other options are not precluded.
[1] R2-2002349
[2] R2-2002350