## Slide 1: WF on switching period in ITS band for NR V2X
Huawei, HiSilicon, LG Electronics[ ]
R4-2005644
3GPP TSG-RAN WG4 #94-e-bis
Electronic Meeting, 20th – 30th April., 2020

## Slide 2: Background
In Justification of latest WID (RP-200129) on 5G V2X, RAN captured as follow
  TSG RAN has already agreed in TR 38.913 that it is not intended for NR V2X to replace the services offered by LTE V2X. Instead, the NR V2X shall complement LTE V2X for advanced V2X services and support interworking with LTE V2X. At least from 3GPP RAN technology development standpoint, the focus and scope of NR V2X is to target advanced V2X use cases. However, this does not imply that NR V2X cannot support basic safety use cases. It is clearly up to the regional regulators and the stakeholders involved (i.e. Car OEMs and automotive ecosystem in general) to decide on the technology of choice for any service and any use case.
V2X UE supporting LTE SL and NR SL in TDM corresponds the following scenario
  The NR V2X shall complement LTE V2X for advanced V2X services and support interworking with LTE V2X
  This mean that LTE V2X shall support the basic safety service.

## Slide 3: WF1: Switching period
Candidate values for intra-band switching
  150us including transient period (majority view)
  210us
Suggested WF on switching period
  150us in square brackets in the CR preparation (Majority view)
  No agreement on switching period so should use [ ] in CR preparation

## Slide 4: WF2: Switching period position
Candidate options
  Option 1: Switching period is placed at the NR slot
  Option 2: The whole switching time including switching period as well as transient periods shall be placed at the previous E-UTRA sub-frame or NR slot.
  Option 3: The switching time can be located on guard period symbol at the end of slot and lower priority RAT signal slot. If there is no priority or same priority, two continuous slots of two RATs should share the part of switching time period minus guard period symbol.
Suggested WF on switching period position
  Alt. 1: Option1 is chosen
  Alt. 2: down select between Option 2 and option 3 is chosen
In next RAN4 meeting, RAN4 shall decide the switch period position

## Slide 5: WF3: Interruption time
Candidate options
  Option 1: Interruption requirement for Tx switch between LTE SL and NR SL is one slot for NR and one subframe for LTE
  Option 2: No interruption time is specified in RF requirements (majority view)
Suggested WF on interruption time
  Go with option 2 and interruption time can be further checked in RRM session
  This should be decided by the RRM session not the RF session

## Slide 6
Reference
[1] R4-2003847, updated Draft CR on switching period and REFSENS requirements in TS38.101-3, LG Electronics
[2] R4-2004469, Switching time between NR SL and LTE SL, Qualcomm
[3] R4-2004743, On switching period for LTE SL and NR SL, Huawei, HiSilicon