## Slide 1: WF on testability issues for transient period capability
CMCC
3GPP TSG-RAN WG4 Meeting # 94-e-Bis R4-2005668
Electronic Meeting, 20 – 30 Apr., 2020

## Slide 2: Background
According to the conclusion [Transient period] of RAN#87e:
  - There is no consensus on whether the transient time capability is feasible to test or not. RAN4 CR is 261 is noted. RAN4 continue discussing the feasibility of testing the transient periods in RAN4 during Q2 and report the outcome at RAN#88.
References
  [1] R4-2003331 Consideration on testability issues for on-to-on transient period, Anritsu Corp
  [2] R4-2004057 Discussion on values for transient period capability, vivo
  [3] R4-2004132 UE transient time capability , Ericsson
  [4] R4-2004719 Testability of reported transient durations, Qualcomm
  [5] R4-2004720 Transient Period Capability in NR using existing window definitions, Qualcomm
  [6] R4-2004721 Transient Period Capability in NR using a new window definition, Qualcomm
  [7] R4-2004752 On transient period UE capability, Huawei, HiSilicon
  [8] R4-2005102 Email discussion summary for [94e Bis] [16]_NR_RF_FR1_Part_3, CMCC

## Slide 3: Summary of testability issues for Transient period
Issue 1-1-1: Whether RMS EVM over 1 slot can represent the transient period capability.
  View 1 (Ericsson, QC, Anritsu, HW): no
Issue 1-1-2: For RMS EVM over 1 slot, whether EVM measurement procedure on equalizing is clear for UE
  View 1 (Ericsson, Anritsu): It can be modified when describing EVM procedure for 1 symbol.
  View 2 (QC): No modifications are required.
  View 3 (HW): no, the equalize procedure can be 1) one DMRS 2) linear interpolation 3) DMRS+ data, it cannot only depend on TE implementation. Whether 1st DMRS can be used for equalization, it will compensate on transient as a part of channel status. The procedure has big impact on whether the EVM measurement is accurate.
Issue 1-1-3: For RMS EVM over 1 symbol, how to define EVM measurement procedure in the spec
  View 1 (Ericsson, QC, Anritsu, Skyworks): Adding a new section/annex for EVM to include symbols with transient period.
  View 2 (HW): It is not an issue whether we create a new section in TS 38.101, we should ensure the procedure could be correct, aligned among TE vendors, high-precision.

## Slide 4: Summary of testability issues for Transient period
Issue 1-1-4: Whether 20dB power change can represent the maximum power change in the network, if not, whether TE can provide the test condition for the maximum power change
  View 1 (QC, Anritsu): 20 dB power step is reasonable for on-on power change.
  View 2 (HW): no, power change>20dB is common case under real network. If the reference power change for transient period is 20dB, it will have performance impact on network, if the reference power change for transient period is worst case(e.g.58dB), how UE vendor get known our capability without reliable test environment.
Issue 1-1-5: How to ensure the transient period is symmetrically positioned
  View 1 (Ericsson, QC, Skyworks): The exclusion window is defined be symmetric about the symbol boundaries.
  View 2 (HW): Need a baseline on how to position transient period.

## Slide 5: Summary of testability issues for Transient period
Issue 1-1-6: Whether EVM=min(EVML, EVMH) can differentiate UE with different transient period ability
  View 1 (Ericsson, Anritsu): Support of transient capability values could be conditioned by supporting the SCS needed to test those values.
  View 2 (Anritsu): Time mask tests by signalled transient period in addition to the EVM measurement.
  View 3 (vivo, Ericsson, Anritsu): Do not introduce 1us as an option of transient period value.
  View 4 (QC, Ericsson, Anritsu): Define a new window location according to the reported capability.
  View 5 (QC, Ericsson): Use the existing sample sets for EVM evaluation (25%, 50%, 75%), but evaluate min() and max() functions for 15 kHz and 30 kHz SCS.
  View 6 (HW): no. RAN4 should consider different EVM window (CP length) for 1st OS and transmitting timing error.
Issue 1-1-7: Whether RMS EVM with DFT-OFDM measurement similar with LTE can be tested for transient period
  View 1(Ericsson, QC, Anritsu): For 10µs transient period, NR can re-use same procedure defined for RMS EVM with power change in LTE.
  View 2(HW):no. There is not test on transient period for LTE, 25us exclusion window is specified. The concept cannot be used for transient period test.

## Slide 6: Summary of testability issues for Transient period
Issue 1-1-8: UL DL configuration
  View 1(Ericsson, QC, Anritsu, Skyworks): This issue can be discussed after the testability issues are solved.
  View 2(HW): 60kHz UL DL configuration should be discussed considering blanked symbol is introduced in the current spec.
Issue 1-1-9: How to calculate EVM for symbols in which the transient occurs
  View 1 (QC, Anritsu, Skyworks): Test procedure detail that needs to be discussed in RAN5.
  View 2 (HW): Transient period is different for ramp up and ramp down, it should be clearly clarified.
Issue 1-1-10: EVM budget for symbol where the transient occurs
  View 1(Ericsson, QC, Anritsu, Skyworks): Keeping EVM budget in square brackets. EVM values can be discussed after agreement is reached on the feasibility of testing transient periods.
  View 2(HW): EVM requirement should decide based on simulation results which can meet network performance on high order modulation.

## Slide 7: WF on testability issues for transient period
1 | Whether RMS EVM over 1 slot can represent the transient period capability. | The unanimous answer is no. Need to clarify why slot level RMS EVM need to be tested even it cannot represent for transient period capability.
2 | For RMS EVM over 1 slot, whether EVM measurement procedure on equalizing is clear for UE | View1 or 2 vs View3
3 | For RMS EVM over 1 symbol, how to define EVM measurement procedure in the spec | Further discuss whether adding a new section/annex for EVM to include symbols with transient period is acceptable, and how to ensure that the procedure could be correct, and that aligned among TE vendors.
4 | whether 20dB power change can represent the maximum power change in the network, if not, whether TE can provide the test condition for the maximum power change | View1 vs View2
5 | How to ensure the transient period is symmetrically positioned? | View1 vs View2
6 | whether EVM=min(EVML, EVMH) can differentiate UE with different transient period ability | Based on Views 1-6, this issue can be summarized as the following two options: Option1 : Do not introduce 1us. For 2us,4us,7us can be further discussed Option2: Including 1us,2us,4us,7us

## Slide 8: WF on testability issues for transient period
7 | whether RMS EVM with DFT-OFDM measurement similar with LTE can be tested for transient period | View1 vs View2
8 | UL DL configuration. | View1 vs View2 Further discuss whether UL DL configuration can be defined after the testability issues are solved.
9 | how to calculate EVM for symbols in which the transient occurs | This test procedure detail needs to be discussed in RAN5
10 | EVM budget for symbol where the transient occurs | View1 vs View2 Keeping EVM budget in square brackets, and EVM values should be discussed with technical justification after agreement is reached on the feasibility of testing transient periods.
Agreement: RAN4 continues the discussion on the testability issues in the May meeting

## Slide 9: WF on How to capture transient period capability
Alternative 1_RAN4 continues the discussion on the testability before introducing the corresponding UE capabilities, and RAN4 recommends a new SI on detailing the test procedure for transient period. It is up to RAN to decide whether a new SI on detailing the test procedure for transient period can be approved
Alternative 2_ RAN4 agrees with CR(s) to introduce the feature into Rel-16. Testability can continue to be discussed as maintenance in future meetings
    If errors or omissions are identified in the specification, Cat F CR’s can be submitted following the usual process

## Slide 10: WF on How to capture transient period capability
Alternative 3_ RF requirement on transient period capability ( section 6.3.3 for on-on time mask ) can be introduced in TS 38.101-1 in Rel-16 with no release independent manner, and test case for transient period capability can be introduced in Rel-17 after the testability issues are solved by a new SI/WI for better management of scope and time budget
Other alternatives are not precluded

## Slide 11: Thanks!