## Slide 1: WF on BC based on CSI-RS
Samsung
3GPP TSG-RAN WG4 Meeting #94-e-Bis R4-2005737 Electronic Meeting, Apr. 20th – 30th 2020

## Slide 2: Background
The remaining issues of Rel-16 BC based on CSI-RS were discussed [1]~[14]:
  The method to achieve “CSI-RS only” condition
  Side conditions
Capability aspects related to BC based on CSI-RS were also discussed [15]

## Slide 3: Way Forward (1): ”CSI-RS only” condition
SSB shall be present and configured as part of side conditions for Rel-16 CSI-RS based BC
“CSI-RS only” condition shall be guaranteed to prevent UE making use of SSB for P3 beam refinement
The method to achieve “CSI-RS only” condition:
  Alt 1: SSB and CSI-RS are present, but SSB’s PSD is backed-off by X dB from CSI-RS
    Continue discussing how to determine X
  Alt 2: Decrease SSB power until UE SSB based SS-SINR measurement reporting is ≤ [-3] dB
  Alt 3: Decide on PSD difference for CSI-RS and SSB according to a calibration procedure [5]
  Other alternatives can be discussed including the one where P1 CSI-RS QCL info is set to “none”
Note: it is agreed that in the final RAN4 specification, the term “CSI-RS only” will not be used

## Slide 4: Way Forward (2): Side conditions
The side conditions in the following table shall be used for BC based on CSI-RS for alt. 1-3
SNR side condition
  CSI-RS min SNR level: 6dB
Parameter | Value
P1 CSI-RS configuration | Yes
P1 CSI-RS periodicity | Slot80(120kHz)
P1 CSI-RS QCL info | qcl-TypeD to SSB
P2 CSI-RS configuration | No
P3 CSI-RS configuration | Yes
P3 CSI-RS repetitions per resource set | maxNumberRxBeam in UE capability IE of MIMO-ParametersPerBand
P3 CSI-RS configuration repetition | On
P3 CSI-RS trigger | once P1 CSI-RS is finished
P3 CSI-RS QCL info | qcl-TypeD to P1 CSI-RS
Tracking CSI-RS periodicity | Reuse Rel-15

## Slide 5
References
Ref | tdoc | source | title
[1] | R4-2003232 | LG Electronics | Enhanced beam correspondence capability in rel-16 at FR2
[2] | R4-2003335 | Nokia, Nokia Shanghai Bell | FR2 Beam Correspondence enhancements
[3] | R4-2003409 | Apple Inc. | On SSB based beam correspondence requirements
[4] | R4-2003876 | Ericsson, Sony | SSB/CSI-RS only and initial-access BC tests
[5] | R4-2004756 | Huawei, HiSilicon | On beam correspondence requirement for Rel-16
[6] | R4-2004887 | Qualcomm Incorporated | Beam management CSI-RS design for BC requirement
[7] | R4-2004992 | Samsung | Discussion on beam correspondence enhancement
[8] | R4-2003232 | LG Electronics | Enhanced beam correspondence capability in rel-16 at FR2
[9] | R4-2003335 | Nokia, Nokia Shanghai Bell | FR2 Beam Correspondence enhancements
[10] | R4-2003409 | Apple Inc. | On SSB based beam correspondence requirements
[11] | R4-2003876 | Ericsson, Sony | SSB/CSI-RS only and initial-access BC tests
[12] | R4-2004756 | Huawei, HiSilicon | On beam correspondence requirement for Rel-16
[13] | R4-2004887 | Qualcomm Incorporated | Beam management CSI-RS design for BC requirement
[14] | R4-2004992 | Samsung | Discussion on beam correspondence enhancement
[15] | R4-2005104 | Moderator (Apple Inc.) | Email discussion summary for [94e Bis][18] NR_RF_FR2_req_enh_Part_2